## Slide 1: 10th EVS-gtr IWG Progress Report TF6 - SOC 2nd March. 2016 TKP Ichigaya Building Hall 3A(3F) 8 Ichigaya hachimancho, Shinjyuku-ku Tokyo, 162-0844, JAPAN
JASIC

## Slide 2: Progress
At all F2F meeting at Brussels on 21 January 2016 All TF members confirmed that the SOC adjustment procedure proposed by TF (EVS-08-07e.docx) is agreed with the exception of verification procedure in para. 6.2.1.2.3．We have only discussion for para. 6.2.1.2.3. TF has 3 options for this Para.

## Slide 3: Draft proposal #1 TF6 amendment proposal on draft GTR (EVS-08-07e)
6.2.1.2.3. After the adjustment of the SOC according to paragraphs 6.2.1.2.1. and 6.2.1.2.2. above, the test shall be started within 48 hours subject to taking all reasonable and practical steps to ensure the initial SOC (i.e. the SOC achieved at the end of the adjustment according to the paragraphs 6.2.1.2.1. and 6.2.1.2.2. above) is maintained, otherwise an appropriate verification shall be made to confirm that the SOC is maintained not less than 90 % of the initial SOC e.g. by checking the voltage-drop and using the OCV-SOC curve of the REESS, etc.

## Slide 4: Draft proposal #2 US proposal to TF6 amendment proposal on draft GTR 6.2.1.2.3.
When the vehicle or REESS subsystem is tested, the SOC shall be no less than 95 % of the SOC according to paragraphs 6.2.1.2.1. and 6.2.1.2.2. for REESS designed to be externally charged and shall be no less than 90 % of SOC according to paragraphs 6.2.1.2.1. and 6.2.1.2.2. for REESS designed to be charged only by an energy source on the vehicle. The SOC will be measured by a method provided by the manufacturer.

## Slide 5: Draft proposal #3 OICA proposed
After the adjustment of the SOC according to paragraphs 6.2.1.2.1. and 6.2.1.2.2. above, the test shall be started as soon as practically possible subject to taking all reasonable and practical steps to ensure the initial SOC (i.e. the SOC achieved at the end of the adjustment according to the paragraphs 6.2.1.2.1. and 6.2.1.2.2. above) is maintained.

## Slide 6: Progress at Tokyo
At TF meeting at Tokyo on 29 feb. 2016, about for para. 6.2.1.2.3. , all TF members reach agreement.

## Slide 7: Agreement para. 6.2.1.2.3
When the vehicle or REESS subsystem is tested, the SOC shall be no less than 95 % of the SOC according to paragraphs 6.2.1.2.1. and 6.2.1.2.2. for REESS designed to be externally charged and shall be no less than 90 % of SOC according to paragraphs 6.2.1.2.1. and 6.2.1.2.2. for REESS designed to be charged only by an energy source on the vehicle. The SOC will be confirmed by a method provided by the manufacturer.

## Slide 8: Summary
TF6 have agreed with all the proposal draft concerning SOC adjustment.
We have finished all TF6 work.
I will input our formal proposal draft to IWG before Washington D.C. meeting.