## Slide 1: SG DSSAD 26 OICA contribution regarding yaw rate
24.04.2025

## Slide 2: Usage of yaw rate: To evaluate whether ADS appropriately behaved to avoid collision, together with the detected distance and relative velocity
Scene example:
ORU ahead of ADS vehicle suddenly decelerate, and ADS vehicle needs to change the direction to avoid a collision.
Evaluating ADS performance:
Whether crash avoiding manoeuvre by changing the course (= Lateral rotation speed of the ADS = yaw rate) is sufficient or not, at the detected distance and the relative velocity in each moment, toward the detected collision event / EDR trigger (=Time 0).
Advantage of yaw rate vs. vehicle heading:
Collision can happen in every direction and vehicle heading in absolute geo direction itself does not relate to the safety performance of ADS.
When using absolute direction of ADS, ORU’s position in absolute direction also need to be known, but it is not feasible.
Yaw rate is widely used for the vehicle motion analysis and the information is available by commonly used g sensor (► more robust technology).
Absolute direction change can be translated into the vehicle rotation speed, but it needs an additional calculation and lowering the accuracy.
ADS
ORU
Yaw rate
Detected object distance
&
Relative speed