## Slide 1: Possible Ways Forward with Outstanding Issues with SIM and Withholding HORs Orientation Slides
Submitted by the TF on ADAS leadership
Document ADAS-38-02
38th TF on ADAS, 30 April 2025
Provisional agenda item 4.1.

## Slide 2: Not Completed Working Items (Outstanding Issues) As reported by the TF on ADAS to the 21st GRVA session in GRVA-21-36
Extending system-initiated manoeuvres and conditions of withholding Hands-On Requests beyond the conditions of para. 5.3.7.2.4.10. of UN R 171
We intend to address now
Key Question: What provisions are needed in UN R 171 to enable such vehicle operation?
Optimizing in-service periodic reporting information (Table 1 of Section 7 of UN R 171) (still remains open)
Reference:
“5.3.7.2.4.10. The system shall only initiate a manoeuvre if the vehicle is located on a highway (including highway slip roads) and it is not withholding HORs”.

## Slide 3: Raised Concerns Regarding Driver-System Interactions (1/2)
Several Contracting Parties identified concerns regarding driver-system interactions, for which safe and proper vehicle behavior should be evidenced, such as (ADAS-37-06):
  Drivers’ ability to take control during system’s performing DDT with an incorrect situational awareness or unexpected situations (e.g., fallen tree)
    Could be subject to accident statistics (to find a border line from manual driving)
    Could be addressed in vehicle control strategy
    Could be addressed by adding new provisions
  Drivers’ ability to respond to critical events after prolonged withholding hands-on requests (“hands-free” operation)
    This is more relevant to highway operation (already allowed by UN R 171)
    Could be subject to drivers’ survey
    Could be subject to accident statistics
  The effect of prolonged “hands-free” operation on drivers’ retention of manual driving skills
    This is more relevant to highway operation (already allowed by UN R 171)
    Could be disproved or answered by field data
    Could be subject to drivers’ survey
  Drivers’ ability to manage secondary controls relevant to DDT while “hands-free”
    Could be addressed in vehicle control strategy
    Could be addressed by adding new provisions

## Slide 4: Raised Concerns Regarding Driver-System Interactions (1/2)
Several Contracting Parties identified concerns regarding driver-system interactions, for which safe and proper vehicle behavior should be evidenced, such as (ADAS-37-06):
  Drivers’ ability to cancel or override system-initiated maneuvers safely (already addressed by UN R 171 -> “controllability”)
    Could be addressed in vehicle control strategy
    Could be addressed by adding new provisions
    Could be verified by physical testing
  Drivers’ ability to remain engaged and situationally aware during system-initiated maneuvers, during long trips and over a long period of frequent system usage
    This is more relevant to highway operation (already allowed by UN R 171)
    Could be subject to drivers’ survey
  Crashes involving systems capable of system-initiated maneuvers and “hands-free” operation are not predominantly caused by controllability issues, drivers’ misuse, or overreliance
    Could be subject to accident statistics or field data
    Could be subject to drivers’ survey

## Slide 5: Longer Term Considerations:
  Collection and analysis of the accident data in jurisdictions where these systems are already deployed such as the US and China (Note: these systems are not compliant with UN R 171)
  Development of questionnaires for drivers who use the systems capable of SIM and withholding HORs. Collection and analysis of the drivers’ replies
  Optimizing in-service periodic reporting information (Table 1 of Section 7 of UN R 171)

## Slide 6: Thank you for your attention!