## Slide 1: UN-R158 Component Approval
JABIA

## Slide 2
UN-R158 N2,N3 Vehicle
In the case of N vehicles, cameras, monitors and processing equipment are
often sold as a set by RVCS manufacturers.
However, since the RVCS manufacturer is not a vehicle manufacturer,
Part II cannot be approved.
Body
Vehicle manufacturer
(Only cab cassis)
RVCS Manufacturer
Body builder install the RVCS
Power

## Slide 3
UN-R158 Component (Important!)
Image
correction
Image
Difficult to approve angle of view !
The projected images are images that have undergone complex image modification.
therefore it can only system approval.
There are a lot of ways to cut an image.
Camera
photographic subject
before
after
Image correction

## Slide 4
Separation of Installation and Components Approval
Components(Part I)
Area of camera positions (UN-R158 15.2. Annex9 2.)
Response time from Reverse signal (UN-R158 16.1.2.1.)
Object size (UN-R158 16.1.1.)
System (UN-R158 16.1.1.1.-16.1.2)
Installation(Part II)
The installation on vehicles of RVCS
which have been type-approved to Part I of this Regulation
Whether the vehicle has a reverse signal or not
Optional equipment which may affect the rearward field of vision
Check the mounting position of the monitor and camera
Of course, Part I and Part II may be merged and approved by Part II.

## Slide 5
UN-R158 Component …Camera angle of view performance
(Even without a vehicle, the camera position can be simulated.)
Area of camera positions (UN-R158 15.2. Annex9 2.)
Determine the area in which the camera can be installed
using a test jig.
Rear end of Vehicle
Camera
Camera
UN-R158 Annex2
Notes: Inversion of the idea

## Slide 6
UN-R158 Component
Response time from Reverse signal (UN-R158 16.1.2.1.)
Reverse signal
Requirements of UN-R158 16.1.2.1.
Test by RVCS manufacture
※UN-R158 Annex2 2.2(d)
Initiate/start the second timer, in accordance with the manufacturer's specification and
no later than when the reverse mode or gear is engaged.
Gear is engaged
Rear-view image on monitor
If the monitor shows the rear-view image within 2 seconds from the reverse signal, requirement of UN-R158 16.1.2.1. is satisfied.
It’s UN-R48 6.4.7. signal
(JPN 別添52 4.5.7.)
Notes: Using a reversing lamp signal would solve the problem.

## Slide 7
UN-R158 Component
Object size (UN-R158 16.1.1.)
Replacement of UN-R46 Class I mirror
(monitor capable of being adjusted
by the driver from the driving position.)
Put the camera on the worst position
Measure the size of the object on the monitor

## Slide 8
UN-R158 Component
Object size (UN-R158 16.1.1.)
Even if the vehicle changes, performance can be guaranteed without identifying the vehicle by fixing the furthest distance to be authenticated.
Fix (max 1500mm)
About 900mm
About 1000mm

## Slide 9
UN-R158 Component
System (UN-R158 16.1.1.1.-16.1.2)
Processor
Overlay system etc.
All devices (cameras, monitors and processors etc.) are sold as a set by RVCS manufacturers.
Power

## Slide 10
Installation Approval
Reverse signal (available or not)
Mounting position of the monitor and camera
Body
Optional equipment which may affect the rearward field of vision
Components approval checks with the devices installed on the vehicle

## Slide 11
RVCS Manufacturer
Guarantee the angle of view of the camera.
Body builder
Design the layout of obstacles.
Guarantee area
Decide on the mounting position of the camera so that there are no obstacles blocking the object.
Next Page

## Slide 12
Design review for installation
If the position is correct, it is legal even if the camera has a different angle of view.