## Slide 1: Aecs regulation Post-crash check with HMI method

## Slide 2
Context
01

## Slide 3
Context
Homologation time to be consider for one new function
  Part I – AECD (~4 weeks)
  Part II – AECD installation (~2 days or more)
   OEM aim to build harmonized and optimized testing plans
It exists currently 4 test methods using the over-the-air transmission for the MSD and voice call via a real or simulated PLMN and GNSS networks, or using the wired method.
These test methods will interfere with R94/R95 homologation procedures because focused after each crash test
It exists other approval protocols already used by technical services which uses vehicle HMI (e.g. EMC)

## Slide 4
Constraints
For methods 1 to 4, AECS post-crash approval is included within the R94/R95 protocol (after each crash test)
Specificities of Electrical Vehicle which increase the verification time after crash (~30 minutes)
Need a network coverage within crash facilities or a specific location to conduct the post-crash tests after the moving of the crashed car
Take into account the AECD power supply autonomy in the above cases (e.g. Back-up battery)

## Slide 5
AECD/AECS test phases for test methods 1 to 4
EMC R10
Mobile network access check
HMI check
Power Supply check
GNSS check
Sled test
Crash-tests
R94 / R95
Objective Audio test (optional)
PART I
AECD
PART II
AECS
R94/95
tests
OR
Functional check
Test methods 1 to 4
>3 weeks for the first approval (tbc)
Test methods 1, 2 and 3 : 1 day
Test method 4 : > 1 day
MSD content
Subjective Audio test
HMI – status indication
R94 and/or R95 operations + (optional) Electric Vehicle
Safety measures
1 additional day without crash preparation (tbc)
1 day (tbc)

## Slide 6
AECD/AECS test phases for test method 5 : HMI check
EMC R10
Mobile network access check
HMI check
Power Supply check
GNSS check
Sled test
Crash-tests
R94 / R95
HMI check
Test method 5
PART I
AECD
PART II
AECS
R94/95
tests
OR
eCall pre-crash operations only for Method 5
Audio test
MSD content
<1 hour
1 day
HMI by camera or recording signals
OPTIONAL
Visual check of the audio parts
(speaker, mic)
R94 and/or R95 operations + (optional) Electric Vehicle
Safety measures
1 additional day without crash preparation (tbc)
>3 weeks for the first approval (tbc)

## Slide 7
Synthesis
Benefits
  The main operations are now pre-crash, and can be done without time constrains just before the R94 or R95 homologation, and outside the crash area.
  Very fast post-crash check through video camera, or electrical signals recording, by checking a HMI’s sequence.
Drawback
  Need to have an extended self-test strategy within AECD/AECS

## Slide 8
HMI check procedure proposal
02

## Slide 9
Requirements
HMI check / Test method 5 can be only used if the in-vehicle AECD/AECS is capable :
1- to check and diagnose the electrical connections between all of the following devices :
- AECD control module
- PLMN communication module + antenna
- GNSS receiver + antenna
- Power source (from vehicle or back-up source)
- Warning/Information device (HMI)
- Hand free audio equipment (microphone, speaker)
2- to discriminate a network failure from an internal failure of the AECD Unit,
the communication with GNSS and mobile networks and PSAP is deemed to be compliant if no internal failure warning is indicated by the vehicle HMI.

## Slide 10
Pre-crash procedure
Cameras which records the Dashboard
(tell-tales) during EMC tests

## Slide 11
Pre-crash procedure
Camera used during
crash test

## Slide 12
Pre-crash procedure
These operations are to be done before the R94 (frontal) and/or the R95 (Lateral) crash tests :
1- Functional check by test methods 1 to 4 following a manual call :
- Conformity of the content of the MSD (location, time stamp, vehicle identification)
- Hands-free voice communication assessment.
For this specific procedure, the possibility to use the subjective voice intelligibility test method should be allowed, as in European eCall with the rated performance at least “3” (appendix 3 to Annex 9), the objective test could also be chosen at the demand of applicant.
2- Installation in the vehicle of the video camera needed to check all HMI involved during an emergency call, or a recorder for all HMI signals.

## Slide 13
After the R94 or R95 crash, the technical service will check the recording of the video camera or the recorded HMI signals, to verify if the HMI sequence defined by the manufacturer is conform.
[optional]
A visual check could be done to verify the damage on the audio parts (loud-speaker and the microphone).
Post-crash procedure : HMI check

## Slide 14
Post-crash procedure : HMI check
t
Example of a sequence of HMI during a crash test, and possible failures.
AUTO
AUTO
AUTO
AUTO
AUTO
eCall
operational
+
Networks OK
Trigger
event
Automatic
eCall detected
Establishing
connection
with PSAP
FAST
SLOW
- Connected to
PSAP
- MSD sending
- Voice request
and starts it
FAST
Crashtest
R94
or
R95
System failure
Partial failure
Impossible to
Contact PSAP
after time-out
AUTO
No coverage
Conform sequence
Possible failures
EXAMPLE

## Slide 15
Visual inspection of audio parts
03

## Slide 16
Post-crash procedure : Visual inspection of audio parts
STATEMENT :
From point of view of functioning principle, a microphone and a loud-speaker are based on the same electrical, mechanical and physical principles.
EXPERIMENT :
What is the behaviour of a loud-speaker in function of its mechanical damage ?
Let’s listen and compare the effects of different damages on a loud-speaker

## Slide 17
Post-crash procedure : Visual inspection of audio parts
Loud Speaker 1
in good condition
Loud Speaker 2
half of the membran
is cutted
Loud Speaker 3
membran and frame
are cutted in 2 locations
Male
Female
Tests sentences
from ITU website

## Slide 18
Post-crash procedure : Visual inspection of audio parts
What is your opinion regarding the inteligibility of these differents sentences in several language ?
- Have you had some trouble to understand the sentence in your native language ? For each damaged loud-speaker ?
- Only a « severe mechanical damage » of the loud speaker or the microphone, or the impossibility to visually check these parts, could lead a complementary
audio subjectif test, at the demand of technical service.