## Slide 1: ETRTO comments on the co-chairs limit setting proposal
TFTA 21 May 2025

## Slide 2: Why is ETRTO not in favor of the concept of a stringent limit (1.0) with a higher tolerance at the beginning that will be tightened over certain period?
ETRTO’s opinion is that limit settings are aimed to eliminate the worst performing tyres from the market, while the tolerances, whatever they are, should reflect the test methods variability [NEW: while COP represent also production variability].
Those parameters have to be addressed in the regulation, but the tolerance cannot be an instrument to increase artificially the limit requirements.
Moreover, tolerance is usually one of the parameters that imply misleading outcome during the market surveillance, raising also unnecessary liability conflicts.

## Slide 3
Abrasion Index
Type Approval
Limit
COP
Tyre A OK
Tyre B high risk of non compliance in COP
Option 1 (cochairs’ proposal):
0 or low COP tolerance
In practice, tyre manufacturers will have to integrate almost all method uncertainties in their risk assessment. Commonly tyre manufacturers will target to have products positioned on average below limit - 2σ (95% confidence interval).
Abrasion Index
Type Approval
Limit
COP
Tyre A OK
Tyre B OK
Option 2 (ETRTO proposal):
COP tolerance ≈ 2 σ
Products positioned on average below the limit
Rationale for a coherent COP tolerance
To ensure effective gain abrasion index it is necessary to set COP tolerance and limits separately.

## Slide 4
Analysis of co-chairs proposal, assuming COP tolerance 0
Normal : 1.30 then 1.15 type approval limit for convoy vehicle method
=> in practice 1.00 (2 σ=0.30 => 1.30-0.30) then 0.95 (2 σ=0.20? => 1.15-0.20) to be targeted by tyre manufacturers for average positioning of products
=> removal rate of 68% then 78%
3PMSF: 1.20 type approval limit for convoy vehicle method
=> in practice 1.00 to be targeted (2 σ=0.20)
=> removal rate of 70%

## Slide 5: ETRTO proposal
Measurement Uncertainty should be included in the gap between type approval limit and COP (0,25) (as it is the case for Rolling resistance)
The co-chair proposal for addressing the MU concern for Normal tyres could be managed in the following way:
  UHP allowance of 0,10
  Constraints on testing temperature range for UHP tyres to improve reproducibility.
   Proposal will simplify the scheme of the regulation.

## Slide 6: Conclusion
When confronted with newly born test methods that have a significant uncertainty, according to tyre industry experience across many years, it is crucial to set a COP coherent with the measurement uncertainty.