## Slide 1: ETRTO additional considerations on limits setting criteria
TFTA 33rd session: 21 May 2025

## Slide 2: Considerations on limits setting criteria
About co-chairs limit proposal ETRTO would like to remark the following:
1) A newly introduced requirement is different from tightening of existing requirements
Abrasion is a new requirement → the entire tyre population will have to be newly assessed, and after assessment, part of it to be re-designed or removed from the market, depending on the limits
Previous UN high impacting changes to requirements (on existing regulations) were set on the basis of an impact assessment of the performance of the current market, impacting less than 25% of the product lines (e.g. R117.02, wet grip or much less for wet grip in worn conditions):
  this kind of magnitude of removal rate has always been relevant to tightening of already regulated performances: manufacturers do not need to assess the entire population in this case
  In general for newly regulated performances with new test methods introduced, the market removal vs the Market Assessment dataset, has been significantly lower (e.g. less than 5% for wet grip at worn).

## Slide 3: Considerations on limits setting criteria
2) Any requirement limit target shall be considered vs the proper application timeline:
  At the time of EU Euro 7 Regulation publication*, the impact assessment analysing the potential economic, social, and environmental impacts of different policy options, did not address tyres: ETRTO limit proposal is based on the Market Assessment vehicle R117 certified tyres test results
  In the case of Abrasion, at EU level at least, the C1 requirements will apply from mid 2030 to the entire tyre market. An ambition of removing 60-70% of the market in such a short time has no precedent and it is not grounded. R117.04 tightened limits on existing requirements for RR/WetGrip targeted to impact about 25% of the market. The impact of of this massive removal of the market is not fully assessed in terms of business continuity and product availability.
Additionally, as mentioned, the impact on tyre re designing is directly linked to the removal rate and will impact beyond tyre industry (vehicle industry).
https://data.europa.eu/doi/10.2873/249061

## Slide 4: Thank you