## Slide 1
Review of EVS 9th Meeting
1> TF8 catch an agreement on the definition of heavy duty electric vehicles as below:
heavy vehicles cover the vehicles belong to category 1-2 with GVM exceeding 4,500kg and the vehicles belong to category 2 with a GVM exceeding 3,500kg equipped with electric power train containing high voltage.
2> China think heavy duty vehicles could be included in the EVS-GTR as an Annex or as the main document content, and nobody is disagree with that.
3> The agreement opinion about items` adoptions is as below:
Applicable items:
1.Thermal shock and cycling; 2.External short circuit protection;
3.over charge protection; 4.over discharge protection;
5.over temperature protection; 6.Fire resistance;
Time : Sep, 16,2015
Address: Changchun
Participants: experts form China, NTSEL, OICA, JAMA, EC
Meeting Summary:

## Slide 2
Review of EVS 9th Meeting
Exemption items: 7.Low energy; 8.Mechanical integrety ;
Modification items: 9.Vibration test ; 10. Leakage requirement;
Not decided items: 11.Water immersion/water resistance;
12.Thermal propogation; 13. venting ; 14.warning;
Addtion:
1.Not decided items are depend on these items for passenger vehicles;
2.Font: phase1 work;
Font: depend on the passenger vehicles part;
Font: phase2 work;

## Slide 3
Review of 6th TF8 Meeting
Time :Jan, 22, 2016
Address: Brussels
Participants:
(in person): EC (DG GROW, JRC), JASIC, UTAC, OICA (ACEA, JAMA, SCANIA, Daimler, Renault, Volvo Cars) - Total 10 participants
(Web/audio):China (TF8 leader, BYD, CATARC), NTSEL, OICA (JAMA)
Meeting Summary:
1> China provide the vibration road test data that shows the vibration acceleration on buses is smaller than passenger vehicles part, and China suggest the random vibration is more close to the practical situation. Other members are not oppose to this but that needs more convincing reason.
2> OICA review the Annex draft by them that shows they are also agree to include the heavy vehicles into the EVS-GTR .

## Slide 4
Key Points of TF8 works
1. This part of EVS-GTR specifies safety-related performance of electrically propelled road heavy duty vehicles and their rechargeable energy storage systems.
Heavy duty vehicles cover vehicles of Category 1-2 with a gross vehicle mass (GVM) exceeding 4,536kg , [and category 2 with a GVM exceeding 3,500kg ]equipped with electric power train containing high voltage bus, [excluding when vehicles can be connected to the grid and at the same time moved by its own propulsion system ] .
Comments from China :
1.1> The reason for scope of EVS-GTR main document is not enough.
Page 8, 4.1 section only explain the reason for heavy vehicle`s exemption of crash requirements, but EVS-GTR considers about safty requirement in normal use either, So that`s not convincing to define the GTR scope as passenger vehicles.
1.2> Heavy vehicles could be included in the main document of EVS-GTR. Because most items for passenger vehicles could be used applied to heavy vehicles directly or could be exempt for heavy vehicles, besides other items also are the same in principle ,the only difference may be the test parameters.

## Slide 5
Key Points of TF8 works
Comments from OICA:
1.3> OICA support to include heavy vehicles into the EVS-GTR as an Annex.
1.4> items not included in R100 may be postponed to phase 2.

## Slide 6
Key Points of TF8 works
Definition of “subsystem”
Comments from china:
“Subsystem” means any functional assembly of REESS components. The subsystem which represents the same safety performance as complete REESS could contain cells,electrical connections, electrical components, electric management controller, physical support and so on.
This explaination is much more important to heavy vehicles than passenger vehicles,
For the REESS in heavy vehicles contains more pack with much bigger dimensions and much heavier weight ,that`s impossible, at least impractical, to test the whole REESS, so in almost all the test items , the manufactures prefers to chose to test with related subsystem(s) whose test result can reasonably represent the performance of the complete REESS under the same conditions. So that`s very important to clarify the definition of “subsystem”.

## Slide 7
Key Points of TF8 works
Vibration test
Comments from OICA:
1> Propose alignment with requirements in R100.02, since this is already applied in EU and Japan.
Comments from NTSEL:
2> Support vibration test align with R100.02 in phase 1 and work on improving test profile in phase 2.
Comments from China:
3> China support a random vibration test for that`s more close to the practical situation.
From BYD test report, we find the acceleration for heavy vehicles is smaller than passenger vehicles request, so China suggest more research on vibration test in phase 1 . Besides ,in order to get convincing rational for vibration test, China suggest to find out how the parameters defined in r100, that helps a lot.

## Slide 8
Key Points of TF8 works
Vibration test
Comments from OICA:
1> Propose alignment with requirements in R100.02, since this is already applied in EU and Japan.
Comments from NTSEL:
2> Support vibration test align with R100.02 in phase 1 and work on improving test profile in phase 2.
Comments from China:
3> China support a random vibration test for that`s more close to the practical situation.
From BYD test report, we find the acceleration for heavy vehicles is smaller than passenger vehicles request, so China suggest more research on vibration test in phase 1 . Besides ,in order to get convincing rational for vibration test, China suggest to find out how the parameters defined in r100, that helps a lot.