## Slide 1: Progress report of Sub Group EV (WLTP-14-15e) 14th WLTP IWG 26 April 2016
WLTP-14-15e

## Slide 2
1. Summary
# | items | RESULTS | status | remarks
EV_1 | HEV system power | Status report by EVE-IWG Continue to collaborate with EVE and develop the test procedure. | OPEN | Classification, Downscaling
EV_2 | Normalization | Initial study report by Japan Discussed next actions | OPEN | Study the applicability to HEV
EV_3 | Supplemental Test (low temp./high altitude) | No progress. (need close collaboration with TF) | OPEN | Handle EV unique portions
EV_4 | Supplemental Test (auxiliary device) | No progress (need close collaboration with TF) | OPEN | Handle EV unique portions
EV_5 | Post processing | Agreed ACEA document with slight modification as a base concept. | OPEN | Handle EV unique portions
EV_6 | Durability | Status report by EVE-IWG including Japan position | OPEN | study on battery durability
EV_7 | OBD | No progress | OPEN | Handle EV unique portions
EV_8 | FCV | No progress | OPEN | OVC-FCV Flow Method
EV_9 | gtr amendment | Agreed ACEA document with slight modification. More amendment is expected. | OPEN | 

## Slide 3
EV_1 : HEV system power
Overview:
Due to absence of HEV system power, all HEVs are classified class_3 and are not allowed downscaling (which are applicable for ICE vehicles, see next slide). WLTP is asking EVE-IWG for developing the methodologies of HEV system power.
EVE-IWG working progress is going well as expected.
Basic concept was developed and detailed procedure are under the discussion. WLTP SG EV is requested to provide the clear guidance for different type of HEV system
Current status:
Next Actions:
Continue to collaborate with EVE-IWG.
Provide clear guidance to EVE-IWG.
Confirm the threshold of classification and downscale ratio after HEV system power developed.

## Slide 4
 | ICE or Motor Power |  | Power Curve | Vehicle Max Speed＋Distance compensation (regional)
 | Classification | Downscale | Shift points | 
ICE | ✔ | ✔ | ✔ | ✔
PEV | NO Why : few statistical data Current : Class3 |  | NO Why : no definition of power curve Current : maker recommended | 
OVC-HEV | NO Why : no definition of system power Current : Class3 | NO Why : no definition of system power Current : WOT |  | 
NOVC-HEV |  |  |  | 
NOVC-FCHV |  |  |  | 
Cycle
Modif.
Veh.
category
Phase2 working items
EV_1 : HEV system power

## Slide 5
EV_2 : Normalization
Overview:
WLTP-IWG has made a decision not to apply “Normalization” since no study on EVs has done during Phase1 activities. After completion of EVs study, applicability of “Normalization” should be re-discussed.
“Normalization” works same level as ICE vehicles for all parameters under CS conditions on specific model.
“Normalization” doesn’t work for all parameters under CD conditions.
Current status:
Next Actions:
Asking other parties for additional study.
Consider the way (possible options) to proceed:
  No correction algorithm but apply drive trace index with criteria for all type of vehicles
  Apply correction algorithm on only parameters which are well justified
  Develop the methodologies to take care of all parameters
 | CO2/Fuel Consumption | Range | Electric Consumption
CS conditions | so-so | NA | NA
CD conditions | NG | NG | NG

## Slide 6
EV_6 : Durability
Overview:
Durability performance up to useful life is one of working items during phase2 activities. After confirming the CP needs which parameter need to be evaluated up to useful life, WLTP-IWG takes care of ICE and/or pollutant devices.
At the same time, WLTP SG EV takes care of EV specific requirements on performance and durability.
Only EC has requested to consider parameters which have an effect on EV performance and durability
All stakeholders understand the difficulty to develop general test procedure at this stage
Recommendation of IWG EVE: it is premature to develop a procedure for battery and therefore vehicle durability; the topic should be continuously followed and the recommendation could be changed
Current status:
Next Actions:
A. Continue collaboration between WLTP and EVE
B. Asking for feedback of contracting parties
C. Evaluation if a specific aging procedure is necessarily needed
or if vehicle performance criteria could be an alternative

## Slide 7
EV_5 : Post Processing
EV_COP : introduce new EU COP procedure
EV_9 : gtr amendment (Phase 1b)
EVAP. TF : EVAP test procedure for HEVs
EV_5 : Introduction and discussion of ACEA proposal (WLTP-SG-EV-11-04_rev1/05/06/07).
These documents are basis for further amendment during phase 2a (e.g. the integration of corrections coming from supplemental test task force)
EV_COP : Introduction of new EU COP procedure for PEVs and OVC-HEVs (WLTP-SG-EV-11-11 and WLTP-SG-EV-11-12)
EV_9 : Introduction and discussion of ACEA proposal (WLTP-SG-EV-11-08_rev1)
EVAP. : Introduction of proposal to SG EV by Japan (WLTP-14-xx TF Evap Status report)
Current status:
Next Actions:
Asking WLTP-IWG for adoption of Post Processing (EV_5) and GTR amendment (EV_9)
EV_COP will be further discussed in next SG EV meeting
EVAP: SG EV will continue to follow TF EVAP meetings to address EV issues

## Slide 8
2. Next Actions
# | items | 2016 | 2017 | 2018 | 2019
EV_1 | HEV system power |  |  |  | 
EV_2 | Normalization |  |  |  | 
EV_3 | Supplemental Test (low temp./high altitude) |  |  |  | 
EV_4 | Supplemental Test (auxiliary device) |  |  |  | 
EV_5 | Post processing |  |  |  | 
EV_6 | Durability |  |  |  | 
EV_7 | OBD |  |  |  | 
EV_8 | FCV |  |  |  | 
EV_9 | gtr amendment |  |  |  | 
collaborate with EVE
consider classification threshold and downscale ratio
additional study
“Normalization” or “Indexes” ?
Amend_1
Amend_2, if necessary
OVC-FCV
collaborate with OBD TF
takes care of EV unique items
Amend_2, if necessary
Amend_2, if necessary
complete
decision for next step
collaborate with EVE
collaborate with TF
collaborate with TF