## Slide 1: WLTP Phase 2 – carryover from 1b – Annex 4 Starting note on split runs in coast down testing
draft
An earlier proposal was to limit the number of splits to 2 (3 segments).
This would prevent some OEMs / test tracks from coast down testing, therefore the issue was skipped.
Alternative solutions have to be developed within this new Annex 4 TF within phase 2. It may include also new issues in that context (improving methods / tightening tolerances, where possible).
Within phase 1b, practically all tolerances within road load and specifically coast down testing have been tightened.
This was proposed by industry and mainly triggered by the results of the road load validation. They had made obvious, that coast down testing is the most inaccurate way determining road load – but that we cannot avoid that method for several reasons.
One of these set of measures was the issue of "split runs".
Split runs are necessary, if the distance of the coast down track is too short, to coast down from ~145 to ~15 km/h within one straight track (up to 6km can occur).
Parameters, that "produce" that problem: - road load of the vehicle in relation to mass - length of track
Parameters, that interfere potentially negatively: - warm-up between the split runs - track between the straight parts (e.g. turning radius)
Measures, that help to improve the result: - statistical requirement between runs – already in place. - new requirements  to be developed.
WLTP-14-18e

## Slide 2: WLTP Phase 2 – carryover from 1b – Annex 4 Information on acceleration for dyno setting
Initially a fixed acceleration of approx. 6m²/s³ was drafted.
For vehicles, not achieving that, a solution (full throttle) was included.
For normal passenger vehicles, that will easily outreach the 6m²/s³, this acceleration requirement is mainly test burden: One coast down run (acceleration + coast down) lasts approx. 10km. Typically 3-4 runs are needed  40km! Especially in COP-testing, kilometres should be limited.
As IWG road load experts concluded, that higher accelerations are to the worst case direction. It was agreed, to set the 6m²/s³ as a minimum and allow for higher accelerations.
That was presented and adopted in Geneva 01/2016.
draft
This issue is presented to ask IWG, if during the review since the Geneva-meeting in 01/2016, questions have emerged.
Recommendation: Conformation of current text.