## Slide 1: Unresolved data elements from EDR-DSSAD-IWG-26-15
EDR-DSSAD-IWG-29
Department for Transport, UK
30/09

## Slide 2: Yaw rate and vehicle orientation – loss of traction
ADS
ORU
yaw rate
ADS
ORU
ADS
ORU
No yaw rate
No yaw rate
Intended direction of ADS
Direction of motion
N
N
N
orientation
orientation
orientation
Without vehicle orientation it is not clear whether ADS was attempting to avoid ORU, particularly in low adhesion event
ORU = other road users
Steering input
No Steering input
Steering input but no change in orientation would suggest a Loss of traction
Direction of motion
Direction of motion

## Slide 3: Conspicuity Data Elements (Lighting, turn signal, hazard flasher, audible warning system)
If the status of the ADS direction indicator is not known, it cannot be determined whether the:
  ADS intentionally or unintentionally crossed the lane
  ADS signalled its intended manoeuvre appropriately with enough notice
  ORU failed to take notice of ADS signal
Therefore, it would be uncertain whether the ADS was at fault
Same situation would occur with other conspicuity data elements
  For exterior lighting - was the ADS making itself clearly visible in low light conditions
  For hazard warning - was the ADS giving an appropriate signal to ORUs
ADS
ORU
ADS
ORU
ADS
ORU
ADS
ORU

## Slide 4: ADS-requested/vehicle indicated gear
Inconsistencies between gear requests and actual gear engagement could indicate critical failures in actuation of the transmission system, potentially leading to loss of vehicle control, which would be indicated by a difference in the ADS requested and vehicle indicated gear.
ADS
ORU
P
R
N
D
Request:
P → D
ADS
ORU
P
R
N
D
Actual:
P → R

## Slide 5
Vehicle indicated service braking
Vehicle indicated service braking can help determine any communication failures from the ADS requesting the service brake. It can also help us determine any brake system issues (unexpected or wrong level of braking applied for the situation) or ADS-decision making errors (braking applied while driving such as phantom braking)
Questions to consider:
If we don’t have this point, how do we determine whether this is a fault of the ADS requesting the braking system or a fault with the braking system itself?
Where will the ESC be implemented in these systems? As part of the ADS or separately to it?

## Slide 6: Recording data post occurrence
It is important to record data after a safety critical occurrence has happened because data collection post-event​ gives us:
1. The full incident sequence, including impact and the vehicle resting state​
2. The operational actions of the vehicle operator(s) after the crash​, did the vehicle behave appropriately and come to a safe stop or carry on driving? Did it choose an appropriate MRC?
3. Contributions of other stakeholders to the event and injuries – corroborating what happened with other witnesses
3s
No data recorded after this point