## Slide 1: Equitable Occupant Protection IWG – report to 78th session of GRSP
Chair: Pernilla Bremer, SE
Co-Chair: Corina Klug, AT
Secretariat: Torbjörn Andersson, CLEPA
Philipp Wernicke, OICA

## Slide 2: Strategic goals and top priorities for the IWG EqOP
Strategic goals – from ToR
Equitable and overall enhanced protection of a diverse population
  Regulations must be inclusive
Robust, inclusive and effective regulatory solutions
  Avoid bias in protection
  Offer protection strategies which reduce the injury risk below a certain threshold for as many as possible
Top priorities – endorsed by GRSP
Rear-end impact (soft tissue neck injuries)
Frontal impact (restraint systems)
Extension of assessment towards currently not considered injury types with high frequency and risk of PMI (brain, soft tissue neck, lower extremities)

## Slide 3: What do we mean with robustness?
Body shapes and initial positions
Injury risk
Body shapes and initial positions
Tolerance level
Robust system
Sub-optimised system
Body shapes and initial positions
Inferior system
Current regulations can identify a clearly inferior system.
Current regulations do not encourage robustness.
How can we assess that we have a robust, not a sub-optimised system?
AIM!

## Slide 4: Decisions and activities in IWG since last GRSP
Dashboard on the wiki: https://wiki.unece.org/display/trans/EqOP+IWG+General+Matters
Accidentology on the wiki: https://wiki.unece.org/display/trans/EqOP+IWG+Accidentology
Workshop ”Equity issues in frontal impacts relevant for restraint systems”
  Based on preparatory material, reading list and summaries of field data
  Extensive presentations on possible improvement in frontal impact safety for diverse occupants
Agreement to kick off task force on frontal impact and restraint systems
Agreement on equity issues and related hypotheses for their root causes

## Slide 5: Result workshop 1/2; see also ’Summary document’ – Consensus on equity issues based on frontal impact field data
Overall improvements in vehicle safety are observed for all groups, with decreasing differences in injury severity outcome between females and males reported in several studies (Kullgren et al. 2020, Noh et al. 2022).
The majority of real-world crashes occur at speeds lower than those specified in regulatory test protocols. The high frequency of low-severity crashes contributes to a considerable number of injuries, the majority of them at AIS1 and 2 level (Ostling et al. 2024, EqOP-Workshop-04-08e - Frontal Impact Crashes - A GIDAS Analysis-1). Based on unweighted GIDAS sample, Ostling et al. 2024 reported that the risk of sustaining AIS 2+ injury in those crashes was found to be equally highest for occupants of small cars, but higher for females across all other vehicle categories. The representativeness of those results for the whole of Germany and their robustness regarding other datasets and countries must still be assessed. Moreover, the study uses EES as crash severity indicator, which as well should be further reviewed in the future, as US studies (Brumbelow et al., 2022, Farmer et al., 2025) indicated the importance of considering the mass ratio between the colliding vehicles and delta-V to account for biological gender-specific differences in crash characteristics.
Fatality risk increases with age. US data shows that differences in fatality risks between females and males are age dependent; where young females are at higher risk than young males and elderly males at higher risk than elderly females (Noh et al. 2022, Abrams et al., 2024). It is currently not clear if this trend is true for other regions.
Differences in injury patterns, risks, and outcomes are observed, depending on vehicle size, vehicle generation, sex, age groups, seat positions, obesity, and crash severity ranges.
Females seem to be at higher risk for being injured than males. Some of the reviewed studies (Kullgren et al. 2020, Brumbelow et al. 2022, Farmer 2025, Abrams & Bass 2024, Ryan and Knodler 2022) indicate a statistically significant higher risk for females of being injured than males, but the ratios differ depending on the following:
  Injury severity: Brumbelow et al. (2022) found a statistically significant higher risk for females at MAIS 2+ levels, but no statistically significant sex-based difference at MAIS 3+ levels when analysing crashes which were compatible and in which the case vehicle’s front airbag deployed.
  Seat position: Noh et al. (2022) reported that the overall fatality risk difference between female and male drivers is minimal (0.5 ± 17.5%), whereas for right-front passengers, females show a higher risk (5.3 ± 16.4%).
  Other studies (Wallbank et al. 2024; Noh et al., 2022) show no statistically significant differences. None of the reviewed studies indicate a higher overall injury/fatality risk for males, only for specific injury types.
The field data studies showed that the injured body region, the severity of the injury (AIS) and the occupant position (passenger or driver) all lead to variations in the risk of injury between males and females.
No single injury stands out in terms of equity issues
  The injury risk seems to be distributed over different body regions with females exhibiting a higher risk in some but not all regions
    Concussion (AIS2+) (Antona-Makoshi et al., 2018)
    Lower Extremity Injuries (AIS 2+) (Brumbelow, 2023)
    Neck Injuries (AIS 1+) (EqOP-Workshop-04-08e - Frontal Impact Crashes - A GIDAS Analysis-1)
    Sternum Fractures (AIS 2+) (Ranmal et al., 2024)
    Abdominal Injuries (AIS 2+) (Brumbelow et al., 2022; Ryan et al., 2022; EqOP-Workshop-04-07e - Sex-Based Disparities in Abdominal Injury Risk (JAMA JARI).pdf citing Abrams et al., 2022
  Elderly occupants, independent of sex, exhibit a higher risk of thoracic (AIS2+, AIS3+) (Ranmal et al., 2024) injury and subdural haematomas (AIS 3-4) of the head (Antona-Makoshi et al., 2018)
The same type of injury is observed to result in different outcomes (risk of permanent medical impairment, shock index) depending on the age of the person and if they are male or female (Kullgren et al., 2020; Somasundaram et al. 2024).

## Slide 6: Result workshop 2/2; see also ’Summary document’ – Consensus on hypotheses of reasons for equity issues in frontal impacts
Occupant Physiological and Psychological Characteristics
  Injury risks in a crash are influenced by age and body shape.
  Body shape (including the internal anatomy) is influenced by sex, age, body height, geometric proportion, weight and weight distribution.
  Body shapes affect the interaction of the occupant with the seatbelt, airbag, seat, and the vehicle interior.
  Psychological characteristics have the potential to influence a person’s perception of risk and comfort, which potentially leads to changes in seat position and seat adjustments (affecting also body position in seat), as well as seatbelt routing across the body.
Seatbelt and Seat Interaction
  Seatbelts are among the most effective life-saving technologies in road vehicles. A seatbelt system includes in a broad sense the belt retractor, buckle, belt webbing and its routing, force loading mechanisms such as pre-tensioners and load limiters, and anchorage points.
  The way a vehicle occupants engage with the seatbelt system depends on their body shape and factors such as the way they adjust the seat (seat back adjustments, seat forwards or rearwards) and seatbelt (the d-ring position) and where the occupant is positioned (in front driver seat or in any of the passenger seats), as well as electronic controls of the seatbelt such as trigger times and loading forces. While seatbelts protect, imperfect fit may decrease their effectiveness:
    Poor shoulder belt interaction with the body can result in the occupant slipping out of the seatbelt, and excessive or rotational torso and head excursion.
    Poor lap belt interaction with the body can result in excessive pelvis displacement or submarining.
  Seat pan performance is important for the prevention of submarining; seat design in general is important for belt routing and fit.
Airbag Interaction
  Interaction with the airbag is strongly influenced by the interaction with the seatbelt, which as mentioned above can be influenced by body shape.
  Furthermore, airbag interaction is affected by the distance and contact situations which is affected by position of the seat as well as the body posture and shape of the occupant.
Interaction with Vehicle Interior
  The interaction with the vehicle interior is strongly influenced by the interaction with the seatbelt, seat and airbag.
Injury Tolerances
  Bone density changes with age and may differ between sexes, which contribute to varying injury tolerances.

## Slide 7: Ongoing task forces
Rear impact seat assessment with focus on soft tissue neck injuries
Virtual crash testing
Frontal impact and restraint system requirements
Extension of assessment towards currently not considered injury types with high frequency and risk of PMI
  Lower extremity injuries in frontal and side impacts
  Upper extremity injuries in frontal and side impacts
  Brain injuries in frontal and side impacts
  Soft tissue neck injuries in frontal and side impacts

## Slide 8: Rear impact assessment
  2 meetings
  Next meeting TBD
  TF agreed to focus on the complete seating system – discussion about how to evaluate the combined performance of the seatback and headrest
    Either by complementing static testing with a quasi-static procedure or by shifting toward more dynamic testing
  The next in-person workshop is being planned for Q2 2026
    A smaller group with both contracting parties and industry will plan the workshop

## Slide 9: Frontal impact and restraint system requirements
Discussed topics derived from the workshop:
  a. Prevent submarining phenomena for all occupants
    i. Integrate submarining criteria into type approval tests (e.g., iliac wing force measurement)
    ii. Refine geometric requirements to improve belt fit for diverse body shapes
  b. Assess abdominal injury risks
    i. Identify causes
    ii. Reproduce injury mechanisms in approval tests using methods with for example ASIS and ATPS
    iii. Evaluate predictive capability of THOR-05F and validate abdominal injury risk curves
  c. Account for occupant diversity, and seat positions and adjustments
    i. Extend testing to rear seats
    ii. Allow random seat position and adjustment selection by technical services
  d. Address real-world crash speeds
    i. Explore methods to assess injury mechanisms at lower, more common crash speeds
  e. Develop a multi-scenario protection evaluation procedure
    i. Create a test protocol covering varied speeds and occupant diversity, aligned with holistic models such as for assessment of emissions
To be prioritized during the next meeting(s)

## Slide 10: Frontal impact and restraint system requirements
Next meeting on 28.1.2026 12:00 CET
Priorities and next steps
    Abdominal injuries and submarining – further field data analysis
      Germany, Austria, Sweden
      JARI & JAMA (HBM simulations to understand injury mechanisms)
    Rear row – further field data analysis
      CLEPA
      Austria, Sweden
    Robustness
      Field data show combinations of equity issues; how can we assess that restraint systems become more robust?
      Find ways to avoid suboptimisation without increasing the number of official tests and to secure harmonized testing among different Technical Services.

## Slide 11: Virtual crash testing
  3 meetings
  Next meeting TBD
  Master document containing agreed parts of the procedure (working document)
  Presentation on the status of the building blocks in the procedure for VCT
    ISO-scores
    Vehicle component validation
    Hybrid III qualification
    HBM qualification
    Traceability
  Next step to determine
    Value of HBM to close equity issues
    If it´s possible to use HBMs in regulations within the next 10 years
    Readiness of respective component models

## Slide 12: Extension of assessment towards currently not considered injury types with high frequency and risk of PMI
  No meetings since last GRSP
  Next meeting planned to be held in Q1 2026
  Topics for discussion and prioritization
    Investigate application of DAMAGE for assessment of AIS4+ Diffuse Axonal Injuries for application in Dummy (HIII or THOR) tests
      What causes the risks and how can it be replicated in type-approval test
    Investigate how to enhance current evaluation of lower extremity injuries
    Investigate how to enhance current evaluation of soft tissue neck injuries in frontal crashes

## Slide 13
The author and the speaker of this presentation confirm that they have authorization to use all content including photos and visual elements.
The material is either copyright-free or the author/speaker hold the necessary copyright or permission.
The UNECE will remove any material from its events and supporting websites if there is unlawful use of copyrighted material.
The author/speaker takes responsibility for any infringement on copyright and holds the UNECE harmless to this effect.