## Slide 1: OICA Position on Tyre Abrasion Limits
TF TA – 34th session
3rd of June 2025

## Slide 2: OICA Position on Tyre Abrasion Limits
OICA is highly supportive to reach the goal of improving abrasion rates of tyres
OICA insists that the upcoming tyre regulation must not lead to reject tyres from the market without a realistic choice of alternatives in all segments
Tyre abrasion limits as proposed are developed only on data for normal and 3PMSF tyres. Additional groups of tyre designs require further considerations

## Slide 3: Test methods
OICA is concerned that limiting the test method choice might lead to supply chain issues.
OICA represents vehicle manufactuers from all over the world and thus asks to respect regional preferences.
OICA supports keeping both on-road and drum method, while continuing the work to improve and align both methods.

## Slide 4: XL Tyres
Extra Load (=XL) tyres (per definition also incl. High Load tyres) run with elevated inflation pressure levels and exhibit due to their design and application requirements a different abrasion behavior
XL tyre designs are required for certain vehicle applications (e.g. combined performance and trailer use requirements)
Design alternatives to XL tyres would lead to increased tyre dimensions to achieve the same load index, which results in higher total wear rates and less environmentally friendly tyres due to increased tyre dimensions
OICA supports the proposal* by providing an allowance for the AICT of +0,1

## Slide 5: Legal Race Tyres
Legal race tyres represent only a very minor market share (0,2%) of the overall tyre market and are designed for very special purposes (race circuit use) – public road use is extremely limited
OICA supports the proposal* to exclude this group of tyres from the tyre abrasion regulation

## Slide 6: Special SS and AR combination
Tyres with SS >= Y and AR <= 40 are designed to ensure very high dry grip performance to ensure especially safety requirements while their use in terms of market share (7,2%) is only limited
Only a few of tyres with these specifications were part of the market assessment, usually, they are mounted on one axle only – both facts might lead to increased uncertainties
Mixed tyre fitments also mean that possible tyre combinations on the after market are limited for the customers already. Without respecting the peculiarities of those tyres for the regulation, product availability and customer choices will suffer extremely (in worst case, tyre combinations will disappear from the market)
OICA supports the proposal* by providing an allowance for the AICT of +0,10, as it is also the case for « Worn Wet Grip » legislation
* UNECE GRBP TF TA session 33, “TA-33-8 ETRTO responses on TFTA co-chairs questions and limit proposal final”,
https://wiki.unece.org/download/attachments/298778721/TA-33-8%20%20ETRTO%20responses%20on%20TFTA%20co-chairs%20questions%20and%20limit%20proposal%20final.pptx?api=v2