## Slide 1
Feedback Opinion about CLIV Regulation Direction for Light-duty Vehicle
The 9th IWG on CLIV
Submitted by experts from China

## Slide 2
NO. | Content | CLEPA Opinion | Feedback from China
1 | Technology fusion overview（Page 6） | General regulatory approach: define tests that need to be met - whatever technology or combination is used (regulation must be "technology neutral") Some combinations appear not to have an added value; a multitude of other combinations is possible The focus should be on useful warnings/interventions. | Agreed. The regulations will not limit what technical means to use. No matter what detection method is used, as long as the child can be detected and meet the requirements for warning or intervention, it is fine.
2 | Scenarios 1&2, test cases, child ages and CRS types （Page 7） | A proper description of test cases is needed | Specific description: TBD Seven tests are required for each seat.​​ Test 1： The newborn dummy is used to sit on the rearward-facing CRS, and the dummy is in a sleeping state.​​ Test 2： A one-year-old dummy is used to sit on a rearward-facing CRS, and the dummy is in a sleeping state.​​ Test 3： A one-year-old dummy is used to sit on a rearward-facing CRS, and the dummy is awake (can have movement).​ Test 4： A 3-year-old dummy is used to sit on a forward-facing CRS, and the dummy is in a sleeping state.​ Test 5: A 3-year-old dummy is used to ride on a forward-facing CRS, and the dummy is awake (can have movement).​ Test 6: A 6-year-old dummy is used to sit on a forward-facing CRS, and the dummy is in a sleeping state.​ Test 7: A 6-year-old dummy is used to sit on a forward-facing CRS, , and the dummy is awake (can have movement);

## Slide 3
NO. | Content | CLEPA Opinion | Korea Opinion | Feedback from China
3 | Temporary deactivation （Page 9） | CLEPA is open for some flexibility related to temporary or long-term deactivation. | Necessary. Korea does not have strong opinion on how to deactivate, but there should be options of deactivation in case of light vehicles. | The temporary and long-term deactivation functions are not mandatory, but if the vehicle has this function, it needs to meet a series of requirements. Such as avoiding misuse and providing status indication after deactivation. Relevant requirements should be established in regulations.
4 | Long term deactivation （Page 9） |  |  | 
5 | System trigger（Page 10） | a) CLEPA OK with 15s; 3 min would be too long. b) in-vehicle reminder is OK, but not sufficient as the only warning c) not needed if "gained access" is not covered | 60 seconds after the doors of vehicle are locked. The shorter time for sensing would be the better, but some manufacturers say they need enough time for sensing in order to minimize false alarm. | TBD For CLEPA: a) Agree for 15 seconds; b) Agreed c) There are two situations: One is Scenario 3, where the delay from the door closing to the initial alarm should not exceed 10 minutes; Second, the delay function is used, which can delay for up to 10 minutes before activating the initial warning.

## Slide 4
NO. | Content | CLEPA Opinion | Korea Opinion | Feedback from China
6 | ATD for direct sensing （Page 15） | Test tools are needed for UN regulation testing, ongoing discussions and development activities; dedicated ISO CPD test tool group. | 1、Reference point for the measurement and calibration is necessary to place a dummy in a vehicle. 2. Calibration specifications would be necessary. If dummies have movement like breathing mechanism, there should be calibration cycle and procedure. 3. If the ISO is going to make a prototype or pilot dummy, the CPs of IWG CLIV would like to participate in the round robin tests. 4. Specifications for testing would be desirable. Although the ISO might not deal with test procedures, if there is any conditions to use the surrogate, such as temperature or humidity, those conditions should be stipulated. 5. Amendment to M.R.1 would be necessary. World SID is included in both ISO and M.R.1. | TBD For CLEPA: Agreed. For Korea： 1. Agreed, when the dummy is placed on the seat, it can be directly installed in the CRS without the need for a reference point. When placing the dummy in the footwell, it is necessary to determine its position and posture to ensure consistency in testing. 2、The calibration standards and cycles for dummies can be defined, and the procedures or methods may vary for different dummies. Should we follow the dummy manual? 3、Agreed. 4、Test conditions can be defined, but it is necessary to investigate the impact of conditions (temperature and humidity) on the dummy and the test results. 5、

## Slide 5
NO. | Content | CLEPA Opinion | Korea Opinion | Feedback from China
7 | applicable categories M1 & N1（Page 17） | Ensure that vehicles typically used as "family cars" are covered within the regulation; include "large" SUVs and pick-up trucks; extension of current TOR likely needed | category 1-1 (M1) passenger cars. For N1, only the vehicles has second row seats and subject to install CRS, or specify as pick-ups. Most Koreans do not use N category vehicle for carrying people, so N are not subject to install CRS. Maybe we can give options like each CP can use its own vehicle categorization when adopting this regulation. | TBD Further discussion is needed. Is it possible to not define the vehicle category? The regulations apply to all vehicles equipped with CPD systems.
8 | detection range（Page 17） | rear row seats (3rd row - if fitted - included) and front passenger seat; seating positions relevant for "child left behind“ | second-row and beyond seats, or passenger cabin. Trunk, frunk, or anywhere that are not intended to put passengers should be excluded. | TBD Further discussion is needed. Further confirmation is needed: CLEPA recommends all front and rear seat positions (including the driver's seat?), excluding the footwell? Korea suggests not including the front seats, only the rear seats. does it include footrests?

## Slide 6
NO. | Content | CLEPA Opinion | Korea Opinion | Feedback from China
9 | way of detection: indirect or direct? （Page 17） | requirement for direct sensing (while allowing support from indirect systems for driver information/alerts, but not as standalone system) | 1)Direct sensing of breath per minute rate. Sensing the breath would be the hardest. If a sensor can detect the breath, it can detect any other movements. Types of sensors shall be up to the manufacturer of vehicles. Regulation should remain technology neutral. 2) Other Opinion: Let‘s keep the regulation technology neutral. As long as children left in vehicle can be detected, any system can be used. If a manufacturer is confident that indirect sensing would be enough to do the job, indirect sensing should be allowed to be applied. | Agree with Korea 2) other opinion, keep technical neutrality, and no matter what technology is used, as long as it meets regulatory requirements.

## Slide 7
NO. | Content | CLEPA Opinion | Korea Opinion | Feedback from China
10 | age range （Page 17） | 0 - 6 years; future discussion needed on how to deal with situations where adult is still in vehicle.0 - 6 岁； | 0 year old in asleep. This would be the worst case for detection. If 0 year old without movement can be detected, others would be easily detected as well. | For CLEPA: Agree that children aged 0-6. We think that no need to make warnings if there are adults in the car. For Korea: We have different opinions, 0-year-old can only be installed in rear facing child seats. If only this condition is tested, it may cause the manufacturer to install sensors at the back, which may not detect forward facing children in actual situations. It is still necessary to test more operating conditions to ensure that the sensor can take into account in various practical situations.
11 | scenarios to be covered （Page 17） | CLEPA in favor of focusing on "child left behind" in UN regulation | ---- | Need to discuss whether scenario 3 (Child enters unlocked vehicle and becomes trapped)is included

## Slide 8
NO. | Content | CLEPA Opinion | Korea Opinion | Feedback from China
12 | self-check（Page 18） | 'Self-check - warning to the driver shall be given if failure is detected (if not already part of OEM specifications -> OICA is investigating; should these CPD self-checks be done at beginning or end of journey?) | Unnecessary It is manufacturer's' job to make sure their system or device function properly. It is not something regulators should worry. | TBD Can accept the opinions of Korea.
13 | special scenarios（Page 18） | Child without CRS is possibly a meaningful test case for certain world regions More than one child in the vehicle - CPD systems shall cover such a situation Mid-journey getting on and off the vehicle - should not be relevant for direct sensing (was an issue for certain implementations of indirect systems) | ---- | Can accept the opinions of CLEPA.
14 | System robustness（Page 18） | System robustness assessments could be considered. | ---- | Acceptable opinions, corresponding testing conditions that affect system robustness should be considered for different technical means, such as camera schemes that need to be tested both day and night.

## Slide 9
NO. | Content | Korea Opinion | Feedback from China
15 | Types of alert signals | audible & visual Warning should be same with buses. Is there any other vehicle warnings that involves smart keys or smartphone? Additional warnings can be provided by vehicle manufacturers, but that should not be regulation. This is a vehicle regulation. Children left in vehicle should be detected by vehicle and alerted by vehicle. | TBD Further discussion is needed. (Refer to E-NCAP: From vehicles or keys; Sound or visual signals; Tactile signals can also be accompanied by sound or visual components.)
16 | Warning phases (initial to escalation) | Unnecessary There seems no necessity for phased warning. Let's keep it simple. | TBD Further discussion is needed. Suggestion: It is not mandatory, but if the vehicle has this function, it should meet the relevant requirements. Regulations should include relevant requirements for multi-level warnings, such as the trigger of escalation warning.
17 | Intervention | Unnecessary The proposed ways of intervention seems either ineffective or goes beyond the scope of vehicle. | TBD Further discussion is needed. Suggestion: It is not mandatory, but if the vehicle has intervention, it should meet the relevant requirements. Regulations should include relevant requirements for intervention, such as the timing of intervention.

## Slide 10
NO. | Content | Korea Opinion | Feedback from China
18 | Cancellation of alarm | Opening the door of vehicle The driver should physically open the door of the vehicle and check if there is any child left in the vehicle. | TBD Further discussion is needed. Partially agree, this can be used as a way, but not the only way. Close range cancellation is ok.
19 | False positive | Let's not include false positive in the regulation. Manufacturers are responsible to make their system function properly. | TBD Agreed, frequent false alarms may cause customer complaints or grievances, so companies will try to control the false alarm rate. Another reason is that false alarms themselves do not have an impact on children's safety (because children are not in the car), they can be excluded from regulations.

## Slide 11
Thanks for your attention!