## Slide 1: Representative Vehicle
Explanation of draft

## Slide 2: Vehicle LCA: Representative vehicle is key link between declaration and application
Vehicle LCA
Electricity Modeling
Primary data share
Secondary data set
End of life modeling
Representative vehicle
Reporting rules
Verification process
Labelling
Green public procurement
Incentive
…
Methodology
Declaration
Application
According to method proposed by SG2/3/4/5/6
Representative vehicles
NOT in SCOPE of GUIDELINE
Completely up to contracting parties
Notes: CATENA X: mention verification framework for components

## Slide 3: Vehicle LCA : Why we need a representative vehicle ?
Material
acquisition
Material
Refining
Vehicle
assembly
System
Assembly
Part
production
Ideal LCA calculation: Track each component of each vehicle  NOT manageable
Complex Supply chain:
It is required a simplification for the calculation of the carbon footprint
It is not practical to follow energy use minute by minute.  Instead, use average values over a set time (e.g. 12 or 24 months)
It is impossible to track every source  Average production values (e.g. secondary data set)
It is not efficient calculating LCA for each individual vehicle, no additional benefit  Use a representative vehicle (this makes calculations simpler and reduces the workload)

## Slide 4: Vehicle Carbon footprint : Modular Approach
Material acquisition
Part Production
Vehicle assembly
Well to Tank
Tank to wheel
Re-use
Recycling
End of Life
Usage
Production
Actual Vehicle mass without battery (kg)
Given Battery Model
Carbon footprint (CO2 eq)
Carbon footprint (CO2 eq)
+
Vehicle mass with options (kg)
Carbon footprint (CO2 eq)
Vehicle Cycle energy demand
Carbon footprint (CO2 eq)
+
-Per Battery Model
-Per production plant
According to existing WLTP regulation with additional co-efficient on ‘well-to-tank’ and ‘real- life usage’
Calculated values on Representative vehicle
Estimated values for declared vehicle
A modular approach is best suited for vehicle life cycle carbon footprint
-Vehicle structure family
-Powertrain type
-Region of Production
Vehicle cycle energy demand
Carbon footprint (CO2 eq)
+
Battery type
Vehicle
Structure
Usage
Maintenance
Recycling

## Slide 5: Upstream Emission : ICE vehicle
Vehicle Structure Family
Vehicle structure Family 1
Vehicle structure Family 2
Vehicle structure Family n
…
Region of production
Region 1
Region 2
…
All Body Types of a same vehicle structure are covered by same group
An upstream LCA group can cover only one region
LCA Group 1
Representative vehicle
Highest selling vehicle
Actual vehicle mass, with installed options (kg)
Carbon Footprint kgCO2e
Powertrain Type
EV
ICE
…
Production
All the variations of one powertrain type are covered by same group

## Slide 6: Upstream Emission : Electric vehicle
Vehicle Structure Type
Vehicle structure Family1
Vehicle structure Family2
Vehicle structure Family n
…
All Body Types of a same vehicle structure are covered by same group without the traction battery
LCA Group 2
Representative vehicle
Highest selling vehicle
Actual vehicle mass, with installed options w/o traction Battery (kg)
Carbon Footprint kgCO2e
Region of production
Region 1
Region 2
…
An upstream LCA group can cover only one region
Powertrain Type
EV
ICE
…
Battery Type
Chemistry A, capacity 40kwh
Chemistry A, capacity 60kwh
Chemistry B, capacity 80kwh
…
Production
A
B
Actual vehicle mass, with installed options (kg)
Carbon Footprint kgCO2e
w/o traction Battery
w/ traction Battery A
w/ traction Battery B

## Slide 7: Use phase Emission : ICE/EV vehicle
Maintenance
IP Family 1
IP Family 2
IP Family n
…
Region of usage
Region 1
Region 2
…
Powertrain Family
IP Family 1
IP Family 2
…
Cycle energy demand (kg)
Carbon Footprint kgCO2e
A single value from a powertrain group can be considered
Use phase
Declared vehicle
Vehicle individual*
Cycle energy demand
Carbon Footprint kgCO2e
+
Cycle energy demand
Carbon Footprint kgCO2e
=
*Certified fuel consumption and energy consumption data, which are included in official homologation documents and regulatory certifications of contracting party.
OEM declare (if not available default value)
Grouping according to present practice of contracting party
Usage

## Slide 8: Representative vehicle example: Interaction with IP family and LCA grouping
IP 3
IP 4
IP 1
IP 2
LCA group : does not include use phase criteria ( powertrain config.) => May include multiple IP families
IP family : Vehicle segment or platform or region of production is not a criteria => May include multiple LCA family
LCA group 1
(upstream & End of Life)
LCA group 3
(upstream & End of Life)
LCA group 2
(upstream & End of Life)

## Slide 9: EoL Emission : ICE vehicle
Vehicle Structure Family
Vehicle structure Family 1
Vehicle structure Family 2
Vehicle structure Family n
…
Region of End of life
Region 1
Region 2
…
Actual vehicle mass, with installed options (kg)
Carbon Footprint kgCO2e
All Body Types of a same vehicle structure are covered by same group
An EoL LCA group can cover only one region
LCA Group 1
Representative vehicle
Highest selling vehicle
Powertrain Type
EV
ICE
…
End of Life
Similar approach to upstream emission
All the variations of one powertrain type are covered by same group

## Slide 10: Example how to follow Representative vehicle approach

## Slide 11: Representative vehicle: How can be implemented ?
Customer Order
Choice of
Vehicle type
Powertrain type
Options etc.
LCA group
LCA Group 1
LCA Group 2
LCA Group 3
LCA Group 4
LCA Group …
Battery Type
Battery model 1
Battery model 2
Battery model …
Powertrain Family
IP Family 1
IP Family 2
IP Family 3
IP Family 4
IP Family …
Upstream & End of Life emission
Vehicle structure family, Powertrain type, production region
╚> Emission factor upstream = 5 kg CO2e/kg
╚> Emission factor EoL = 0.15 kg CO2e/kg
Actual Vehicle mass with installed options without battery
╚> mass w/o battery = 1398 kg
Battery
╚> Battery carbon footprint 6350 kg CO2e
Use phase emission
Powertrain family => IP family 4
╚> energy consumption real life (WTW)= 9412 kg CO2e
Powertrain family => IP family 4
╚> maintenance factor = 148 kg CO2e
Upstream + EoL = (5 + 0.15) * 1398 + 6350 = 13550 kg CO2e
Use phase= 9412 + 148 = 9560 kg CO2e
Total CFP
23 110 kg CO2e

## Slide 12
384 kg
Step 1
Rep-resentative Vehicle
Traction battery emission
6.350 kg CO2,eq
Total carbon footprint
6.935 + 6.350 + 9.640 +208
= 23.133 kg CO2,eq
Separate calculation
Representative vehicle
Actual vehicle mass, with installed options w/o Battery: 1.387 kg
LCA Group 2
Carbon footprint calculation*
Upstream:
EoL:
6.935 kg CO2,eq
Upstream Emission factor: UEF = 5,0 kg CO2,eq /kg
208 kg CO2,eq
EoL Emission factor: EEF = 0,15 kg CO2,eq /kg
1.387 kg
Representative vehicle for LCA Group 2
Calculated value
Estimated value
Step 3
Down-stream emission
IP family 2
VH
VL
IP family 2
Calculate In-use energy consumption
Calculate Maintenance
+
9.640 kg CO2,eq
*Excluding: Use phase & traction battery

## Slide 13
384 kg
Actual vehicle mass, with installed options w/o battery (kg)
Upstream Carbon Footprint (kgCO2e)
6.935 kg CO2,eq
6.990 kg CO2,eq
6.740 kg CO2,eq
Step 2
Upstream
End-of-Life emission
Vehicles for LCA declarations
LCA Group 2
Estimated Upstream Carbon footprint
Traction battery emission
6.350 kg CO2,eq
Total carbon footprint
6.990 + 6.350 + 9.560 +210
= 23.110 kg CO2,eq
6.740 + 6.350 + 8.620 +202
= 21.912 kg CO2,eq
Separate calculation
Declared vehicle 1
Declared vehicle 2
Calculated value
Estimated value
Step 3
Down-stream emission
IP family 2
VH
VL
IP family 1
VH
VL
IP family 1
IP family 2
Calculate In-use energy consumption
Calculate Maintenance
8.620 kg CO2,eq
9.560 kg CO2,eq
Calculate In-use energy consumption
Calculate Maintenance
+
+
9.640 kg CO2,eq
1.387 kg
1.398 kg
1.348 kg
Emission factors LCA group 2: UEF = 5,00 kg CO2,eq /kg
EEF = 0,15 kg CO2,eq /kg
Actual vehicle mass, with installed options w/o battery (kg)
End-of-Life Carbon Footprint (kgCO2e)
208 kg CO2,eq
210 kg CO2,eq
202 kg CO2,eq
6.935 + 6.350 + 9.640 +208
= 23.133 kg CO2,eq
Representative vehicle for LCA Group 2
*Excluding: Use phase & traction battery
Estimated End of Life Carbon footprint
Step 1
Rep-resentative Vehicle
Representative vehicle
Actual vehicle mass, with installed options w/o Battery: 1.387 kg
LCA Group 2
Carbon footprint calculation*
Upstream:
EoL:
6.935 kg CO2,eq
Upstream Emission factor: UEF = 5,0 kg CO2,eq /kg
208 kg CO2,eq
EoL Emission factor: EEF = 0,15 kg CO2,eq /kg
1.387 kg