## Slide 1: HWT “Literature” Status Report
GRE/TF-GP 4th session
9 September 2025
TFGP-04-02

## Slide 2
Status of the activity so far
The HWT examined the following presentations extracted from the ADAC symposium material:
#12 Glare due to headlights – Jealousy of expensive cars or a real risk for traffic safety?
#15 The impact of luminance in nighttime encounter situations
#17 Soiling of headlight cover as a cause of glare presentation
#18 Glare Contributors in the Automotive world presentation
  A 1st meeting of the HWT was held on the 21 August 2025 to summarize and identify the first topics treated in theabove literature material.
Outcome of the examination (next page)
  Disclaimer
  Some referenced studies are old, and may not take into account the evolution of light technology

## Slide 3
Preliminary outcome of the examination
Illuminance is a major factor influencing glare and is connected to:
  Alignment of the headlamp
  Road geometry
Additional factors influencing glare:
  light color temperature
  Size of the headlamp (luminance, minor influence)
Soiling of the lens can greatly increase illuminance (6-7 times more than in clean conditions, 3 times higher than DRL)
  More common in periods with harsh weather conditions, where there are agents on the road contributing to the dirt sticking onto the headlamp (typical case: water/salt brine in winter times spread by winter maintenance vehicles)
Misaim of the headlamp is very common.
Reasonably new cars can show misaim already after 10.000 km of use.

## Slide 4
Additional observations
There seems to be a great difference in the results obtained from lab testing and real driving situations (measured according to both the De Boer scale and disability glare)
  Complex scenes or complex driving situations have influence on the feeling/sensitivity/thresholds/visual capability/discomfort of a test person.
  The test persons have to split their attention because of other stimuli and tasks they have to follow. And thus – thresholds increase, visual acuity decreases and discomfort rating increases (becomes less negative)
  These 2 items need to be taken into account while comparing lab testing and real driving situations

## Slide 5
Investigation points
More research needed on car fleets?
 original study was performed 10 years ago
What happens until the car is delivered (typically during transportation from the factory until delivery to customer)
What happens in the beginning of the vehicle life (typically in the first 10.000 km)
Difference in tolerance between the devices used to measure the alignment at OEM, PTI and garages

## Slide 6
Next Steps
3-Steps process:
Finalize the examination of the literature without any summary available
Merging of the inputs from the HWT Literature with those coming from GTB
Identification of aspects:
  covered by the literature
  where further research is needed
ADAC presentations:
  #13
  #14
  #16
  #19
Ref. 08 + 09
Ref.10
Ref.28
Ref.29
Ref.30
Ref.31
Ref.32

## Slide 7
🗓️ Timeline
2025 | 
ADAC material examination | 26 September 2025
2nd HWT meeting on ADAC material | 2 October 2025
Examination of docs Ref.08, 09, 10, 28 29 | October 2025
3rd HWT meeting | Last week of October 2025 (exact date TBD)
Examination of docs Ref. 30,31 and 32 + new UK study on glare (if available) | November 2025
4th HWT meeting | Last week of November 2025 (exact date TBD)
Submission of 2nd status report to TF-GP | 5th December 2025
2026 | 
Merging HWT Literature summaries | Beginning of January 2026
5th HWT meeting to identify known factors + areas for further research + concrete actions to mitigate glare + “who does it?” | Middle January 2026
Submission of final status report to TF-GP | End of January 2026