## Slide 1: Special Purpose Vehicles (SPV) in UN-Rs
Proposals for UN-R154/04, UN-R83/09 and UN-R168/01

## Slide 2: Overview SPV Categories.
Comparison between (EU) 2018/858 and R.E.3.
1: Only defined for EU 2018/858 | 2: Regulation (EU) 2018/858 | 3: Consolidated Resolution R.E.3
Name | Code1 | EU 2018/8582 |  | R.E.3.3 | 
 |  | Defined | Category | Defined | Category
Motor caravan | SA | YES | M | YES | M1
Armoured vehicle | SB | YES | - | YES | -
Ambulance | SC | YES | M | YES | M
Hearse | SD | YES | M | YES | -
Wheelchair accessible vehicle | SH | YES | M1 | NO | N.A.
Trailer caravan | SE | YES | O | NO | N.A.
Mobile crane | SF | YES | N3 | NO | N.A.
Special group | SG | YES | - | NO | N.A.
Converter dolly | SJ | YES | O | NO | N.A.
Exceptional load transport trailer | SK | YES | O4 | NO | N.A.
Exceptional load transport motor vehicle | SL | YES | N3 | NO | N.A.
Multi-equipment carrier | SM | YES | N | NO | N.A.
In scope of proposed amendments for UN-Rs, as SPV definitions are present in both (EU) 2018/858 and R.E.3
Not in scope of proposed amendments for UN-Rs, as SPV definitions are not present in R.E.3. First an amendment of R.E.3 would be necessary to introduce the additional “European” SPV definitions.
SPVs not in scope of the relevant UN-Rs (83/09, 154/04, 168/01) due to their vehicle categories (N3 and O).
To achieve as much harmonization as possible between the European and the UN Euro 7 requirements, SPV provisions should be transposed to the relevant UN-Rs.
Scope of the proposed amendments is focusing on those SPVs, which are defined in (EU) 2018/858 AND in the Consolidated Resolution on the Construction of Vehicles (R.E.3).

## Slide 3: Overview SPV Categories.
Special Provisions for SPVs within (EU) 2018/858 and Euro 7 Main Implementing Act.
Motor-caravans, ambulances and hearses:
All items of category “G” within the table of (EU) 2018/858, Annex II, Part III, Appendix 1 are related to multi-stage approval, a concept not present in the UN-set of regulations.
    No need to transpose requirements into UN-Rs.
  Hearses are not subject to ISC requirements in accordance with MIA Article 10 (8b).
    Needs to be transposed.
Armoured Vehicles:
Possibility for exemptions in accordance with the table of (EU) 2018/858, Annex II, Part III, Appendix 2 for the items of category “G” which are / will be covered by UN-R83/09, UN-R154/04, UN-R168/01 and UN-R on OBM.
  Possibility for exemptions need to be transposed.
  Armoured vehicles are not subject to ISC requirements in accordance with MIA Article 10 (8b).
    Needs to be transposed.
Armoured Vehicles: Possibility for exemptions need to be transposed to all relevant UN-Rs.
Hearses and Armoured Vehicles: Exemption from ISC measures need to be transposed to UN-R83/09.

## Slide 4
Overview SPV Categories.
Proposal on Special Provisions for Armoured Vehicles within UN-R83/09.
Paragraph 12, amend to read:
"12. Transitional and Special provisions"
Include a new paragraph 12.2. to read:
"12.2. Provisions for special purpose vehicles
12.2.1. Provisions for armoured vehicles
The responsible authority may grant type-approvals including exemption(s) to requirements of this regulation to armoured vehicles in accordance with paragraph 2.5.2. of the Consolidated Resolution on the Construction of Vehicles (R.E.3), if the manufacturer demonstrates that the vehicle cannot meet the requirements due to its special purpose.
The type of special purpose vehicle and the exemptions granted are to be described in point 1.0. of section I of the type-approval certificate in accordance with Annex 2 to this regulation.
The requirements on In-service conformity in accordance with paragraph 9. of this Regulation shall not apply to armoured vehicles.
12.2.2. Provisions for hearses
The requirements on In-service conformity in accordance with paragraph 9. of this Regulation shall not apply to hearses in accordance with paragraph 2.5.4. of the Consolidated Resolution on the Construction of Vehicles (R.E.3)."
Transposition of the requirements from (EU) 2018/858, Annex II, Part III, Appendix 2 to the UN-R.
Transposition of the exemption for ISC from MIA Article 10 (8b).

## Slide 5
Overview SPV Categories.
Proposal on Special Provisions for Armoured Vehicles within UN-R154/04.
Include a new paragraph 12.2. to read:
"12.2. Provisions for special purpose vehicles
12.2.1. Provisions for armoured vehicles
The responsible authority may grant type-approvals including exemption(s) to requirements of this regulation to armoured vehicles in accordance with paragraph 2.5.2. of the Consolidated Resolution on the Construction of Vehicles (R.E.3), if the manufacturer demonstrates that the vehicle cannot meet the requirements due to its special purpose.
The type of special purpose vehicle and the exemptions granted are to be described in point 1.0. of section I of the type-approval certificate in accordance with Annex A2 to this regulation.
Transposition of the requirements from (EU) 2018/858, Annex II, Part III, Appendix 2 to the UN-R.

## Slide 6
Overview SPV Categories.
Proposal on Special Provisions for Armoured Vehicles within UN-R168/01.
Paragraph 15, amend to read:
"15. Transitional and Special provisions"
Include a new paragraph 15.2. to read:
"15.2. Provisions for special purpose vehicles
15.2.1. Provisions for armoured vehicles
The responsible authority may grant type-approvals including exemption(s) to requirements of this regulation to armoured vehicles in accordance with paragraph 2.5.2. of the Consolidated Resolution on the Construction of Vehicles (R.E.3), if the manufacturer demonstrates that the vehicle cannot meet the requirements due to its special purpose.
The type of special purpose vehicle and the exemptions granted are to be described in point 1.0. of section I of the type-approval certificate in accordance with Annex 2 to this regulation.
Transposition of the requirements from (EU) 2018/858, Annex II, Part III, Appendix 2 to the UN-R.

## Slide 7
Proposed text aims to harmonize requirements for type-approval of motor-caravans, ambulances, hearses and armoured vehicles as SPVs between EU and UN legislation.
This would allow to type-approve SPVs either according to EU or UN legislation, which in turn increases potential acceptance throughout the world.
In addition to the current proposals, discussion should be started on the necessity of SPVs provisions for brake particle emissions and OBM.
Overview SPV Categories.
Summary.