## Slide 1: Time Until the CLIV Alarm Is Activated in the Japanese Guidelines
Danger
High Alert
Alert
Caution
Mostly Safe
Air conditioner shutdown
In Japan, guidelines for safety devices to prevent children being left behind on school buses were established in December 2022, mandating their installation on nursery school buses and similar vehicles.
These guidelines stipulate that the time from engine shutdown to the activation of the external warning (i.e., the time for checking inside the vehicle) must be within 15 minutes.
This 15-minute basis is determined from the following experimental results using WBGT (Wet Bulb Globe Temperature).
If the check is done within 5 minutes of engine shutdown (air conditioning shutdown), WBGT remains within the ‘Caution’ range, posing minimal risk at worst.
In Japan, no fatal incidents involving children being left behind have been reported since the guidelines were applied to school buses.
Assuming a situation where a child is left in a vehicle in a car park under the following conditions:
Weather: Sunny
Air temperature: 35°C
WBGT calculated using a heatstroke index meter
WBGT | Guidelines for Activities Requiring Caution | Precautions
Danger (31 or above) | Risk present in all daily activities | For the elderly, the risk of heatstroke is high even at rest. Avoid going out and move to a cool place indoors.
High Alert (28 to 30) |  | When going out, avoid direct sunlight; indoors, stay alert to rising room temperature.
Alert (25 to 27) | Risk associated with moderate or higher-intensity daily activities | When exercising or doing heavy work, take regular, sufficient rest breaks.
Caution (below 25) | Caution | Generally, the risk is low, but there is a risk of heatstroke during intense exercise or heavy work.
Heatstroke Index Meter
Source: JAPAN AUTOMOBILE FEDERATION (JAF) (https://jaf.or.jp/common/safety-drive/car-learning/user-test/temperature/summer)
Evolution of Wet Bulb Globe Temperature (WBGT)
5 min 10 min 15 min