## Slide 1
Contents | R94 (Offset) | R95 (Side) | R135 (Pole) | R137 (Frontal)
“except for those necessary to support the weight of the dummy” | O | X | X | O
“This is not applicable to convertibles where the top can be easily opened to allow the evacuation of the occupants” | O | X | X | O
“In case no displacement system is available for the evacuation of a rear seated occupant, it shall be shown that a 50th percentile manikin can be evacuated without the use of any devices to support its weight and any other tools” | X | O | X | X
“For vehicles of category N1 this evacuation may be done via an emergency window if this window can be easily opened, but if tools are necessary,(e.g. for breaking the window) those tools shall then be provided by the manufacturer and shall be visible and located in proximity to that emergency window” | X | O | X | X
“shall be capable of being released by a maximum force of 60/100 N on the centre of the release control” | O | O (but, no force) | X | O
“remove the dummies without adjustment of the seats” | O | O (but, no ‘without~’) | X | O

## Slide 2
Contents | R94 (Offset) | R95 (Side) | R135 (Pole) | R137 (Frontal) | R153 (REAR)
No door shall open during the test | O | O | X | O | X
Doors unlocked after test | O | O | X | O | X
Open at least one door per row of seats | O | O | X | O | X
To release the dummies from their restraint system | O (60N) | O | X | O (60N) | X
To remove the dummies from the vehicle | O | O | X | O | X
No interior device or component shall become detached in such a way as noticeably to increase the risk of injury from sharp projections or jagged edges; | X | O | X | X | X
Ruptures, resulting from permanent deformation are acceptable, provided these do not increase the risk of injury; | X | O | X | X | X
Any side door which impacts the pole shall not separate totally from the vehicle. | X | X | O | X | X
Any door which does not impact the pole and is not wholly partitioned from the passenger compartment by a permanently attached partition or fixed or fold-down seat back, shall meet the following requirements: 1) The door shall remain latched; 2) The latch shall not separate from the striker; 3) The hinge components shall not separate from each other or from their attachment to the vehicle; and 4) Neither the latch nor the hinge systems of the door shall pull out of their anchorages. | X | X | O | X | X