## Slide 1: 8th joint meeting of the WP.29 expert groups on regulatory fitness for ADS
Supporting material from GRVA TF FADS

## Slide 2: Category X and general safety
FADS acknowledges the fact that GRSG TF AVRS does not wish to exempt certain vehicles of Category X from the scope of certain regulations (R46, R121, R125…)
FADS proposes to strengthen the requirements for “special manual controls” in R13, R13-H and R79 in a way that would allow this exemption
  FADS could also consider requirements on preventing the overuse or misuse of this special controls in R13, R13-H and R79

## Slide 3: “Logic signal”
Several GRs have been using the words “logic signal” or “logical signal” to describe the signal sent from other vehicle systems to an ADS
FADS would like to emphasise the fact that “logic signal” means a binary 0/1 signal, and is not technologically neutral.
FADS therefore recommends to use only the word “signal”

## Slide 4: “Complies with UNR ADS”
FADS recommends to use the following words:
“…provided that the ADS complies with the requirements of UN Regulation No. [ADS] [or UN Regulation No. 157] according to its original version or later series of amendments.”
“or UN Regulation No. 157” should be included in most cases, but not in cases where it should not apply to an ALKS (e.g., because ALKS is an ADSF-1)

## Slide 5: Deactivation / reactivation
FADS recommends to use the following words for all functions that should not be ON at the same time as an ADS:
“[The function] shall be [deactivated] upon activation of an ADS feature, and shall not be able to be [activated] whilst an ADS feature is active.”
  This should be adapted to the wording of each regulation, e.g. in R171 “DCAS shall be switched to 'OFF' mode upon activation of an ADS feature, and shall not be able to be switched to 'ON' mode whilst an ADS feature is active.“
Also, for functions or systems that are automatically activated at the initiation of the powertrain): “[The function] shall be automatically reactivated/reinstated/etc. upon deactivation of an ADS feature.”
  For functions that are not automatically activated at the initiation of the powertrain, FADS proposes not to include any text about their automatic reactivation. This implies that the driver must activate them automatically after deactivation of the ADS feature.
    FADS has not encountered any GRVA function or system that is not automatically activated at the initiation of the powertrain, and that FADS believes should be reactivated automatically.

## Slide 6: Ignition / turned on / master control switch
Please note that several GRs are currently harmonising the wording across regulations to only refer to the notion of “powertrain” (M.R.2)
This is not usually relevant for our groups but if a task force is already planning to change a paragraph where the words “ignition, key ON, master control switch” etc. are used, FADS suggests to consider using “powertrain” instead in the whole regulation.

## Slide 7: Which definitions to include in each regulation
Definitions for ADS, DDT, and categories X and Y no longer need to be included (a footnote to R.E.3 rev 8 can be used instead)
Definitions for ADSF-1 ADSF-2 may be included as they are not present in R.E.3.
FADS does not recommend using definitions from UNR ADS that could clash with definitions from other regulations (e.g., using a definition of “driver” based on the DDT)
FADS does not recommend using other ADS-related definitions (ODD, etc.) unless absolutely necessary.

## Slide 8: Other standard text templates
“1.2. This regulation does not apply to:
  1.2.x. [Vehicles of categories X1 and Y1] / [Vehicles of category Y1]”
    1 As defined in the Consolidated Resolution on the Construction of Vehicles (R.E.3.), document ECE/TRANS/WP.29/78/Rev.8, https://unece.org/transport/vehicle-regulations/wp29/resolutions."
“Whilst an ADS feature is active”
“In the case of vehicles equipped with an ADS[F-2], …” or “For vehicles equipped…”
“In the case of vehicles of [categories X and Y], …” or “For vehicles of categories…”

## Slide 9: Other standard text templates: testing (replace text in red as appropriate)
  For vehicles of categories X and Y, all tests in this annex shall be conducted, and all respective requirements shall be fulfilled. In the absence of manual driving controls, tests shall be conducted using dedicated activation methods, which may include:
  (a) A test mode allowing to manually control or trigger the acceleration functions, or
  (b) Any other method subject to agreement between the vehicle manufacturer and the technical service, ensuring that the evaluation accurately reflects real-world ADS performance.
  Wherever this annex details a manual control being actuated or an action being applied on it, that shall be understood as an acceleration demand being made through the selected activation method above. The manufacturer shall demonstrate that the test activation method accurately replicates ADS performance, and a detailed description of the method used shall be included in the test report. The acceleration demand made shall be recorded in the test report alongside the results of each test.
  For vehicles equipped with an ADS, other than those of categories X and Y, the tests in this annex shall be performed at least in the manual driving mode. Tests do not have to be performed in ADS mode providing the manufacturer can demonstrate to the technical service that the same SLF performance can be achieved when acceleration demands are made by the ADS. However, testing to verify this shall be performed at the request of the technical service."