## Slide 1: Unresolved data elements from EDR-DSSAD-IWG-26-15
EDR-DSSAD-IWG-29
Department for Transport, UK
30/09

## Slide 2: Yaw rate and vehicle orientation – loss of traction
ADS
ORU
yaw rate
ADS
ORU
ADS
ORU
No yaw rate
No yaw rate
Intended direction of ADS
Direction of motion
N
N
N
orientation
orientation
orientation
Without vehicle orientation it is not clear whether ADS was attempting to avoid ORU, particularly in low adhesion event
ORU = other road users
Steering input
No Steering input
No change in orientation would suggest a Loss of traction
Direction of motion
Direction of motion
Notes: We have 3 scenarios here, the first is where the ADS is actively trying to avoid a collision which we could deduce from looking at the steering input and matching this with the yaw rate to conclude that it was actively trying to turn right. In the second scenario we have a vehicle with no steering input and no yaw rate colliding into the back of the vehicle. In the third scenario we also have no recording of yaw rate, however we can see from the orientation of the vehicle that there was some attempt to try and avoid this collision and this could have possibly been because of a loss of traction due to black ice etc. However if we do not have an orientation included then it is not clear to us when comparing the second and third scenario whether or not the ADS was attempting to avoid a collision. When it comes to yaw rate and vehicle orientation it’s common practice in collision investigation to have a level of redundancy to provide data integrity because incomplete datasets or questionable data integrity is a common issue and having redundant sources—such as both video and heading—enables cross-validation, which is a standard and critical practice in collision investigations.
TRL - we would have to use the raw data to calculate this which is possible but a lot of extra work for us. If there is not enough sufficient objects to calculate this then it won't be valid either
Video specification is not yet finalised The group has not yet agreed on what level of information can reliably be extracted from the proposed video/image element. Until it is clear that heading/orientation can consistently be derived from video, this data element should be retained.
Video resolution constraints From a collision investigation standpoint, the originally proposed 480p @ 30Hz is insufficient, even under ideal conditions. For orientation or dynamics analysis, 1080p @ 30Hz is the minimum acceptable standard, in line with commercial dashcam specs. More on this is provided in Point 4.
Video data limitations Real-world video data may be compromised (e.g. poor lighting, occlusion, fog, snow). In such cases, heading information is necessary where visual reference points are insufficient.
Redundancy and data integrity
Incomplete datasets or questionable data integrity is a common issue. Having redundant sources—such as both video and heading—enables cross-validation, which is a standard and critical practice in collision investigations.

## Slide 3: Conspicuity Data Elements (Lighting, direction indicator, hazard warning, audible warning)
If the status of the ADS direction indicator is not known, it cannot be determined whether the:
  ADS intentionally or unintentionally crossed the lane
  ADS signalled its intended manoeuvre appropriately with enough notice
  ORU failed to take notice of ADS signal
Therefore, it would be uncertain whether the ADS was at fault
Same situation would occur with other conspicuity data elements
  For exterior lighting - was the ADS making itself clearly visible in low light conditions
  For hazard warning - was the ADS giving an appropriate signal to ORUs
ADS
ORU
ADS
ORU
ADS
ORU
ADS
ORU
Notes: So conspicuity elements are any data elements that the ADS uses to make itself aware and indicate its intentions to other road users. In this scenario we have a collision where the ADS has crossed over into the right-hand lane and the ORU has collided into the back of them. If we were not to record the status of the ADS direction indicator, then it cannot be known if the ADS intentionally or unintentionally crossed the lane, when it signaled its direction indicator and therefore it if gave enough notice for the other road user to react to it lane change. So, it would be uncertain in this situation who was responsible for this collision. The same can be applied for the other conspicuity elements, such as exterior lighting, which is a very safety critical data element when it comes to driving in low light conditions, was the ADS making itself clearly visible in low light conditions and if not could that have been the reason why another road user collided with the ADS.

## Slide 4: Visual images
Our proposal for the resolution and frequency is 1080p at 10Hz.
This has been recommended by TRL’s forensic collision investigation team which includes specialists in forensic video retrieval and analysis, who have delivered forensic video analysis services to the UK courts for many years.
1080p has allowed for more robust analysis and thus better admissibility of the evidence produced for court. Given 4k is now almost standard for dashcams, it is not considered an onerous requirement to have a resolution of 1080p. This will give us sufficient image quality to support analysis in most circumstances without substantial storage demands of higher resolutions.
A higher resolution is more important than a higher frequency, as we are more concerned with when a hazard becomes perceivable, and so we need higher quality images for this. Having a lower frequency will also help offset the data storage requirements.
Compression of the images can also help reduce the storage requirements, so long as they do not cause a significant loss of image quality when compressed.

## Slide 5: Visual images
Proposal:
1If any of the cameras used to produced the visual images is unable to meet this requirement then the native resolution of that camera will be provided instead. Any file compression used shall not result a discernable loss in image quality.
2This should provide a 360 view around the vehicle that covers a distance relevant to its ODD
Data element | Condition for requirement | Resolution | Minimum Range2 | Recording interval/time (relative to time stamp) | Data sample rate (samples per second) | Accuracy
Visual images | Mandatory | 1080p1 | - | -10 to 10 sec | 10Hz | N/A

## Slide 6: ADS-requested/vehicle indicated gear
Inconsistencies between gear requests and actual gear engagement could indicate critical failures in actuation of the transmission system, potentially leading to loss of vehicle control, which would be indicated by a difference in the ADS requested and vehicle indicated gear.
ADS
ORU
P
R
N
D
Request:
P → D
ADS
ORU
P
R
N
D
Actual:
P → R
ADS requested vs vehicle indicated:
ADS requested means the control signal issued by the ADS to operate a system on the vehicle which is contributing to the performance of the DDT
Vehicle indicated means the signal produced [or received] by a system on the vehicle that provides the actual status of that system
Notes: For the conspicuity elements and also the vehicle gear, our proposal includes recording both the ADS-requested actions and vehicle-indicated outcomes is important for identifying:
Misalignments in motion planning and actuation
Potential system-level integration faults, including conflicts between ADS and vehicle embedded active safety systems
This is particularly valuable for identifying edge cases or latent faults not previously captured in type approval testing.
The ADS Requested Gear is valuable for:
- Identifying critical gear selection errors: Analysing gear requests can help detect potentially dangerous situations where the ADS selects an inappropriate gear, such as shifting into reverse while moving forward or engaging drive while in reverse.
- Detecting transmission system malfunctions: Inconsistencies between gear requests and actual gear engagement could indicate critical failures in the transmission system, potentially leading to loss of vehicle control.
- Evaluating hill-start safety: Analyzing gear requests during uphill starts can assess the ADS's ability to prevent rollback and maintain vehicle stability in challenging terrain.
- Investigating sudden acceleration incidents: Gear request data can help determine if unexpected vehicle acceleration is due to ADS errors in gear selection or other system malfunctions.
- Assessing traction control in adverse conditions: Examining gear selection patterns in low-traction scenarios can evaluate the ADS's ability to maintain vehicle stability and prevent skidding or loss of control.

## Slide 7
Vehicle indicated service braking
This data element records the moment the vehicle’s service braking system - regardless of the ADS capabilities (i.e. ABS/ESC) and where the ADS control is assessed - is confirmed as actively engaged. It reflects the status of the service brake either being applied or not applied.
It serves as a confirmation that the brake actuation following a brake request has indeed been achieved by the physical braking system.
There are systems onboard the vehicle which will modulate the braking demand that is applied (such as ABS/ESC), and it is currently uncertain whether they will be incorporated into the ADS control or remain as separate systems modulating the braking demand. Having this data element allows us to deduce whether there is a fault with the ADS control, or a fault with (a part of) the braking system itself.
If this data element was not recorded, we therefore have to address:
How we determine whether there is a fault of the ADS requesting the braking system or a fault with the braking system itself?
Where the ESC be implemented in these systems. Will it be part of the ADS or as a separate system?

## Slide 8: Recording data post occurrence
It is important to record data after a safety critical occurrence has happened because data collection post-event​ gives us:
1. The full incident sequence, including impact and the vehicle resting state​
2. The operational actions of the vehicle operator(s) after the crash​, did the vehicle behave appropriately and come to a safe stop or carry on driving? Did it choose an appropriate MRC?
3. A way of corroborating the contributions of other stakeholders to the post-collision event
3s
No data recorded after this point
Notes: So in this example which is a real-life example which has been investigated by TRL, we have an ADS who has collided with the central reservation and as soon as this collision happens the DSSAD stops recording but it carried on driving along the central barrier for another 3 seconds before it finally comes away. Clearly the ADS has exhibited dangerous driving but crashing into the central reservation in the first place but then it has continued the dangerous driving by driving along the central reservation for a further 3 seconds. If we don’t have any data recorded after the initial collision we don’t have any data on why the ADS kept on driving along the reservation, and what made it suddenly come away from the central reservation at the time that it did, whether it came away from the central reservation in a safe manner. All of these things will affect the safety of other road users and whilst we do we to know whether the ADS took the correct steps to try and avoid the collision it’s also very important to assess if it behaves in a safe manner after a collision has occurred to minimise as much harm as possible.

## Slide 9: Authorised entities
Proposal – add paragraph 5.1:
5.1 The stored data defined in paragraph 6 shall be readily accessible to [the approval authority and] authorised entities for the vehicles in their territory of deployment. The authorised entities and the extent necessary shall be defined by the applicable laws of the territory of deployment.