## Slide 1
Review of the cryogenic vessel design standard
1. ISO 21029-1_2018
- The brand-new international design code for cryogenic vessel.
- In clause 10.1, two primary paths for verifying the design of a pressure vessel
  Option 1: design by calculation – Clause 10.1.2
  └ “Fatigue life calculation shall be conducted according to EN 13445-3, ASME VIII-2
  or equivalent standards/codes”
  Option 2: design by experimental method – Clause 10.4
2. ASME VIII-2
- Part 5. Design by analysis requirement
- Liquid hydrogen tanks operate under cyclic pressure loading; therefore, their design shall be performed in accordance with the procedures stipulated in Section 5.5.3, 5.5.4, or 5.5.5.
  Section 5.5.3: Fatigue Assessment — Elastic Stress Analysis and Equivalent Stresses
  Define Load History: Define the loading conditions for all anticipated operating cycles over the entire design life of the vessel.
  Cycle Counting: Identify and count the stress-strain cycles from the defined load history (e.g., using the Rainflow method as per Annex 5-B.4).
  Stress Range Calculation: For each cycle, calculate the range of the six stress components (the stress tensor).
  iv. Calculate Effective Alternating Equivalent Stress Amplitude (S_alt,k): As shown in Equation (5.30), the effective stress amplitude is calculated by applying factors such as the fatigue strength reduction factor (K_f) and the plasticity correction factor (K_e,k) to the calculated stress range. This is a sophisticated calculation method that goes beyond simple stress comparison by accounting for the geometric effects of welds and local plastic deformation.
  Equation (5.30)
  Determine Permissible Number of Cycles (N_k): Using the calculated S_alt,k value, determine the permissible number of cycles (N_k) from the material's Fatigue Design Curve (Annex 3-F). → This is a potential point where KHK could counter our argument. The anticipated counter-argument is that "a valid fatigue design curve does not exist for cryogenic hydrogen environments."
  Cumulative Damage Assessment: Using Miner's Rule, calculate the cumulative fatigue damage for all cycles and demonstrate that this value is less than or equal to 1.0.
Same level of design verification

## Slide 2
Review of the cryogenic vessel design codes
  Section 5.5.4: Elastic-Plastic Stress Analysis
  - It involves modeling the material's actual plastic behavior with a stress-strain curve to directly calculate the effective strain range for each cycle, which is then used to evaluate fatigue life. This method also provides detailed procedures and formulas.
  - If the tank manufacturer possesses the necessary cryogenic material property data, this method can be utilized for a more effective design. The cryogenic properties of the material would be discussed in detail during Phase 3.
  Section 5.5.5: Fatigue Assessment of Welds
  - This specialized method for weld fatigue assessment calculates fatigue life based on the 'Structural Stress' parameter, a value derived from the weld's geometry and stress distribution.
3. Conclusion
- As established above, the methodology for designing a vessel's durability through calculation is well-defined in existing standards. We propose to discuss a more specified approach during Phase 3. However, mandating cryogenic testing at this stage is infeasible due to current developmental constraints. Therefore, for the recent time, it would better to referencing the existing GTR No. 13. Subsequently, once concrete test data and the necessary testing infrastructure are secured, a comparative analysis between the design-by-test and design-by-calculation approaches will be required.