## Slide 1: Proposal„Euclidean“ and predicted TTC

## Slide 2: Calculation Eucl. TTC
Ego
Vlat|ego
Vlon|IV
vego
IV
Shortest Distance (SD)
Vlon|ego
Vlat|IV
vIV
VSD|IV
VSD|ego

## Slide 3: Calculation Crossing Routes
Ego
Route prediction along velocity vectors
IV

## Slide 4: Definitions
"Time-to-Collision (TTC) trigger” means longitudinal and lateral calculation of the Time-to-Collision (TTC), which is the relative Euclidean distance divided by the relative Euclidean velocity between the vehicle and the safety relevant object, calculated based on the fused sensor data. TTC is calculated in cases the current trajectories of the ADS and the object along their current routes are crossing.

## Slide 5: Data Elements
The data elements shall be recorded [in compliance with paragraph 6.3.1] if the following thresholds are reached or conditions occur:
a) Detected collision
b) EDR trigger input (excluding last stop trigger)
(c) TTC trigger threshold of 0.2s, where the speed of the vehicle is 10kph or more.
(c) A trigger chosen by the manufacturers resulting in recording of data in all situations featuring a similar level of collision risk to the situation where TTC trigger threshold of 0.2s is reached. In such cases, the similar triggering performance shall be documented in the ADS safety case.

## Slide 6: Data Storage and Security
3.1.1. However, as regards times series data recorded following the trigger referred to in point 6.3.2. (c), the data storage system shall be sufficient to store the data corresponding to 5 occurrences. The recorded data shall be overwritten by the current occurrence data, on a first-in first-out basis.