## Slide 1
GTB Task Force “Glare Control”
The glare phenomenon, its causes and relevance ranking of glare events
2025-12-09
- GTB/TF-GC -
TFGP-05-06

## Slide 2
To better understand the glare phenomenon during night-time driving, the GTB Task Force «Glare Control» examined the results of a lot of studies and researches conducted in the time period from 1996 to the current year in different countries, trying to better identify these reasons.
The activity resulted in a preliminary classification of glare type, in relation to their potential reason.
…more on that later. First, some questions.

## Slide 3
GLARE (as we intend it)
Excessive amount of light directed into the eyes of drivers of oncoming vehicles or, through the rear-view mirrors, preceding vehicles

## Slide 4
ILLUMINATION
Emitting light into the traffic area in such a way as to allow the driver:
to see the road ahead of the vehicle
to recognize obstacles on the road and in its immediate vicinity
detect an obstacle with sufficient time to stop the vehicle / to avoid collision

## Slide 5
How much light is "too much"?
This amount of light (“too much”) can only be determined as an average, due to the wide range of a driver’s visual performance.
The perception of both illumination and glare depends on the individual driver’s visual performance (e.g. adaptation capability of the eye) and to ambient conditions.
In other words: there will always be someone who will feel dazzled.
At what level does the amount of light become "excessive"?

## Slide 6
More importantly:
Glare is a phenomenon that
cannot be totally eliminated.
Target is to mitigate a significant amount of strong glare events.

## Slide 7
VISIBILITY
ROAD ILLUMINATION
GLARE
(discomfort & disability)

## Slide 8
Glare Relevance Level is depending on:
Intensity I (glare illuminance level at driver‘s eye)
Exposure time E (length of glare peak)
Occurance frequency F (how often the glare event takes place)
1
2
3
Glare Relevance Level = Intensity x Exposure Time x Occurance Frequency

## Slide 9
Glare Relevance Level = Intensity x Exposure Time x Occurance Frequency
Basis for future proposal of effective countermeasures for glare reduction
Ranking of glare effects: (see table in doc TFGP-05-07) Red (very high), Orange (high), Yellow (mid), Green (low)

## Slide 10
FUTURE inputs from GTB
First ideas for countermeasures to glare events
Quantification of the effectiveness of proposed countermeasures.