## Slide 1: HWT “Literature” Status Report
GRE/TF-GP 5th session
9 December 2025
TFGP-05-09

## Slide 2
Status of the activity so far
The HWT held a total of 5 meetings in 2025, and examined the following literature material during :
#13 Nighttime Traffic Glare Analysis by Measurements and new Statistical Evaluations (ADAC, March 2025)
#16 Glare from Headlamps on Wet Roads and the Potential to Increase Road Safety (ADAC, March 2025)
#19 How glare is regulated and should be regulated in UN ECE Regulations (ADAC, March 2025)
Ref.08 The Persistence of Headlight Glare as a Problem for the Driving Public
Ref.09 Why is Headlight Glare Such a Persistent Problem for the Driving Public? A Review
Ref.10 Headlamp Glare Complaints: Why are they rising?
Ref.28 Recommendations for Dimming Headlamps through AFS
Ref.29 Glare from vehicle headlights in night-time traffic
Ref.30 New Studies about the Influence of Small Light Emitting Areas on Headlamp Glare
Ref.31 Field Study: Discomfort Glare of Headlamps with Small Light Emitting Areas
Ref.32 Requirements and evaluation methods for adaptive glare-free low beam headlights on reflective road surfaces
Ref.33 CITA Recommendation n25 Headlamp Alignment Testing in Vehicle Inspection
Ref.35 Headlight glare in police-reported crash data: prevalence, contributing factors, and potential effects
Ref.36 Glare from Vehicle Lighting on UK roads (Latest study from UK, 2025)
Outcome of the examination (next page)

## Slide 3
Preliminary outcome of the examination
Illuminance and Contrast Reduction: Glare is fundamentally understood as the reduction of contrast due to scattered light (disability glare), and the glare illuminance on the eye is the most important parameter. High illuminance levels are identified as the key cause of strong glare.
Aiming and Vehicle Dynamics: The failure to maintain correct headlamp aiming, especially due to vehicle pitch and roll movements in dynamic traffic, is repeatedly mentioned as a primary mechanism by which excessive glare reaches oncoming drivers.
Light Source Characteristics (Colour/Wavelength): The shift toward bluer/shorter-wavelength light (associated with gas discharge and certain LED systems) is linked to an increase in psychological or discomfort glare.
Age and Sensitivity: The increased sensitivity of older drivers and their prolonged readaptation time following exposure to glare is a critical and recurring human factor.
Regulatory Gaps and Real-World Conditions: current photometrical standards and type approval regulations are insufficient because they do not account for the wide range of real-world driving conditions, road geometry, or dynamic vehicle movements.
Adaptive Lighting Technology: Adaptive lighting systems (such as Adaptive Driving Beam (ADB) or dynamic masking) are evaluated as the primary technological solution to mitigate glare in challenging conditions, especially on wet roads or curves.

## Slide 4
Additional observations
Cut-off definition: the definition of cut-off should be improved to improve its assessment during PTI.
The “Purkinje effect”: the tendency of the human eye’s peak sensitivity to shift toward the blue-green part of the spectrum as light levels decrease, making reds appear darker and blues/greens relatively brighter at dusk or in dim light.
  In bright light (photopic vision), the eye is most sensitive to wavelengths around 555 nm (greenish‑yellow).
  In dim light (scotopic vision), the sensitivity peaks around 507 nm (blue‑green).
  During the transition (mesopic vision), both rods and cones contribute, causing a shift in perceived brightness toward shorter wavelengths.
    In practice: Because of this phenomenon, LED headlights are perceived as 20% brighter than xenon headlights with similar light parameters.
Discomfort glare should not be neglected: especially at night during long drive, constant discomfort may generate tiredness. Tiredness affects the psychological and physiological state of the driver, including how light is perceived.

## Slide 5
Investigation points
Modern technologies: Some studies were not made on LED, so it could be interesting to perform the same studies using modern technology.
How much light is too much?
How much light is needed for safety?

## Slide 6
Next Steps
Merging of the inputs from the HWT Literature with those coming from GTB
Identification of aspects:
  covered by the literature
  where further research is needed
concrete actions to mitigate glare
“who does it?”

## Slide 7
🗓️ Timeline
2025 | 
ADAC material examination | 26 September 2025
2nd HWT meeting on ADAC material | 2 October 2025
Examination of docs Ref.08, 09, 10, 28 29 | October 2025
3rd HWT meeting | 3 October 2025
4th HWT meeting | 28 October 2025
Examination of docs Ref. 30,31 and 32 + new UK study on glare (if available) | November 2025
5th HWT meeting | 28 November 2025
Submission of 2nd status report to TF-GP | 5th December 2025
2026 | 
Merging HWT Literature summaries | Beginning of January 2026
6th HWT meeting to identify known factors + areas for further research + concrete actions to mitigate glare + “who does it?” | Middle January 2026
Submission of final status report to TF-GP | End of January 2026