II. TEXT OF REGULATION

[1.	Scope and Purpose

This regulation specifies safety-related performance of electrically propelled road vehicles and their rechargeable energy storage systems.  The purpose of this regulation is to avoid human harm that may occur from the electric power train.

[2.	Application

This regulation applies to all road vehicles (excluding category 3) with a maximum design speed exceeding 25 km/h, equipped with electric power train containing high voltage bus, excluding vehicles permanently connected to the grid.

[Individual Contracting Party may elect to adopt the requirements of:

- Part 1 (light vehicles) of this GTR or

- Part 1 (light vehicles) and Part 2 (heavy vehicles) of this GTR. ]

Part 1 applies to all vehicles of Category 1-1; Category 1-2 vehicles with a Gross Vehicle Mass of up to 4,500/4536 kg; and Category 2 vehicles with a Gross Vehicle Mass of up to 4,500/4536 kg..

In addition, the following vehicles are excluded:

(a) 	A vehicle with four or more wheels whose unladen mass is not more than 350 kg, not including the mass of traction batteries, whose maximum design speed is not more than 45 km/h, and whose engine cylinder capacity and maximum continuous rated power in the case of hybrid electric vehicles do not exceed 50 cm3 for spark (positive) ignition engines and 4 kW for electric motors respectively; or whose maximum continuous rated power in the case of battery electric vehicles does not exceed 4 kW ;

and

(b) 	A vehicle with four or more wheels, other than that classified under a) above, whose unladen mass is not more than 450 kg (or 650kg for vehicles intended for carrying goods), not including the mass of traction batteries and whose maximum continuous rated power does not exceed 15 kW.

Part 2 applies to all vehicles of Category 1-2 vehicles with a Gross Vehicle Mass exceeding 4,500/4536 kg or any other applicable lower mass; and Category 2 vehicles with a Gross Vehicle Mass exceeding 4,500/4536 kg or any other applicable lower mass.

[3.	Definitions

For the purpose of this Regulation the following definitions apply:

# Footnotes

A Contracting Party may restrict domestic implementation of the GTR to a lower vehicle mass limit depending on the vehicle classification systems used in the domestic legislation.

Idem.as footnote 1

Depending on the vehicle classification system used in the domestic legislation

Idem as footnote 3

# Text boxes

EVS-11-28e