## Slide 1
Tyre Abrasion C3 tyres
TFTA 39th session, 4 and 5 December 2025
TA-39-xx

## Slide 2: Status C3 tyre abrasion investigations
ETRTO defined test concept and draft clusters for C3 tyre testing
ETRTO focused its studies on one circuit for truck/trailer 22.5 tyres for road usage, coherent with European usage of these sizes, which represent about ~65% of volume and ~82% of “tons to wear” put each year on the market.
A first set of tests on 22.5” road usage (@ cold/hot temperatures, 45+30 kKm) just finished and Temperature sensitivity assessment to be made
Tyre market distribution (tyres sizes, vehicle architecture and usage) confirmed a high complexity to be further studied.
Next steps:
  Candidate reference tyre performances assessment on the truck- trailer axles,
  Confirmation or modification of reference tyre strategy,
  Assessment/Confirmation/Technical definition of all possible clusters,
  Test method definition of all existing segments (on/off, urban, 17.5”, 19.5”)
  Research of alternative solutions for C3 tyres abrasion mitigation.

## Slide 3
ETRTO ongoing work on C3 test method “feasibility” development has raised the following points:
• Complexity to study all C3 tyre usage applications
• Starting reflection on alternative methodology
• Need to spread the C3 research cost over a longer time
   According to the current state of knowledge, at least 1 year more for the UN test method feasibility study and parameter testing (GRBP Feb 2027 GRBP Feb 2028)
ETRTO also reflected on the most realistic way to proceed for the C3 Market Assessment: Monitoring approach
This will require the:
• Need to wait on the laboratory accreditation
• Need to prepare the monitoring governance
• To perform sufficient test to collect relevant data
• Post processing requires the right governance and sufficient time
   According to the current state of knowledge, at least 1 year more for the UN state-of-the-art assessment (monitoring) to fix the limit settings (GRBP Sept 2029  GRBP Sept 2031)
Status C3 tyre abrasion investigations
Based on the above industry initial estimation of the need for revising the UN workplan, Tyre Industry recommends considering at least 2 years postponement of corresponding (C3) deadlines in TFTA ToR and Euro7 regulation.

## Slide 4: C3 Test method Gantt (best case scenario)
C3 Test method adoption in GRBP February 2028

## Slide 5: C3 Market assessment (Monitoring) Gantt
C3 Test limits settings adoption in GRBP not before September 2031

## Slide 6: Thank you

## Slide 7: C3 tyres: abrasion rate index vehicle test concept (draft)
Concept similar, but with a lot of differences to C1 tyres vehicle test method
Convoy of up to 4 vehicles with reference tyres
Vehicles:
  For 22.5’ “big” tyres: tractor + semi-trailer, loaded 36T (6.5 front +10 drive +19.5 trailer)
  For smaller tyres: rigid trucks 2 axles, load conditions to be defined.
Test per axle :
  FRT tyres on trailer axles, compared to reference tyres on trailer axles
  Traction tyres on drive axle(s), compared to reference tyres on drive axle(s)
  Other tyres on front axle, compared to reference tyres on front axle.
Controlled driving condition representative of market driving conditions
  Acceleration standard deviation : X: ~0.3 m/s2, Y ~0.4 m/s2 (mix regional/long haul application)
  Road distribution: 60% motorway, 40% regional roads,
  Circuits to be defined
  Total test distance to be defined.
Test conditions and segregation method to be defined for tyre clusters.
Reference tyres: candidate available to be confirmed
Note : document TA-31-5

## Slide 8: Draft layout and loading for test conditions
Note : document TA-31-5
Tyre sizes | Acceleration | FRT on trailers | TRACTION on drive | OTHERS on front | SRTT
19.5” 17.5” | StdX 0.35/0.55 m/s2 StdY 0.45/0.6 m/s2 |  | Rigid vehicle (without trailer) Dual fitment [90]% of dual LI, capped 11.5T | Rigid vehicle (without trailer) Single fitment [90]% of single LI, capped 7.5T | 245/70R19.5
275/70R22.5 (Urban) | StdX 0.6 m/s2 StdY 0.25 m/s2 |  | Rigid truck or bus | Rigid truck or bus | 245/70R19.5 ?
Dual tyres 22.5” > 275/70 19.5” FRT 17.5” FRT | StdX 0.3 m/s2 StdY 0.4 m/s2 | 3 axles semi-trailers Tyres in dual fitment 6.5 T per axle (LID>125) [90]% of Z(LID) (LID<125) | Tractor on drive with semi-trailer 19.5T Dual fitment 10T per axle | Tractor on front with semi-trailer 10T Single fitment 6.5T per axle | 315/70R22.5
Single Tyres |  | 3 axles semi-trailers Tyres in single fitment 6.5 T per axle (LID>=152) [90]% of Z(LID) (LID<152) | Tractor on drive with semi-trailer 19.5T Single fitment 10T per axle | Tractor on front with semi-trailer 19.5T Single fitment 6.5T per axle | 315/70R22.5
On/Off tyres | StdX 0.4 m/s2 StdY 0.55 m/s2 | ? | Rigid truck 6*4 | Rigid trucks 6*4 | 315/70R22.5
16, 19, 20, 24, 24.5” |  | Not in the scope, as representing less than 1.5% of the market |  |  | 
“Few” tyre C2 like |  |  |  |  |