## Slide 1: Abrasion methods equivalence - EC-JRC proposal of 14 November – ETRTO analysis and Considerations
TFTA 39th session 4 and 5 December 2025

## Slide 2: Background
During the last GRBP session, a revision of the Terms of Reference (GRBP-82-34-Rev1) was agreed including the statement “…to secure inclusion of both the vehicle test method on public roads and the indoor drum test method…” at the upcoming GRBP meeting (February 2026).
This decision called for a deep technical analysis of the available data (GRBP 83rd session in February 2026) and a joint workplan aimed at reducing uncertainty in both methods and improving correlation by GRBP 84th session in September 2026.
The following activities were triggered by last GRBP (updated TFTA ToR, GRBP-82-34rev1) by creating a Subgroup on Data Assessment and Test Methods Improvement:
  Technical work to understand the correlation differences between COVA and MA and check the equivalence of both methods.
  Further data assessment to support the workplan definition for test methods improvement.
The EC-JRC Proposal on Test Method Equivalence Criteria doesn’t seem directly descending from last GRBP data analysis
  The European Commission (EC) stated the need for complementary work to define criteria in the UN Regulation for demonstrating equivalence between the two methods. This requirement is intended to provide sufficient political confidence.
  EC and JRC have prepared a proposal for equivalence criteria to be included in the UN Regulation.

## Slide 3: 1. EC-JRC proposal for correlation criteria
ETRTO acknowledges the intent behind the European Commission’s proposal and appreciated having been consulted in advance 2 weeks ago on the proposal.
ETRTO proceeded with an in-depth analysis considering the following aspects of the JRC/EC proposal:
Exact purpose
Technical feasibility
Regulatory impact
Need of a correlation criteria in the UN Regulation
More details in next slides.

## Slide 4: 1. EC-JRC proposal - Regulatory impact (1/2)
0. Still unclear what are the technical elements triggering the need of the EC-JRC proposal  JRC technical analysis missing
1. Concept
This proposal is completely new and seems to go against the principles of the 1958 agreement (Schedule 2, Part 2, For Category A activities: any laboratory that is ISO 17025 accredited and designated by a TAA of a CP can run type approval tests and the results are mutually recognized by all the other CPs).
The equivalence requirements for each lab are an additional obligation in the UN Regulation and could invalidate test centers currently meeting existing requirements.
Verification “once and for all” is made for other regulatory performance:
  why this should be different for Abrasion?
2. Equivalence and Verification
What does it mean “all [open public road] circuits that were included in the latest exercise [shall] participate?”:
  shouldn’t be the criteria for participation based on the competences and ISO17025 accreditation?
  Do we know whether the circuits of the latest exercise are ISO17025 accredited and, if accreditable, under which conditions?
Does this proposal give circuits joining UN TFTA test campaigns a competitive advantage?
3. ISO 17025 and Interlaboratory Comparison
Interlaboratory comparison (or proficiency testing) is already in place under ISO 17025, even if managed by individual accreditation bodies.
  Is this proposal necessary?

## Slide 5: 1. EC-JRC proposal - Regulatory impact (2/2)
4. Monitoring and Reference Tyres
The monitor tyres are intended to act as SRTT in all respects, but they are not SRTTs.
  How will performance be monitored and checked?
  How can consistency of tyres be guaranteed?
  Who will store and supply these tyres?
5. Harmonization and Mutual Recognition
Requiring proof of equivalence with specific laboratories or using specific test methods for Tyre Abrasion introduces a new constraint when other countries will implement Tyre Abrasion regulations
  is this scheme acceptable from the perspective of harmonization of standards and mutual recognition under the 1958 Agreement?
Implementing the criteria should be done across contracting parties to the 1958 Agreement:
  How to take into consideration the timing for conducting the evaluation & accreditation given the early date prescribed for mandatory homologation?
6. Legal consequences and Missing Legal provisions to manage transition of alignment, with unclear regulatory area How to handle in case of a tyre approved for abrasion but not passing anymore the limit in case of a new alignment? How to handle results obtained from an approved lab that failed to miss criteria for the following exercise? How will be considered results obtained for type approval or COP around the alignment campaign?
7. Governance, cost and burdens
What will be the governance structure to address this new concept of defining equivalence?
Has any cost assessment been made?

## Slide 6: 1. EC-JRC proposal - Technical questions
Existing Technical Requirements
Current technical requirements based on SRTT are sufficient (SRTT tested at 3 temperature where SRTT Abrasion level shall be in a certain limit + permanent monitoring).
The suitability of circuits and drums is continuously monitored during testing through the abrasiveness level of the SRTT.
Therefore, the proposal introduces unnecessary burdens.
2. Monitor Tyres
As the baseline can vary depending on the selection of monitor tyres also the validity of a new circuit or drum can vary depending on the selection of the monitor tyres
3. Reference Circuits
Repeatability and inter-laboratory variation among the four reference laboratories would require stricter specifications than those applied to other laboratories.
What happens if a circuit within the reference network drifts?
How can such drift be detected?

## Slide 7: 2. ETRTO and JASIC experts are focus on the work agreed in GRBP 82nd session that shall remain the short term priority (TA-38-2):
Re-assess the available data in depth to secure the adoption of both test methods in February 2026
To identify the parameters to improve the test methods and alignment of the drum test
To prepare a workplan to assess the test methods improvement (reproducibility and correlation) aimed at preparing a working document for adoption in September 2026
From subgroup preliminary analysis it results that there is a physical correlation between the two methods that is hidden by single methods variability, these could be reduced by working on factors such as the reference and candidate vehicle effects.
 Similar in-depth analysis shall be conducted on the drum method.

## Slide 8: 3. Conclusions
ETRTO believes that before any intention of introducing an additional prescription in the UNR on test methods equivalence criteria the outcome of the data assessment and workplan definition need to be considered.
The technical elements triggering the need of the JRC/EC proposal need to be clarified.
The approach to introduce additional requirements on the equivalence of test laboratories and test methods has raised several technical and regulatory questions to be tackled.
Current UNR already addresses technical requirements on the SRTT abrasiveness that is the alignment condition between test laboratories.
ETRTO believes that proposed equivalence provision proposed by JRC/EC is very complex, expensive and that the governance structure is missing.

## Slide 9: Thank you!