## Slide 1
Japan’s proposal for EPPR-11-15e-Rev.1
7/Oct/ 2016
JAPAN AUTOMOBILE STANDARDS INTERNATIONALIZATION CENTER
http://www.jasic.org

## Slide 2
Japan’s proposals
NO | 11-15e Rev.1 | Japan proposal | Justification
3.1 | Vehicle sub-classification. Class1. Vehicles that fulfil the following specifications belong to class 1: | 3.1.1. Vehicle sub-classification. Class0. Vehicles that fulfil the following specifications belong to class0: 3.1.2. Vehicle sub-classification. Class1. Vehicles that fulfil the following specifications belong to class 1: | Define "Class 0". Need to add Category 3-1 vehicle to the classification of WMTC Class 0. The test methods for Category 3-1 vehicles differs depending on their engine capacity and vmax. Class1 classification inline with GTR2.
Engine capacity<150cm3 and vmax<100km/h | Class1
Engine capacity≦50cm3 and vmax≦25km/h | Class0-1
Engine capacity≦50cm3 and 25km/h<vmax≦50km/h | Class0-2
50cm3<engine capacity<150cm3 and vmax≦50km/h or engine capacity<150cm3 and 50km/h<vmax<100km/h | Class1

## Slide 3
Japan’s proposals
NO | 11-15e Rev.1 | Japan proposal | Justification
5.2 | General requirements. Vehicles with a maximum design vehicle speed ≤ 25 km/h or ≤ 45 km/h or with a maximum net or continuous rated power ≤ 4 kW shall meet all the relevant requirements of this GTR applying to vehicles with a maximum vehicle design speed of > 25 km/h or maximum net or continuous rated power > 4 kW. Annex B.5.15. includes test cycles dedicated for such vehicles with a low maximum vehicle design speed or low maximum power. | Delete the whole paragraph 5.2. | No need to describe "classification" in "general requirements". Move the definition of Category 3-1 vehicle to 3.1.1.

## Slide 4
Japan’s proposals
NO | 11-15e Rev.1 | Japan proposal | Justification
7 8 | General requirements applicable for manufacturers requesting type-approval.. | Delete the whole paragraph 7 and paragraph 8. | Type approval is not needed in GTR.
9.1 | Performance requirements for the type1 test of a two-wheeled motorcycle. For low displacement motorcycle. | Delete the whole paragraph 9.1. -After the decision of the emission limit, combine the sentence in 9.2. | No need to describe each emission limit of Category 3-1 vehicle here.
9.2 | The principal performance requirements for a two-wheeled motorcycle | Fill in the emission limits later. | The emission limits of each CP are under consideration. So revise the description of emission limits after making decisions about each emission limit.