## Slide 1: Study on Drive Trace Index of Electrified Vehicles
Prepared by JAPAN
10 JAN 2017
WLTP 17th IWG

## Slide 2
BACKGROUND
 | Normalization | Drive Index
ICE | study by EC  SOC correction was adopted | study by Japan  Require to submit each index value of each test
NOVC-HEV | study by Japan  Normalization doesn’t work for some of performance parameter. | study by Japan  Report during 17th IWG
OVC-HEV |  | 
PEV |  | 
WLTP IWG Decision | Premature to adopt “Normalization” except SOC correction | TBD
Overview of previous study
Today’s Topics

## Slide 3
SUMMARY_1
It is observed that some of Drive Trace Indexes are able to detect the smooth/rough driving technique of electrified vehicles.
Test results have macro correlation with Drive Trace Indexes, however, it is difficult to normalize by using the drive indexes from the view points of accuracy and practical lab. operation

## Slide 4
SUMMARY_2 (candidate indexes)
Vehicle category | ICE | NOVC-HEV OVC-HEV(CS) | OVC-HEV(CD) |  |  |  | PEV | 
parameter | CO2 |  |  | EC | EAER | RCDA AER | EC | PER
ER | × |  | 〇 |  | 〇 | × | 〇 | 
DR |  |  | × |  | × |  | × | 
EER |  |  | 〇 |  | 〇 |  | 〇 | 
ASCR | 〇 |  |  |  |  |  |  | 
IWR |  |  |  |  |  |  |  | 
RMSSE |  |  |  |  |  | 〇 |  | 

## Slide 5
NEXT ACTIONS
Initial Proposal
candidate index
Threshold
(by Japan)
18th 19th 20th 21st
2017/Jan Mar Jun Oct 2018/Jan
Feedbacks
Comments
Counter-proposals
(by WLTP IWG member)
Final Decision
Consolidated Proposal
candidate index
Threshold
(by Japan)

## Slide 6: Appendix
6

## Slide 7: Drive Trace Indexes (SAE J2951)
7
7
Energy Rating (ER)
  is defined as the percent difference between the total driven and target cycle energy.
Distance Rating (DR)
  is defined as the percent difference between the total driven and scheduled distance.
Energy Economy Rating (EER)
  is defined as the percentage difference between the distance per unit cycle energy for the driven and target traces. Since fuel economy is a measure of the distance traveled per unit of fuel consumed, the effect of distance driven must also be considered in an assessment of a drive quality that is intended to correlate with fuel economy.
Absolute Speed Change Rating (ASCR)
  is defined as the percentage difference between the ASC for the driven and target traces. It provides an indicator of the "smoothness" of the driven trace relative to the scheduled trace. A driven trace that is "smoother" will have a lower ASC than the scheduled trace and so will result in a negative ASCR.
Inertial Work Rating (IWR)
  is defined as the percentage difference between the inertial work for the driven and target traces. It can indicate when the drive style might substantially impact the overall efficiency of the engine, such that a metric based strictly on cycle energy might not fully characterize observed deviations from expected emission rates.
Root Mean Squared Speed Error (RMSSE)
  provides the driver’s performance in meeting the schedule speed trace throughout the test cycle in terms of the Root Mean Squared Speed Error. The value is always a positive number with lower values (closer to zero) indicating better performance. RMSSE has units of kilometer per hour (km/h) in this study.

## Slide 8: Overview of Test
8
8
The study of the driving trace index of Electrified vehicles
  Purpose: Check the influence of driving style and Consider the appropriate criteria
  Test vehicles： 1 EV and 1 OVC-HEV
  Test cycle: WLTC 4-phase
  Driving style:
    Normal (trace target speed as much as possible)
    Smooth (Smooth acceleration and Smooth deceleration)
    Rough (Aggressive acceleration, Rough behavior and High deceleration)
Low acceleration
High deceleration
Fluctuate
High acceleration
Low deceleration
Smooth driving
Rough driving
Smooth
(note) All test are within drive trace tolerance

## Slide 9: Test sequence for OVC-HEVs CD～CS Test
9
9
day 1
day 2 （Normal）
CD test
Soak
CS
Charge
Charge
day 3~ （Smooth/Rough）
CD test
Soak
CS
Charge
Pre-con.
Charging

## Slide 10: Test sequence for EVs
10
PERest is the estimated pure electric range of the considered PEV, km
dDS1 is the length of dynamic segment 1, km
dDS2 is the length of dynamic segment 2, km
dCSSE is the length of constant speed segment CSSE, km
apply Shortened test procedure

## Slide 11: Vehicle specification
11
11
OVC-HEV (4WD)
EV

## Slide 12
12
12
Test results of OVC-HEVs

## Slide 13: Number of driving cycles under CD condition
13
13
# of CD cycles did not change when driving style was changed on test vehicle.
（CD-4 = confirmation cycle）

## Slide 14: Drive Trace Indexes
14
14
Energy Rating [ER]
Distance Rating [DR]
Energy Economy Rating [EER]
Absolute Speed Change Rating [ASCR]
Root Mean Squared Speed Error [RMSSE]
Inertia Work Rating [IWR]
Drive trace indexes are varied according to driving style.

## Slide 15: Influence on CO2
15
15
Compared to Average CO2 of Normal driving
ER
DR
EER
ASCR
RMSSE
IWR
CO2 has variability up to 20 g/km according to driving style.
Smooth <- -> Rough
Smooth <- -> Rough
Smooth <- -> Rough
Smooth <- -> Rough
Smooth
Rough
0.8
-2
+4
Approx. 20 g/km

## Slide 16: The utility factor-weighted charge-depleting CO2
16
16
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
ER
DR
EER
ASCR
RMSSE
IWR
MCO2,CD has variability up to 10 g/km according to driving style.
Approx. 10 g/km
0.8
-2
+4

## Slide 17: The utility factor-weighted mass emission of CO2
17
17
[Average of CD 1-4&CS]
[Average of CD 1-4&CS]
[Average of CD 1-4&CS]
[Average of CD 1-4&CS]
[Average of CD 1-4&CS]
[Average of CD 1-4&CS]
ER
DR
EER
ASCR
RMSSE
IWR
MCO2,weighted were changed approx. 10 g/km according to driving style.
Approx. 10 g/km
0.8
-2
+4

## Slide 18: All-electric range (AER)
18
18
ER
DR
EER
ASCR
RMSSE
IWR
AER were changed approx. 16 km according to driving style.
Large reduction was observed when rough driving was operated.
AER of Smooth driving and Normal driving were almost same.
Approx. 16 km
0.8
-2
+4

## Slide 19: Engine start timing in 1st cycle (AER)
19
19
Normal-1
Normal-2
Normal-3
Smooth-1
Smooth-2
Rough-1
Rough-2

## Slide 20: Equivalent all-electric range (EAER)
20
20
ER
DR
EER
ASCR
RMSSE
IWR
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
Approx. 5 km
EAER has variability up to 5km according to driving style.
0.8
-2
+4

## Slide 21: The actual charge-depleting range (RCDA)
21
21
ER
DR
EER
ASCR
RMSSE
IWR
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
Approx. 2 km
RCDA has variability up to 2 km according to driving style.
Hard to detect driving style
0.8
-2
+4

## Slide 22: The charge-depleting cycle range (RCDC)
22
22
ER
DR
EER
ASCR
RMSSE
IWR
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
RCDC were not changed.
0.8
-2
+4

## Slide 23: The electric energy consumption of the applicable WLTP test cycle based on the recharged electric energy from the mains and the equivalent all-electric range (EC)
23
23
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
ER
DR
EER
ASCR
RMSSE
IWR
Approx. 20 Wh/km
EC has variability up to 20 Wh/km according to driving style.
0.8
-2
+4

## Slide 24: The utility factor-weighted charge-depleting electric energy consumption based on the recharged electric energy from the mains (ECAC,CD)
24
24
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
[Average of CD 1-4]
ER
DR
EER
ASCR
RMSSE
IWR
Approx. 10 Wh/km
ECAC,CD has variability up to 10 Wh/km according to driving style.
0.8
-2
+4

## Slide 25: The utility factor-weighted electric energy consumption(ECAC,weighted)
25
25
[Average of CD 1-4]
ER
DR
EER
ASCR
RMSSE
IWR
[Average of CD 1-4&CS]
[Average of CD 1-4&CS]
[Average of CD 1-4&CS]
[Average of CD 1-4&CS]
[Average of CD 1-4&CS]
[Average of CD 1-4&CS]
Approx. 6 Wh/km
ECAC,weighted has variability up to 6 Wh/km according to driving style.
0.8
-2
+4

## Slide 26: Comparison of vehicles on CO2_CS
26
26
5 g/km
4 g/km

## Slide 27
27
27
Test results of PEV

## Slide 28: Drive Trace Index
28
28
Energy Rating [ER]
Distance Rating [DR]
Energy Economy Rating [EER]
Absolute Speed Change Rating [ASCR]
Root Mean Squared Speed Error [RMSSE]
Inertia Work Rating [IWR]
Drive trace indexes are varied according to driving style.

## Slide 29: Electric energy Consumption (EC)
29
29
ER
DR
EER
ASCR
RMSSE
IWR
EC has variability (-2% ~ +8%) according to driving style.
0.8
-2
+4

## Slide 30: Pure Electric Range (PER)
30
30
ER
DR
EER
ASCR
RMSSE
IWR
PER has variability (+2% ~ -8%) according to driving style.
0.8
-2
+4

## Slide 31
31
31
< Previous study >
Test results of ICE and NOVC-HEV vehicles

## Slide 32: Relationship between indexes and CO2
32
32
ER
DR
EER
ER, DR and EER is not appropriate to detect unexpected driving style.
Not detected!!
Not detected!!
Not detected!!

## Slide 33: Relationship between Indexes and CO2
33
33
ASCR
IWR
RMSSE
Rough
Smooth
Rough
Smooth
Rough
Smooth
ASCR, IWR and RMSSE are able to detect unexpected driving style