## Slide 1: WLTP-17- 08e Rev1
1
Heinz Steven
10.01.2017
Cycle / Gearshifting
Status report about the work of the task force on cycle and gearshift issues

## Slide 2: Audio-web telco at 16.12.2016
2
After WLTP IWG #16 at 05. to 07.10.2016 the gearshift issues task force had an audio-web telco at 16.12.2016 where the following items were discussed:
Annex 1, Combination of downscaling and speed cap,
Annex 2, paragraph 3.4 Calculation of available power – ASM (deletion of the word “exponential”),
Annex 2, Paragraph 3.5, Determination of possible gears to be used,
Definition of nmin_drive,
Round Robin tests for GS calculation tools,
Downshifts during decelerations down to standstill.

## Slide 3: Annex 1, Combination of downscaling and speed cap
3
  (a) The new updated gearshift calculation tool applies downscaling first and then the speed cap on the downscaled cycle. This is in line with the rank order of the paragraphs in annex 1.
  After a short discussion this item was adopted by the group.
  (b) Which cycle version, if for a class 3 vehicle the maximum speed according to annex 2 would be >> 120 km/h and a speed cap < 120 km/h is applied: class 3-1 or class 3-2.
  Convenors proposal: class 3-2, because there is no need for such vehicles to reduce the dynamics of the cycle.

## Slide 4: Annex 1, Combination of downscaling and speed cap
4
  The discussion about this item focussed on the questions how the maximum speed is defined and about the difference between vmax in annex 1 and vmax in annex 2.
  The convenor made clear that vmax in annex 2 is calculated for the individual test vehicle as (indirectly) defined in annex 2, paragraph 2 (i).
  Annex 2, paragraph 2 (i) specifies the gear in which the maximum speed is reached, but not explicitly vmax itself. And the calculation is based on the equivalence of the road load power and the available power. So, the design of the drivetrain and the road load for the individual test vehicle is taken into account.

## Slide 5: Annex 1, Combination of downscaling and speed cap
5
  The Japanese colleagues made clear that vmax in annex 1, which is used as borderline (120 km/h) between the class 3a and class 3b cycle is vmax as defined in paragraph 3.7.2 of the GTR.
  This paragraph reads: "Maximum speed" (vmax) means the maximum speed of a vehicle as defined by the Contracting Party. In the absence of a definition, the maximum speed shall be declared by the manufacturer according to Regulation No. 68. But the reference to this paragraph is missing in annex 1.
  It was decided to better specify vmax in annex 1 as well as in annex 2 but to leave the decision on the question, which cycle version should be used in case of a speed cap, to the IWG.

## Slide 6: Annex 1, Combination of downscaling and speed cap
6
  A revised text for annex 1 and annex 2 regarding vmax was already sent to the drafting coordinator.

## Slide 7: Annex 2, paragraph 3.4 Calculation of available power - ASM
7
  The current explanation of ASM is as follows:
  ASM is an additional exponential power safety margin, which may be applied at the request of the manufacturer.
  The word “exponential” needs to be deleted, as already requested by the Japanese colleagues.
  This proposal was accepted by the group without further discussions.
  A revised text was already sent to the drafting coordinator.

## Slide 8: Annex 2, Paragraph 3.5, Determination of possible gears to be used
8
  Paragraph 3.5 reads:
  The possible gears to be used shall be determined by the following conditions:
  (a) The conditions of paragraph 3.3. are fulfilled, and
  (b) If ni,j ≥ nmin_drive of ngear > 2, Pavailable_i,j ≥ Prequired,j
  (b) should read:
  If ni,j ≥ minimum engine speed of the Pwot curve (see paragraph 2 (h) of this annex), Pavailable_i,j ≥ Prequired,j
  Justification: If Pwot is provided at lower speeds than nmin_drive, the available power check should start at this speed.

## Slide 9: Annex 2, Paragraph 3.5, Determination of possible gears to be used
9
  After a discussion about the influence of this modification on the gear use and after the clarification of some misunderstandings this proposal was accepted by the group.
  A revised text was already sent to the drafting coordinator.
  Paragraph 3.5 is continued with the following text:
  If in (b) Pavailable,i,j ≥ Prequired,j can only be fulfilled by using a gear where paragraph 3.3.(a) of this annex cannot be fulfilled because the corresponding engine speed exceeds nmax_95, this shall be accepted as long as the engine speed does not exceed nrated.

## Slide 10: Annex 2, Paragraph 3.5, Determination of possible gears to be used
10
  This sentence should read:
  If paragraph 3.5 (b) Pavailable,i,j ≥ Prequired,j can only be fulfilled in gear ng-1, when paragraph 3.3 (a) cannot be fulfilled, because the corresponding engine speed exceeds nmax_95, this shall be accepted as long as the engine speed does not exceed nrated.
  Justification: The restriction to the second highest gear is necessary, otherwise the upper limit would always be nrated.
  This proposal was accepted by the group.
  A revised text was already sent to the drafting coordinator.

## Slide 11: Definition of nmin_drive
11
  A modified version of the latest VCC/convenor compromise proposal would have been necessary, in order to have a basis for further discussions. But no proposal was sent to the convenor prior to the web-telco.
  The status of the discussions within ACEA could be summarised as follows:
  ACEA currently has no common position, there are two remaining options:
    Option 1: leave the definition as it is,
    Option 2: use the VCC/convenor proposal with target accelerations based on torque to mass ratio and power to mass ratio (areq = 6*Tmax/mtest + 15*Pmax/mtest + 0,4), but replace the coefficients 6 and 15 by 4 and 16.

## Slide 12: Definition of nmin_drive
12
  The Japanese colleagues stated, that they assessed option 2 with the coefficients 6 and 15 and could not accept it. But since they did not yet assess this option with the coefficients 4 and 16, they were asked to check it.
  The Japanese colleagues promised to do so, but asked the convenor to provide the development database, which was used by ACEA.
  And the Japanese colleagues repeated their preference for having both options as options in the GTR to be chosen by the manufacturer.

## Slide 13: Definition of nmin_drive
13
  One group member further mentioned that a compromise would be necessary prior to the next IWG meeting in January 2017, in order to ensure the adoption for the EU legislation.
  Therefore the convenor proposed to leave the issue open in his report to the IWG and to provide a revised version of his report prior to the next IWG, in case an agreement could be achieved.
  Since the group did not find such a compromise, it is proposed to close this item and leave the definition of nmin_drive unchanged.

## Slide 14: Round Robin tests for GS calculation tools
14
  At the last meeting Christoph Lueginger proposed a round robin test for gearshift calculation tools in order to check the tools as well as the common understanding of the text in annex 2.
  This proposal was welcomed by the TF but the organisation could not yet be started due to lack of time.
  Christoph Lueginger and the convenor apologised for the delayed start of the organisation of the round robin test.
  The Japanese colleagues asked, whether a participation could be skipped, if the ACCESS based gearshift calculation tool would be used, since the tool will anyway be included in the test.

## Slide 15: Round Robin tests for GS calculation tools
15
  That is the case, but it was mentioned that example vehicles for the round robin test from Japan would be highly appreciated.
  It was also pointed out, that – at least for European participants - a GTR version and a EU legislation version would be included, in case, there will be differences in the prescriptions between the latest GTR text and the EU legislation.

## Slide 16: Downshifts during decelerations down to standstill
16
  This issue was brought up and added to the agenda by Nick Ichikawa. He proposed the following modification for final decelerations to standstill of each short trip:
  The gear used just before the deceleration starts should be kept with the clutch engaged during the deceleration until the engine speed drops below nmin_drive. For the rest of the deceleration phase either the gear lever shall be set to neutral with the clutch engaged or the gear shall be kept with the clutch disengaged.

## Slide 17: Downshifts during decelerations down to standstill
17
  One group member expressed objections, because this would not reflect normal practical use and reminded the group that the use of the 1st and 2nd gear is already prohibited (the 1st gear in any case, the 2nd gear in most cases) by the current provisions.
  Nick Ichikawa was asked to provide example files with a comparison of the current gear use and his proposal and he promised to provide these.
  The convenor made a similar proposal as for agenda point 5 (nmin_drive): To leave the issue open in his report to the IWG and provide a revised version of his report prior to the next IWG, in case Ichikawa’s proposal could be accepted.

## Slide 18: Downshifts during decelerations down to standstill
18
  Meanwhile example files were send to the convenor but so shortly before the IWG that they could not be distributed to the GSTF in due time.
  But, since the example files could demonstrate the need for further consideration, it is proposed to leave this item on the agenda of the GSTF and work on an amendment proposal for IWG #18.
  In addition to that further amendments for the text in annex 2 might be necessary in order to make the requirements more precises.
  As an example, it needs to be stated that nmin_drive as lower limit for the Pwot curve is nmin_drive as defined in paragraph 2 (k) of annex 2 and not a higher value that might be chosen by the manufacturer.

## Slide 19: End
19
Thank you for your attention!