| JW WG | Contents | regulation14. | ed | Missing words | Names and addresses of technical Services responsible for conducting... | Accepted. |
| --- | --- | --- | --- | --- | --- | --- |
| JW WG | Contents | Annexes 1+2 | ed | Missing words | 1 communication concerning devices 2 communication concerning vehicles | Accepted. |
| JW WG | Scope | 1.1. | ed | Missing words | ...as being mutually compatible and interchangeable | Accepted. |
| JW WG | 2. Definitions | 2.2. | ed | Missing orthographic signs and wrong reference number | “standard mechanical coupling devices and components” conform to… in accordance with annex 5 (or 5 and 6?) | Accepted. |
| JW WG | Definitions | 2.4. | ed | Missing word | …listed in paragraph 2.6., but conforming to existing… | Accepted. |
| JW WG | Definitions | 2.5. | ge | To be discussed | Rail plates / ladder frames / slider tow beams… It shall be possible to approve as separate technical unit as well as integrated part of the device performing the connection to the second vehicle | The optional approval is accepted, not yet included in ACDC-02-03e Rev 2. Base wording on R55 (Angelo to give ref.) |
| Jw WG | Definitions | 2.6.2. | ed | Wrong wording | Coupling head 80 and keeper plate | Accepted. + 2.6.9 … hitch rings or drawbar … |
| WG | Definitions | 2.11 | te | Statement to maximum design speed is missing for coupling as well as for vehicle | After “g = acceleration: vmax is the maximum design speed for which the coupling device resp. the vehicle is tested and approved with regards to this regulation | Accepted and included in ACDC-02-03e Rev 2. To add before subscripts. |
| JW WG | 3. Application | 3.2.2. and 5.3.2 | ed | Cancel words, because of old-fashion procedure | Three sets of drawings | Accepted. |
| JW WG | Application | 3.2.3.1. | ed | Missing words | The characteristic values of the coupling devices shall be at least | Accepted. |
| JW WG | 7. Markings | 7.1 | ge | Missing reference to a type plate | …shall bear a type plate with the trade name, | Accepted and included in ACDC-02-03e Rev 2. |
| JW WG | Markings | 7.1. | te | v (maximum design speed) is not mentioned | … shall bear…., the maximum design speed, … | Accepted and included in ACDC-02-03e Rev 2. To be inserted in 7.3. |
| JW WG | Markings | 7.5. | ed | Cancel one word | … if it the use | Accepted. |
| JW WG | Approval | 8.5.6. | ge | Insert new item, renumber 8.5.5. to 8.5.6. | 8.5.5. a capital letter T for 2-component testing | Accepted and included in ACDC-02-03e Rev 2. |
| JW WG | 2. Communication | 7. | ge | Unclear, if the given values are the performance values or the required values by the vehicle. | Add “required” | Accepted and included in ACDC-02-03e Rev 2. Add “Required characteristic values” as header. |
| JW WG | Annex 4 | Footnote to table 1 | te | If Av is given, no S- nor V-value is given, so no needed | * hinged drawbars…., no S-nor V-value | Accepted. |
| JW WG | Annex 5 | 3.1.5. | ed | Missing word | Clevis type drawbar coupling… | Accepted. |
| JW WG | Annex 5 | 4.2. | te | Missing drawings | Drawings of 6 hole and 8 hole flange coupling shall be added | Not accepted. Too many types, not flexible. |
| JW WG | Annex 5 | Table 2 | te | References to be reviewed |  | All to review for next meeting. |
| JW WG | Annex 6 | 1.1. | te | Theoretical check shall be possible only in case of certain classes and constructions of couplings similar to this classes | (Add at the end of sentence:) In addition, the type…check possible, in case of coupling class d, e, f, I, j and class s similar to the coupling classes mentioned before. | Accepted and included in ACDC-02-03e Rev 2. Add: “in case of coupling class d, e, f, l, j and class s similar to this coupling classes.” |
| JW WG | Annex 6 | 1.5. | ed | Missing word | The characteristic values D, Dc, S, Av and vmax | Accepted and included in ACDC-02-03e Rev 2. |
| JW WG | Annex 6 | 3.1.3. | te | Distinction between vmax until 40 km/h and more than 40 km/h | 3.1.3.1 Loading assumptions if vmax not higher than 40 km/h | Obsolete due to limitation to 60km/h |
| JW WG | Annex 6 | 3.1.3.1. | ed | V is just defined in 2.definitions 2.10.3 | Cancel formula for V-value, a and x/l value | Accepted and included in ACDC-02-03e Rev 2. |
| JW WG | Annex 6 | 3.1.3. | te | 2- component test for coupling balls, if vmax is higher than 40km/ | 3.1.3.2. Loading assumptions, if vmax is higher than 40 km/h, optional for devices with vmax is not higher than 40 km/h Dynamic pulsating endurance test with Fhor = +-0,6 D for full trailers Fvert = s +- 0,6 V | Obsolete due to limitation to 60km/h |
| JW WG | Annex 6 | 3.2.1. | te | The 2-component test for devices with vmax higher than 40km/h shall be obligatory | (Cancel the 2. Sentence, add) 3.2.2. Loading assumptions, if vmax is higher than 40 km/h, optional for devices with vmax is not higher than 40 km/h Dynamic pulsating endurance test with Fhor = +-0,6 D for full trailers Fvert = s +- 0,6 V (Renumber 3.2.2. to 3.2.3.) | Obsolete due to limitation to 60km/h |
| JW WG | Annex 6 | 3.3.1.1. | te | Distinction between vmax until and higher 40km/h | 3.3.1.1.1. Loading assumptions if vmax not higher than 40 km/h | Obsolete due to limitation to 60km/h |
| JW WG | Annex 6 | 3.3.1.1. | ed | V-value is just defined | (Cancel formula for V-value, a and x/l value Cancel “alternatively: asynchronous…) | Accepted and included in ACDC-02-03e Rev 2. |
| JW WG | Annex 6 | 3.3.1.1. |  |  | Add new 3.3.1.1.2.. Loading assumptions, if vmax is higher than 40 km/h, optional for devices with vmax is not higher than 40 km/h Dynamic pulsating endurance test with Fhor = +-0,6 D for full trailers Fvert = s +- 0,6 V | Obsolete due to limitation to 60km/h |
| JW WG | Annex 6 | 3.3.1.2. | GE | To be discussed, if the coupling between trailers can not be rigid drawbars, without required Dc | (Add dynamic test up to and higher than 40km/h taking into account also the V-value) | Obsolete due to limitation to 60km/h |
| JW WG | Annex 6 | 3.3.3.1 | te | Missing exclusion of couplings with vmax higher than 40km/h | (Add after last sentence( Otherwise test conditions as in 3.3.1.1. | Obsolete due to limitation to 60km/h. |
| JW WG | Annex 6 | 3.7. | te | Testing and verification requirements on drawbars are completely missing. | For drawbars with vmax more than 40km/h refer to ECE R55.01 annex 6, class E, for calculation of bending refer to ISO 7641-1:2013, For drawbars with vmax up to and including 40km/h may be possible to copy requirements of TA31, of German StVZO, so that higher performance values are possible. | Text to be drafted. Andreas Schauer will initiate. To be considered during 4rd ACDC meeting. |
| Jw WG | Open issues | rails |  | Didn`t get the proposal of Mr. Afflerbach |  | Proposal of Mr. Afflerbach to be circulated. To be considered during 4rd ACDC meeting. |
| JW WG | Open issues | Static / one component testing / 2 component testing |  | Open discussion (see Bologna meeting and requirements in UNECE on brakes, tires, lights, |  | Obsolete |
| JW WG | Open issues | Missing drawings |  | Have been delivered !?!? |  | Italian WG contribution to be included in ACDC-02-03e Rev 2 (See secretariats observations in ACAC-03-05e). To be considered during 4th ACDC meeting. |
| JW WG | Open issues | Missing angles |  | Unfortunately the tractor manufacturer didn`t collaborate |  | To be considered during 4th ACDC meeting. |
| JW WG | Open issues | Missing class for tractor drawbar |  | Will be added little later |  | Obsolete, is Class i |