## Slide 1: India’s Comments on EPPR-19-26 (Part-B2)

## Slide 2
Row no 14: Inclusion of Test cell humidity requirement.
  Humidity requirement is already there in R83, R15 and GTR-15(WLTP) for 4 wheelers.
  Indian regulation based on GTR2 also incorporated humidity requirement inline with R83.
  The logic for exclusion for 2 wheelers is not known.
  India feels that inclusion of this requirement will reduce the test variations and improve repeatability.
Row no 16 : Soak Room / test cell temperature
  Based on the presentation on 11th May 2017 tele-con and comments from members, India agreed to keep same temperature for test cell and soak room as 23 +/- 3 Deg C.
Row no 19 : Definition for RST25 & RST45
  RST25 means : Reduced speed test cycle of Part 1 cycle of WMTC with maximum cycle speed truncated to 25 km/h for Sub-class 0-1
  RST45 means : Reduced speed test cycle of Part 1 cycle of WMTC with maximum cycle speed truncated to 45 km/h for Sub-class 0-2

## Slide 3
Row no 24: Reference fuel specification:
  India propose the principal norms based on Euro 5 and its reference fuel. GTR shall also include alternate norms for regional application with regional reference fuels.
Row no 40: Exhaust gas measurement system
  During tele-con on 11th may 2017, closed type of CFV-CVS system was agreed by the members.
  India had suggested Open type CFV-CVS system need not be permitted, in absence of data.
  India had requested IMMA to provide appropriate data showing no influence on the emissions in comparison to CFV-CVS closed type system for retaining Open type CFV-CVS system as an option.
  Data from IMMA is awaited to conclude.

## Slide 4
Row no 59, 63, 71, 82 to 109 & 115 : Procedure for PM Measurement
  EPPR group members have to decide on the fundamental requirement whether we should follow the route for PM measurement in line with
    R 83 ( Euro 5a / Euro 6 / WLTP) with pre-classifier to cut down particles above 2.5 µm
    OR
    R83 up to Euro 5 ( Which doesn’t include pre-classifier to cut down the particles above 2.5 µm).
  The above decision will change the procedural part as well as test set up required.
  Hence group’s decision is required to take final route so that the concrete proposal on PM measurement can be made.
  India’s current proposal is based on WLTP text considering Euro 5a / Euro 6 requirement.
  This proposal will also address the future requirement of PN beyond Euro 5 for two wheelers.

## Slide 5
Row no 67 : Provision for Regeneration
  India’s proposal on exhaust sampling is already agreed.
  India views on provision of regeneration in this clause need to be retained, to address the need of vehicles (Diesel and GDI) fitted with DPF.
  To conclude, views from other members is requested.
Row no 139 : Procedure for vehicles having deceleration levels not matching the cycle speed :
  Faster deceleration can happen without using the brakes, because of vehicle characteristics
    E.g. vehicle with automatic transmission
  However faster deceleration should not be permitted by application of deliberate braking.
  Hence the clause to be modified to cater to vehicles having such characteristics.

## Slide 6
Row no 146, 150 & 240 : idle start stop
  Benefits of this system depends on the idling period of test cycle and manufacturer strategy therefore test should be done with start stop in OFF condition .
Row no 277 : Pollutants to be monitored
  India had proposed to change the (28.04.2017) title as:
  “Type I test (verifying the average emission of gaseous pollutants, PM for GDI and diesel vehicle, CO2 emissions and fuel consumption in a characteristic driving cycle)”
  Based on the comments by Chairman that technology specific terms to be avoided, so India now makes the following proposal.
  “Type I test (verifying the average emission of gaseous pollutants, prescribed in applicable tables in item 9.2 or 9.3 of Section B.1, CO2 emissions and fuel consumption in a characteristic driving cycle)”
    This proposal will take care of requirements of Principal and Alternate norms.
    There will be no change required to modify this title if at a later stage any new pollutant is required to be added in the regulation.

## Slide 7
Row no 29, 242 & 244 : Requirement of two roller for twinned wheel vehicle.
  Indian proposal is only to take care of the twinned wheel 2 wheelers, and not for 3 wheelers.
    Currently, 3 wheelers are not in the scope
Row no 262:
  India proposed to change the title of paragraph as “Running resistance force derived from a running resistance table or on road coast down”
    The clause is applicable for both table method and road coast down method
Row no. 326 : Removal of Fixed load type chassis Dynamometer / CO2 measurement
  India proposed to remove fixed load type chassis dynamometer.
  This means Row no. 328 (Clause no. 4.2.2.2.5.1) to be deleted
  This needs to be discussed in EPPR.
  IMMA proposal to add Fuel consumption and delete Electric vehicle parameters, is acceptable.

## Slide 8
Row no 458: Monitoring of soak room temperature
  India had suggested monitoring temperature of soak room
    At 1Hz and 5 min average should not have systematic error
  Agreed to align the temperature with test cell condition
  India has agreed to keep the soak room temperature same as test cell temperature so the soak room temperature tolerance should now be changed to 23+5°C, and remove the condition of 1 Hz and 5min avg temp measurement.
  India proposes following wording :
  “After this preconditioning, and before testing, vehicles shall be kept in a room in which the temperature remains relatively constant between temperatures specified in clause number 6.1.1 20 °C and 30 °C at 23± 3 °C .on a 5 minute running average and shall not show a systematic deviation from the set point. The temperature shall be measured continuously at a minimum of 1 Hz. This conditioning shall be carried out for at least six hours and continue until the engine oil temperature and coolant, if any, are within ± 2.0 °C of the temperature of the room.”

## Slide 9: Thank you