## Slide 1: India Proposal on EPPR-19-24 rev.1 (Part B3)

## Slide 2
Row no 30 & 66 : Compliance to limit values
  The purpose of the requirements laid down in this section is to demonstrate that the [approved] / [certified] vehicle complies with the requirements of in use vehicles.
  In use vehicle requirement cannot be harmonized in GTR since the subject is covered in 1997 agreement
  This section covers harmonized test procedure for all pollutants known to be used by the CPs for Type II test.
  REPPR requirements are based on the in-use vehicle regulation for Europe. Hence, compliance to the REPPR requirements may not be relevant for CPs having different in-use norms, considering regional needs.
  India, therefore suggest that recording of the result is enough and the CPs can take their own decision of pass/fail
  Alternatively, If EPPR can agree to discuss principal and alternate norms can be worked out.

## Slide 3
Row no. 24 to 40 : Adjustments for Type II test
    As the Type-II test is to be conducted with the same settings of Type-I test without any changes, there is no need to measure the characteristic at different positions. Hence, proposed to delete these clauses on the subject matter.
    Additionally India has also observed following :
      The requirements given here are similar to what was in R15 historically.
    More appropriate for carburetor vehicle.
    No relevance for technology for EU 5 type of vehicles.
  Request IMMA to reconsider suggestion of retaining the clause for aligning with REPPR.

## Slide 4
Row no 58 , 59 & 60: Correction factor for CO and HC
  India proposes the following correction factors:
  For any value of correction factor coming less than 1.It should be treated as 1
Correction factor
cCO is the measured concentration of carbon monoxide, in vol. %;
cCO2 is the measured concentration of carbon dioxide, in vol. %;
cCOcorr is the corrected concentration for carbon monoxide, in vol. %;
cHC is the measured concentration of hydrocarbon, in vol. ppm;
cHCcorr is the corrected concentration for hydrocarbon, in vol. ppm, expressed by methane CH4 equivalent;
a is 1,8 when concentration of hydrocarbon is measured by NDIR (Non-Dispersion Infra Red), and a is 1 when the concentration of hydrocarbon is measured by FID (Flame Ionization Detector);
b is m when the concentration of hydrocarbon is expressed by ppm Cm (for example b is 6 for n-hexane C6H14 equivalent or b is 1 for methane C1H4 equivalent).
r
Correction factor

## Slide 5
  This formula is taken from ISO 17479:2013
  Even though ISO specifies that only for secondary air injection India feel this can be applied for air dilution
  It appears this formula is applicable only for 4 stroke engines
  Request EPPR secretory to consult ISO if this formula can be used for 2 stroke also.
  In ISO 17479 the correction formula given is only for vehicle having secondary air injection system
  In ISO 17479 two more formula are given, which are much older than proposed one.
  In case of two stroke vehicles, correction factor is only available for CO and not for HC.