## Slide 1: OICA input on software updates to UN TF CS/OTA
Current Situation
Possible Needs
Possible Solutions
  Vehicle Type Approval and Registration
  Periodical Technical Inspection
TFCS-05-08

## Slide 2: Current situation of software updates
ECU | SW version
1 | V3.6
2 | V1.3
3 | V1.6
4 | V8.9
Etc. | 
Type approval test
ECU | SW version
1 | V3.9
2 | V1.4
3 | V1.6
4 | V9.1
Etc. | 
First registration
ECU | SW version
1 | V4.1
2 | V1.8
3 | V2.3
4 | V9.3
Etc. | 
After registration
Note: Only some specific combinations of SW versions are compatible.
For example V4.1 of ECU 1 may not be compatible with V1.7 of ECU 2.
Example for 1 vehicle (VIN)
Software updates are performed during the whole vehicle life cycle.
The very big majority of updates does neither impact type approval nor PTI.

## Slide 3: Possible needs
Software configuration control may be necessary
  For vehicle type approval and registration
    To update information on vehicle registration if a software update has an impact on vehicle type approval
  For Periodical Technical Inspection
    To check whether type approval relevant software installed on the vehicle is compatible with vehicle type approval
    Note:
      PTI can check the software versions of type approval relevant systems but cannot check whether the software is corrupted
      The case of cyberattacks (e.g. a hacker modifies a software without changing the official version) shall be covered by the Threat Analysis of UN TF Cybersecurity and OTA

## Slide 4: Vehicle type approval and registration
Case 1: An already registered vehicle is updated and the software update will change the properties of the vehicle such that *)
  One or more existing type approvals covering systems in the vehicle are affected (modification of existing functions) and/or
  One or more additional type approvals are necessary to cover additional functionalities (new functions)
Case 2: The software update does affect type approval but the vehicle is not yet registered  similar to case 1 but simpler to handle
Case 3: The software update does neither affect type approval nor registration
*) : this could also include the case that the vehicle production is definitely discontinued

## Slide 5: Vehicle type approval and registration Possible mid-term solution
The necessary system type approvals are extended or newly obtained and linked into the Whole Vehicle Type Approval (WVTA). This step is also necessary for the ongoing production of vehicles (case 2).
For the already registered vehicles (case 1) a transparent documentation of the modification is needed. This can be achieved by allowing for an „extension“ of the CoC/DoC* of the vehicle.
With such documentation, changes of the registration can be performed according to national processes.
Type approvals of the modified or new systems
WVTA
Updated CoC/DoC
Necessary for new production vehicles (case 2)
Documentation of changes for already registered vehicles (case 1)
*CoC: Certificate of Conformity, see article 18 of Directive 2007/46/EC
*DoC: Declaration of Conformance, see Annex 6 of draft UN Regulation No. 0 (doc. WP.29-171-11)

## Slide 6: Vehicle type approval and registration Mid-term target process
Background and necessary boundary conditions for the target process:
Europe: It is assumed that the CoC will be stored in electronic format in the next years. The EREG activity is ongoing, inclusion in the new EC framework regulation planned. It is an industry objective to replace the paper CoC by the electronic CoC after a transition time.
UNECE: With IWVTA and implementation of DETA, the DoC on VIN-basis will be implemented. This will include reference to the Regulations (and their versions) the individual vehicle complies with.
Today in Europe, this information is not directly included in the CoC where only reference to a WVTA is made. In the future, the information that figures in the DoC may need to be included in the CoC.
In Summary: for this target process we will need (application outside UN TF CS)
  DETA
  Electronic CoC/DoC data
  A secure process to update a CoC/DoC: like the extension of a type approval

## Slide 7: Vehicle type approval and registration Interim process
Since prerequisites for the target process are not yet available, an interim process is needed
The interim process will be relevant only for a limited period of time  it should not impose too much burden on all stakeholders.
The following way forward could be envisioned:
  The manufacturer provides a documentation describing the software update and listing the new/modified type approvals for each impacted VIN. This will also identify whether and how the change affects registration- or tax- relevant parameters (CO2, engine power, etc.)
  This documentation is provided via the type approval authority to the registration offices.
  In case of relevant changes, the registration information is adjusted according to the national processes.

## Slide 8: Vehicle type approval and registration Solution for 3rd party SW updates
For software updates that are not performed by the original manufacturer of the vehicle, a multistage type approval process may apply.
Here, the manufacturer’s responsibility is (partly) transferred which can be adequately covered in the multistage process.
The multistage process is not supported for updates performed under control of the vehicle manufacturer as the high volume of concerned vehicles creates too much administrative burden.

## Slide 9: Periodical Technical Inspection
The need for PTI is to check whether the type approval relevant software installed on the vehicle is compatible with the vehicle type approval
This covers also the previously described update of type approval and registration data:
  In the target process, the PTI needs an access to the electronic CoC/DoC
  In the interim process, the PTI needs access to the documentation describing the update and listing the new/modified type approvals (e.g. via the type approval authority or the registration offices)