## Slide 1
LT/C Endurance harmonization

## Slide 2
Endurance Test
• FMVSS 139 (all LT tires up to Load Range E)
– Defines test pressure based on Load Range of tire (not LI or speed
symbol)
– Starts test at 85% of max load of tire (sidewall marking, not LI) and ends
at 100%
– Has 3 steps of 4, 6 and 24 hours (34 hours total)
– Uses speed of 120 km/h, regardless of speed symbol (110 km/h for
severe snow tires)
– Uses 38°C test conditions
• R54 (all C tires, only speed symbols less than Q)
– Allows manufacturer to choose test pressure nearest design pressure
for max load carrying capacity
– Uses loads based on speed symbol and LI (3 sets of load steps)
– Has speeds based on speed symbol
– Has 3 steps based on speed symbol: 7, 16 and 24h (47h for lower
speed symbols) or 4, 6 and 24h (34 h for higher speed symbols)
– Uses 20 – 30°C temperature range
Ref WGLTC-10-006

## Slide 3
Endurance Test Questions
• What pressure to use?
– Based on Load Range?
– Based on pressure for max load carrying capacity (LI)?
Reminder: There is no formula for moving between LR and LI!
• What speed to use?
– always 120 km/h?
– based on speed symbol?
• What duration to use?
– 4, 6 and 24 hours?
– 7, 16 and 24 hours, or 4, 6 or 24 hours based on speed symbol?
• What load to use?
– From 85% to 100% of max load?
– Based on speed symbol and LI?
• What temperature to use?
– 20 – 30°C?
– 38°C?
Ref WGLTC-10-006

## Slide 4
Market Share LT/C per Speed Symbol and Region
Significant share of LT/C with SS <‘Q’ in Japan, India, and with SS > ‘Q’ in Europe, US, India