## Slide 1: China Proposal (TYREGTR-15-06): Tyre Industry Assessment
Tyre GTR Informal WG Meeting
June 7-9, 2017

## Slide 2: Load Range and Ply Rating
China Concern
  Since Load Range is optional in GTR, China would like Ply Rating included since it is allowed in China. China requests to include a Ply Rating to Load Range table.
Industry Assessment
  Load Range is the more current, recognized terminology
    Ply Rating is not common terminology for global, radial LT and C-type tyres.
    Ply Rating is more common on Off-the-Road and Agricultural tyres.
Recommendations
  Tyre industry recommends that this additional table not be included in the GTR
  Could China add this table during the transposition of the GTR into the national regulation?
  China is asked to clarify their request to have a correspondence in PR in the table 3.3.1.2.3.3.1?
  Question to GTR Convenor: What is the possibility for a CP to amend and/or add local provisions when transposing the GTR in their national regulations? Can a CP when transposing have specific TA or self certification requirements (technical markings and administrative markings) that are not harmonized?

## Slide 3: Plunger Energy and Beat Unseat
General Comment: compendium of tests in Tyre GTR only contains UNECE and FMVSS tests
  Plunger energy and bead unseat tests are only contained in FMVSS
  Question for GTR Convenor: Should GTR be limited to tests listed in the compendium?

## Slide 4: LT Plunger Energy
China Concern
  Adopted ISO 10454 for metric LT tyres and it does not match the current text in the GTR for strength requirements and plunger tip diameters
Tyre Industry Assessment
  ISO 10454 is titled, “Truck and Bus Tyres – Verifying Tyre Capabilities – Laboratory Test Methods
    Does not pertain to metric (or any type) LT tyres
    Standard is out of date with the last revision being 1993
Recommendation
  ISO 10454 is Out of Scope of the GTR
  Not relevant to LT tyres
  GTR text for Plunger Energy should remain the same

## Slide 5: LT Plunger Energy
China Concern
  List 4 LT sizes that have more higher requirements in GTR than in the China GB (ISO) standard
Tyre Industry Assessment
  ISO 10454 does not apply to LT tyres
  GTR requirements are based on well established FMVSS 119 requirements for LT tyres
Recommendation
  ISO 10454 is Out of Scope of the GTR
  Not relevant to LT tyres
  GTR text for plunger energy should remain the to reflect what is the Compendium.
  If China wants to implement lower requirements than the GTR into its national regulations, Can it be done at the level of transposition of the GTR in their National regulation?

## Slide 6: LT Plunger Energy
China Concern
  For rim diameters < 12 and 13-14, China adopted the ISO 10454 which is lower than GTR requirements
Tyre Industry Assessment
  ISO 10454 does not apply to LT tyres
    Also appears that China is using a combination of Table 3 and Table A.3 in Annex A
      China requirements for < 12 are under Table 3
      China requirements for 13-14 are under Table A.3
    Under Annex A, it states “Tables A.1, A.2 and A,3 apply in place of tables 1, 2, and 3 respectively”.
      It appears that China has misinterpreted these tables by using a combination of the tables instead either Table 3 or Table A.3
  GTR requirements are based on well established FMVSS 119 requirements for LT tyres
Recommendation
  ISO 10454 is Out of Scope of the GTR
  Not relevant to LT tyres
  GTR text for plunger energy should remain the to reflect what is the Compendium.
  If China wants to implement lower requirements than the GTR into its national regulations, Can it be done at the level of transposition of the GTR in their National regulation?

## Slide 7: LT Plunger Energy
China Concern
  Proposes that LT tyres with rim diameter > 16 and single load capability > 1500 kg (122 LI) use 32 mm plunger diameter
  Suggest that maybe LT tyres > 122 LI could be handled later
    Is China suggesting that these tyres should be excluded from GTR since they are considered Class C3 tyres in Europe?
Tyre Industry Assessment
  GTR requirements are based on well established FMVSS 119 requirements for LT tyres
    Require 19 mm plunger diameter for all LT tires
  Over 40 LT tyre sizes in 2016 TRA Year Book would be affected
    Thus lowering the requirement on these sizes
    LT tyres with LI > 122 are common in USA and Canada and would be difficult to exclude them from GTR
Recommendation
  GTR text for plunger energy should remain the to reflect what is the Compendium.
  If China wants to implement lower requirements than the GTR into its national regulations, Can it be done at the level of transposition of the GTR in their National regulation?

## Slide 8: LT Plunger Energy
China Concern
  Propose to change the GTR text for “average strength…” to “breaking energy of each test point shall be no less than…”
Tyre Industry Assessment
  GTR text is consistent with FMVSS 119 requirements
  Although not applicable to LT tyres, the GTR text is also consistent with ISO 10454
Recommendation
  GTR text for plunger energy should remain the to reflect what is the Compendium.
  If China wants to implement lower requirements than the GTR into its national regulations, Can it be done at the level of transposition of the GTR in their National regulation?

## Slide 9: LT Bead Unseat and Low Pressure Test
China Concern
  These tests are not required for LT tyres in China
Tyre Industry Assessment
  Both tests are currently required in USA and Canada for LT tyres
  GTR text should remain consistent with USA/Canadian law
  China can choose not to transpose these tests into national law for regional tyres
Recommendation
  GTR text for bead unseating should remain the to reflect what is the Compendium.
  If China wants to implement lower requirements than the GTR into its national regulations, Can it be done at the level of transposition of the GTR in their National regulation?

## Slide 10: LT Load/Speed Endurance
China Concern
  Propose to do both ECE54 load/speed (HS test) and FMVSS 139 endurance tests on LT tyres that have speed symbol Q and above
  Propose to only do ECE54 load/speed (endurance test) on LT tyres below speed symbol Q = No FMVSS High speed or FMVSS endurance test.
Tyre Industry Assessment
  All LT tyres for USA and Canada require FMVSS 139 endurance, low pressure, and high speed
  Additional work by the industry needs to be done on harmonizing the ECE54 load/speed test and FMVSS 139 high speed test
  Additional work by the industry needs to be done on how to handle LT tyres below speed symbol Q
Recommendation
  GTR should remain the same at this time
  Both the FMVSS 139 endurance and the ECE54 tests are in the GTR, so an individual CP can transpose them as desired into its national regulations
  Additional work remains for Phase 2B on high speed test harmonization and on LT tyres below speed symbol Q speed

## Slide 11: Physical Dimensions
China Concern
  Propose to add -4% requirement for Overall Width
  Propose to change +4% requirement for Section Height to +3%
Tyre Industry Assessment
  There are no minimum Overall Width requirements in ECE 54
    China references to TRA and ETRTO having -4% requirements. However, these are design standards based on the Design Section Width, not based on Overall Width
      Therefore, -4% would be unacceptable for overall width because it would be very close to the design section width
  GTR text for section height requirements are consistent with ECE 54
    But + 3% for section height does match TRA standards
Recommendation
  The GTR text should remain the same, without amendment
  GTR Phase 1B addressed issues related to passenger car tires; this issue was not raised
  Overall width proposal of adding -4% requirement is not acceptable
  Section height should not be a regulatory requirement – maximum tolerance is that the tyre doesn’t touch the vehicle