## Slide 1: Software and Regulation

## Slide 2: Why should software be regulated?
Already 33 existing Regulations depend on software
This software can influence safety and/or security
Software updates can effect safety and/or security, or requirements of system type approval, even if the update is not related to type approval.
Updates are also delivered to the vehicles as functional changes and each function may have an impact on multiple systems(approvals)

## Slide 3: Regulations affected by software
Number | Regulation | Reason
11 | Door latches and door retention components | Locking and unlocking of door can be associated with speed, collision impact etc.
16 | Safety belts | Pre- tensioner and force limiter behavior (during crash and near crash scenarios)
17 | Seats | Seat positioning during a crash or near crash event
94 | Frontal Collision Protection | Airbag deployment strategy during crash or near crash event, sensors for detecting crash or near crash scenario, EDR logging of events
95 | Lateral Collision Protection | Airbag deployment strategy during crash or near crash event, sensors for detecting crash or near crash scenario, EDR logging of events
100 | Electric power trained vehicle | Charging and discharging,temperature control controlled by software
127 | Pedestrain safety | Sensors for detecting proximity with pedestrians
134 | Hydrogen and fuel cell vehicles | Fuel cell system operation including charging/ discharging of cells, working pressure and thresholds etc.
135 | Pole side impact | Airbag deployment strategy during crash or near crash event, sensors for detecting crash or near crash scenario, EDR logging of events
137 | Frontal impact with focus on restraint systems | Airbag deployment strategy during crash or near crash event, sensors for detecting crash or near crash scenario, EDR logging of events
39 | Speedometers and Odometers | Digital speedometer, odometer and milage calculators, data storage for distance, speed parameters
46 | Device For indirect vison | Camera monitoring system operation including picture quality parameters, image display processing, image settings, embedded vision sensor fusion etc.
116 | Anti theft and alarm systems | Sensor for unauthorised entry, user/driver notification fucntion, tilt sensor, remote vehicle operations using smartphones etc.
2015/758 | eCALL | Crash detection, data collection(MSD) and transfer
121 | Identification of controls, tell tales and indicators | 
122 | Heating systems | Optimum temperature maintenance requires reading of temperatures from heat sensors and implementing corresponding temperature regulating measures
10 | Electromagnetic compatability | System integration effects, electromagnetic emission effects as noise/interference on microprcessor and RAM
14 | Safety belt anchorages | Pre- tensioner and force limiter behavior (during crash and near crash scenarios)
15 | Emission of gaseous pollutants | ECU logic for air fuel ratio and determining emission levels and compositions
130 | Lane departure Warning system | Software controlling Advanced driver assistance systems, sensors to detect lane changes and provide notification in case of a departure
131 | Advanced emergency braking system | Software controlling Advanced driver assistance systems, sensors to identify incoming traffic obstacle and apply necessary braking force and reduce acceleration.
*This is just an initial list. More regulations may be affected depending on the exact nature of the software change

## Slide 4: Example case(LIDAR System)
LIDAR system software Update
Braking system
Steering systems
Safety System
Vision system
AEBS- R.131
Brakes- R.13,13-H
LDWS- R.130
Steering equipment-R.79
Frontal collision Protection- R.94
Lateral Collision Protection – R.95
Pole Side Impact- R.135,
Frontal Impact with focus on restraining systems- R.137
Brake Assist System- R.139
Electronic Stability Control- R.139
Steering mechanism- R.12
Handling and Stability of Vehicles- R.111
Device For indirect vision- R.46
* Individual SWIN for each approval would result in 13 approval documents for a single software change
Software updates are delivered to the vehicles as functional updates, where each function( like LIDAR system) is a collection of systems which may require individual approvals. SWIN to be used for identifying each functional updates, with reference to affected type approvals(numbers)

## Slide 5: How should software be regulated
Unlike mechanical systems, software is not suited for type approval as the number of possible situations is too high;
Also the complicated and coupled nature of software change has the possibility of affecting multiple system regulations(within a single change)
Software code is often related to more than one Regulation
Requirements for software will develop over time as more and more complex systems are developed( like LIDAR) supporting autonomous driving and improved safety requirements.
The appendix in R13 and R79 already describe some general requirements for (development of) software
Therefor guidelines in a Consolidated Resolution would be preferable

## Slide 6: Scope?
The scope of the UNECE Taskforce is to arrange security and updates
Moving existing requirement from R13/R79 to a consolidate resolution and adding the ones required for security and updates does not conflict with the scope; the advantage is that only two Regulations will have to be modified instead of 33(and more probably), and one resolution will have to be drafted