Proposal for amendments relating to the approval of modules of Enhanced Child Restraint Systems

The modifications to the existing text of the Regulation are marked in bold for new or strikethrough for deleted characters.

I.	Proposal

Annex 2.,Insert numbering, amend to read:

“1. 	Arrangements of the approval mark”

….

“2. 	Arrangements of the approval mark in combination with an module mark”

….

Insert paragraph numbers, new images, and amend to read:

“2.1. 	Example of a Arrangements of the module mark in combination with an approval mark

2.1.1		Where a module is approved for use with more than one base, the individual base and module combinations shall be indicated on the module in separate module marks, each bearing their applicable size ranges.

An Enhanced Child Restraint System  that bears an approval mark for the stand-alone mode of use, and module marks for its use on three different bases, shall carry the following arrangement of approval and module marks:

The Enhanced Child Restraint System bearing the above marks is capable of being used as an Infant Carrier Module with a vehicle belt for the 45 cm - 75 cm size range; it is approved according to Regulation No. 129-03 under the number 032348.

The Enhanced Child Restraint System can also be used as a module in combination with the base “brand name & model A’, for the 45 cm - 75 cm size range and mass limit of 12 kg; approved according to Regulation No. 129-03 under the number 032439.

The Enhanced Child Restraint System can also be used as a module in combination with the base “brand name & model B’, for the 45 cm - 75 cm size range and mass limit of 12 kg; approved according to Regulation No. 129-03under the number 032440.

The Enhanced Child Restraint System can also be used as a module in combination with the base “brand name & model C’, for the 45 cm - 75 cm size range and mass limit of 12 kg; approved according to Regulation No. 129-03 under the number 032441.

The approval numbers indicate that the approval was granted in accordance with the requirements of the Regulation concerning the approval of Enhanced Child Restraint Systems used on board of motor vehicles as amended by the 03 series of amendments.

2.1.2.	Where a module is capable of being installed in different orientations, separate module marks shall be indicated on the module, each bearing their applicable size ranges.

The Enhanced Child Restraint System bearing the above marks is capable of being used in a rearward facing mode with the base “brand name & model A’, for the 60 cm - 105 cm size range and with a mass limit of 18 kg; approved according to Regulation No. 129-03 under the number 032441.

The Enhanced Child Restraint System bearing the above marks is also capable of being used in a forward facing mode with the base “brand name & model A’, for the 85 cm - 105 cm size range and with a mass limit of 18 kg; approved according to Regulation No. 129-03 under the same number 032441.

The approval number indicates that the approval was granted in accordance with the requirements of the Regulation concerning the approval of Enhanced Child Restraint Systems used on board of motor vehicles as amended by the 03 series of amendments.

2.2		Examples of the symbols to be used on the module mark are given in the figure below. As chosen by the ECRS manufacturer, one of the symbols or an equivalent shall be used on the module mark. ”

II. Justification

According the agreements up to the 66rd Informal Group meeting:

- The approval mark and module mark serve an administrative purpose, for that reason they must indicate the information on their approved use.

- The examples of the module marks are changed in order to ensure that information is provided on the seating unit, indicating to which base(s) the module can be combined.

- The examples of the module marks are changed in order to ensure that information is provided on the seating unit to reflect the possible transportation modes of the product.

- The examples of the symbols to be used on the module marks are separated into four options.

- The text is corrected to use consistent wording of module mark  and not module label)

- The correct reference to the Regulation is done with “UN-Regulation No.129-01”

Editorial

- The size of the letters for the approval label are defined, following the requirements of the approval label.

- The text of the approval label on the stand alone baby shell is changed from ‘Universal ECRS” into “Infant Carrier Module”, to reflect the wording of Annex 22.

- The icon options are indicated to be examples; equivalent images are allowed as well, by choice of the manufacturer.

- Version 10 ‘V10’: English wording corrects, multiple instances

- Version V11: replaced all references to phase 1 by reference to  phase 3 (e.g. “UN-Regulation No.129-01” -> “UN-Regulation No.129-03”