## Slide 1: ACSF-C2 2-actions system
Industry input to ACSF IG
14th meeting
August 2017, Köln
v4
Informal Document: ACSF-14-05
Submitted by the experts of OICA

## Slide 2: Summary
Philosophy
Ultra-sonic sensors capablities
Radar capabilities
Proposal for a blind zone detection
Proposal
Justifications
Mode confusion issue

## Slide 3: Philosophy
Level-2 system, i.e. the driver drives, the system assists:
  the driver monitors the vehicle environment
  the driver may not perform secondary tasks
The driver is aware of the vehicle environment thanks to direct FOV and R46 mirrors
The system must only monitor the zones out of mirrors coverage
  M1/N1: Class I and III FOV
  N3: Class II, IV and V FOV

## Slide 4: Ultra-sonic sensor capabilities
Range: 0-5 m
Sensor-to-target relative speed: < 10 km/h
Angle of detection: ~ 120°
Target movement: stationary and moving
Target nature: any solid, no distinction
HMI: ON/OFF detection
Sensitivity to wheather conditions: low

## Slide 5: Radar sensor capabilities
Range: < 100m
Sensor-to-target relative speed: 0-max speed
Angle of detection: 150°
Target movement: stationary and moving
Target nature: any solid, no distinction
HMI: can transmit distance and speed
Sensitivity to weather conditions: low

## Slide 6: Proposed blind zone detection M1/N1
ISO 17387 „shall warn“ area
UN R46 Class III Field of view
Ocular points 95%ile
Leading edge
Rear edge
3m
3m
0.5m
Outside edge
20m
1m
4m
4m

## Slide 7: Proposed blind zone detection N3 vehicles
UN R46 Class II Field of view
Outside edges
Driver‘s ocular points
4m
1m
1.5m
5m
4.5m
30m
15m
25m
10m
UN R46 Class IV Field of view
3m
3m
0.5m
Leading edge
Rear edge
(truck)
ISO 17387 „shall warn area“
2m
UN R46 Class V Field of view
2.75m

## Slide 8: Proposal
  “3X3m” blind spot detection area (ISO17387 – see sketches) for M1/N1
  “3X3m” blind spot detection area inspired from ISO17387 – see sketches) for M2M3/N2N3
  If target detected in blind spot, then
    Warn the driver
    Ignore 1st and 2nd actions
    Abort lane change support

## Slide 9: Mode confusion issue
What happens if the driver have wrong perception of the system installed in the car
OK | B
A | OK
The car is equipped with
C1
C2
C1
C2
The driver thinks to have

## Slide 10: Mode confusion issue
A situation : The driver think to be in C1 in a C2 equiped car.
The driver will use the command to launch the procedure without monitoring environment and nothing happen (the car expect a second action)
 Not a safety issue
B situation : The driver think to be in C2 in a C1 equiped car.
The driver will use the direction indicator to start the procedure and
: the car start a manoeuver if it is a safe situation
 Not a safety issue

## Slide 11: Justifications
The driver expects an HMI similar to that of the manual driving
The driver can manage the time between the 2 actions
  Unintentional activation prevented thanks to
    ON/OFF switch
    2-action activation
  Low overriding force (< 50 N)
 | Manual driving LC manoeuvre | 2-action ACSF Category-C LC manoeuvre
1st action | Activating the direction indicator to inform the other users | Activating the direction indicator to inform the other users
2nd action | Action on the steering control to change lane | Action on the steering control to change lane