## Slide 1
Presentation of ACSF C tests
Industry input to ACSF IG
14th meeting
August 2017, Köln
v2
Informal Document: ACSF-14-06
Submitted by the experts of OICA and CLEPA

## Slide 2
Lane change procedure
Lane change manoeuvre ≦ 5sec.
3.5.1. Lane change functional test
Conditions are not met
Direction Indicator lamp
flashing time≧ 3sec.
Vsmax≧Vtest ≧ Vsmin
All conditions are met
Lateral jerk and below max values
B1 resumes
DI lamp off ≦ 5sec.

## Slide 3
3.5.2. Abort of lane change test
vtest
vtest
Minimum value of Sdrear
≦[15m]
The driver shall initiate the lane change by the deliberate action.
The lane change procedure does not start. or
The lane change procedure is canceled no later than 10 seconds after the deliberate action of the driver, if the lane change procedure has started and the manoeuver is delayed. The driver is informed that the manoeuver is delayed.
A high volume series production passenger car of category M1 AA saloon
Center of the lane ±20cm
Center of the lane ±20cm
Vsmax≧Vtest ≧ Vsmin
Is it needed?

## Slide 4
3.5.3. Overriding force test
Applicable Paragraph
5.6.5.3
Procedure
Initiate lane change
Before the start of the lane change manoeuvre, the driver shall firmly maintain the steering in the straight direction.
Measure the steering effort
firmly maintain the steering in the straight direction
Vsmax≧Vtest ≧ Vsmin

## Slide 5
Deactivate the direction indicator
flashing time < 3sec.
Deactivation by the driver (5.6.5.6.8.)
3.5.4. Deactivation test
Procedure
Initiate lane change
Before the start of the lane change manoeuvre, the driver shall deactivate the direction indicator.
Vsmax≧Vtest ≧ Vsmin

## Slide 6
3.5.5. Sensor performance test
≦63m
≦6m
Rear sensor
ECUs
CAN
CAN monitor
Capture Trigger
Measurement
Capture the sensor data at the timing the rear vehicle is detected
Confirm the actual distance to the rear by using GPS data of both vehicles
Connection of CAN monitor system should be allowed.
Vehicle system under test
vtest + 10 to 50 km/h
A high volume series production passenger car of category M1 AA saloon
Vsmax≧Vtest ≧ Vsmin
The test shall be repeated with a motorbike (L3), and the distance shall be set at 55m.

## Slide 7
The rear sensor(s) is made blind.
3.5.6. Sensor blindness test
Vsmax≧Vtest ≧ Vsmin
Extra-test proposed by industry
A lane change is commanded
The lane change does not start

## Slide 8
3.5.7.3. Engine start/run cycle test (Phase 1)
Vsmax≧Vtest ≧ Vsmin
Procedure
A new engine start/run cycle
Check ACSF C is default off.

## Slide 9
3.5.7.3. Engine start/run cycle test (Phase 2)
Vsmax≧Vtest ≧ Vsmin
Procedure
Perform phase 1
The driver switches on ACSF C
The driver commands a lane change right after ACSF C switched on  No lane change

## Slide 10
≦48m
≦6m
Rear sensor
ECUs
CAN
CAN monitor
Capture Trigger
Measurement
Capture the sensor data at the timing the rear vehicle is detected
Confirm the actual distance to the rear by using GPS data of both vehicles
Connection of CAN monitor system should be allowed.
Vehicle system under test
vtest + 10 to 50 km/h
A high volume series production passenger car of category M1 AA saloon
Vsmax≧Vtest ≧ Vsmin
3.5.7.3. Engine start/run cycle test (Phase 3)
Procedure
Following the completion of the test phase 2
A vehicle approaches from the rear on the adjacent lane
After the rear coming vehicle entirely passed the test vehicle, the driver commands a lane change.
Test is passed if:
The lane change is performed and
The distance between both vehicles at the time ACSF detects the rear coming vehicle is ≧ 48m