## Slide 1
Japan’s proposal for
GTR2 B2 and B3
7 June 2017
JAPAN AUTOMOBILE STANDARDS INTERNATIONALIZATION CENTER
http://www.jasic.org

## Slide 2
JAPAN proposal
Add Japanese fuel (E0) to the reference fuel of the principal limit value(B2.3.3 ).
Justification:
Japanese fuel is allowed to use as alternative reference fuel in GTR 2 (Annex 2.1, footnote 7).
２．Although E0 fuel has different alcohol concentration from that of E5 fuel (EURO5 fuel), the influence of this difference on exhaust gas is considered to be minimal when expected exhaust gas reduction system is used.
B.2

## Slide 3
JAPAN proposal
Delete the manufacturer declaration value of normal idle CO.
Change the provision of high idle and lambda to CP option.
Justification:
According to the idle values of Japanese two wheelers of JPN 3, the manufacturer declaration value exceeding CO 0.5% is unnecessary.
Since some countries have already legalized these, they are to be options for each CP.
B.3

## Slide 4: Justification for deleting manufacturer declaration value
Values exceeding the average value + 3σ are extremely rare.
The average value + 3σ of idling CO concentration of 42 models is 0.33%.
Therefore, values above the idling CO concentration of 0.5% need not be taken into account.
(σ: standard deviation)