## Slide 1: Tianjin Motorcycle Technical Center
TMTC’s proposal for
GTR2 B3

## Slide 2: GTR 2 B3 3.6
GTR 2 B3 3.6
The type II emission test shall be conducted immediately after the type I emission test. In any event, the engine shall be warmed up until all coolant and lubricant temperatures and lubricant pressure have reached equilibrium at operational levels.
TMTC’s proposals
The type II emission test shall be conducted immediately after the type I emission test. In any event, if Type-II test is required to be conducted independent of Type-I test ， the engine shall be warmed up until all coolant or lubricant temperatures have reached at least 70 °C.

## Slide 3
Justification:
1. The proposal is based on the relative rules of EU 44/2014. : ‘warm-up cycle’ means vehicle operation whereby the coolant temperature rises by at least 22 K from engine start-up to at least 343,2 K (70 °C);
2. Lubricant temperatures of more than 30 motorcycle types in China have been measured after the type I emission test. These data show that the temperatures range over 70 to 100 °C.