## Slide 1: OICA „Certification of automated Vehicles“
Submitted by OICA Document No. ITS/AD-12-11
(12th ITS/AD, 22 June 2017, agenda item 3-4)

## Slide 2
Content
Some basic facts
How can automated operation be regulated?
Initial Proposal
Conceptual Outline
Initial ideas for a new certification system to accommodate AV / software functionalities
Illustration of generic concept
Summary

## Slide 3: Some basic facts
Automated vehicles that can/will also be operated manually (automation switched-off):
  No justification to derogate from currently existing legislation for manual operation
  Automated operation will need to be addressed in addition in order to enable certification
Future years: mix of manually operated/automated/fully autonomous (driverless) vehicles/pods
Fully autonomous vehicles/pods with no possibility of manual operation will still need to meet various pieces of existing legislation (i.e. some crashworthiness requirements, braking performance, …)
  Critical review/adaptation of remaining necessary requirements will be needed in order to adapt, where needed, existing legislation currently applicable to "manual" vehicles
Existing legislation and certification will remain necessary for automated vehicles, when operated manually
Even fully autonomous/driverless vehicles/pods (no manual operation) will for long time need to meet some requirements due to traffic mix  need to evaluate and possibly adapt each regulation
Need to develop additional requirements and certification scheme for automated driving functions (Levels 4 and 5, possibly level 3)

## Slide 4: How can automated operation be REGULATED?
Current legislation is "vertical", i.e. different vehicle aspects/systems covered by different regulations (front impact, side impact, steering, braking, lighting, …)
Automated operation however entails that the vehicle can "replace the driver" and is not a "simple" combination of vertical systems anymore:
 Vehicle must:
  Monitor the driving environment
  Evaluate the situation
  Make decision
  Perform the decision
 Automated functions will entail some "classical" performance requirements to assess the safety of the various components/software/…but this will likely not cover all aspects
Current regulatory system approach likely not able to cover all aspects of automated driving

## Slide 5: Initial Proposal
Focus will be on level [3] / 4 / 5 systems (level 3 is at least partially addressed through UN R79 activities)
Focus on the development of a concept to get automated/autonomous vehicles certified
Introduction of a „technology umbrella“ supported by modules / building blocks, instead of a continuation of an approach for each and every upcoming technology / system

## Slide 6: Conceptual Outline
Assisted driving
(conventional vehicles)
Level 0-2
Conditional automated vehicles Level 3
Pods / high-automation vehicles
Level 4-5
Current certification of systems/components - with modification depending on the automation level
New certification system to accommodate AV / software functionalities

## Slide 7: Initial IDEAS for “New certification system to accommodate AV / software functionalities”
  Basic capability of the vehicle based on test cases that represent well the 4 use cases (parking / urban / interurban / highway)
    Results of OEM internal real world drives etc.
    Desired outcome: Assurance of basic capabilities before further testing
  Assessment of these test cases to be conducted on dedicated test fields (video recording?) or through simulation or other type of demonstration
   Desired outcome: Vehicle is capable of dealing with the typical driving conditions for each use case/domain that a certification is requested for
  Real world test drive (e.g. by a technical service) - Similar to today‘s random „driving test“ lasting 30-60 minutes
   Desired outcome: Targeted at demonstrating how the vehicle generally behaves in traffic and that relevant rules of the road are obeyed
  „Extreme / interesting“ traffic situations: via simulation based on industry pooled data sets
       Desired outcome: understanding how the vehicle reacts under extreme conditions (as safe as a human driver)

## Slide 8: Illustration of the generic concept For „New certification system to accommodate AV / software functionalities“
[3]* When not covered by ACSF

## Slide 9: Summary
The proposed process aims at maintaining the existing certification process, including witness testing and shared responsibility
However, augmenting it with several elements to accommodate AV / software functionalities which
  Introduce a new concept as multiple systems and technologies have to interact and the focus cannot remain on a single component any more
  Suggests a modified release and approval system that takes into consideration the multitude of different traffic scenarios that cannot be described/ tested in the traditional way any more
Suggested test/validation process is expected to be applicable in a type approval as well as in a self certification environment