## Slide 1
Reaction time & Safety time gap
On the public road
Korea Automobile Testing & Research Institute
Automated Driving Research Office
Informal Document - ACSF-15-04

## Slide 2
Configuration of Experimental Vehicle
    Experimental Vehicle Configure
Front Radar
(Delphi)
Front LiDAR (IBEO LUX)
Rear-side LiDAR
(SICK LMS151)
Rear-side Radar
(Delphi)
Micro Autobox
Computer
RT GPS

## Slide 3
Lane Change Data Acquisition
Highway from Seoul to Incheon airport - Total 50km
Highway near Seoul - Total 250km
Triangular merge section
    Experiment Location(highway)
50~110kph
50~100kph
50~100kph
50~100kph

## Slide 4
Safety Region Plot based on driving data
Relative Velocity[km/h]
Clearance[m]
Clearance[m]
Relative Velocity[km/h]
O : LC Start X : LC End

## Slide 5
Reaction time for Lane Change Procedure
    Example of Reaction Time decision
Vehicle moving Start(=LC start)
Target Vehicle deceleration
Reaction
Time
time [sec]
Target velocity[m/s]
Lateral Distance[m]
Srear = dv*tB+ dv²/2abrake + vego*tG

## Slide 6
Reaction time for Lane Change Procedure
Relative Velocity[km/h]
Reaction Time[sec]
→ Average 0.83sec
From 0~10km/h
Min = 0.1sec, Max = 2.2sec
Average = 0.85sec
From 10~20km/h
Min = 0.1sec, Max = 1.9sec
Average = 0.86sec
From 20~30km/h
Min = 0.2sec, Max = 1.5sec
Average = 0.60sec
    Reaction Time distribution
Srear = dv*tB+ dv²/2abrake + vego*tG

## Slide 7
    Example of Safety time gap
Deceleration of braking
ends
time [sec]
Target velocity[m/s]
Lateral Distance[m]
Safety time gap for Lane Change
Srear = dv*tB+ dv²/2abrake + vego*tG

## Slide 8
Safety time gap for Lane Change
    Safety time gap at the end of deceleration
Relative Velocity[km/h]
Safety time gap[sec]
→ Average 0.95sec
From 0~10km/h
Min = 0.49sec, Max = 2.41sec
Average = 1.03sec
From 10~20km/h
Min = 0.48sec, Max = 1.86sec
Average = 0.88sec
From 20~30km/h
Min = 0.51sec, Max = 1.14sec
Average = 0.87sec
Srear = dv*tB+ dv²/2abrake + vego*tG