Proposal for Addendum ХХ to UN Regulation No. 48 including 05 series of amendments

| The following text was prepared by experts of the Russian Federation with the purpose of editorial amendment of separate Regulation paragraphs in order to exclude the ambiguous interpretation of some of their conditions. Amendments to the existing text of the Regulation are in bold (with an additional yellow highlighting). The text to be deleted is marked with a strikethrough (with an additional blue highlighting). |
| --- |
| I. | Proposal |
|  | Paragraph 5.11.1.3 to read as follows: |
|  | 5.11.1.3 | When light signalling system operates according to 6.2.7.6.2. the position lights operate simultaneously with the daytime running lights. In that case, at least rear position lights shall be switched ON; either |
|  | Paragraph 5.11.2 to renumber as 5.11.1.4 |
|  | Paragraph 5.11.3 to renumber as 5.11.2 |
|  | Paragraph 6.2.7.5 to read as follows: |
|  | 6.2.7.5 | Dipped-beam headlamps may be switched ON or and OFF automatically. However, it shall be always possible to switch these dipped-beam headlamps ON and OFF manually. |
|  | Paragraph 6.2.7.6 to read as follows: |
|  | 6.2.7.6 | If daytime running lamps are present and operate according to paragraph 6.19., If there is an automatic dipped-beam headlamps on/off system: |
|  | Paragraph 6.2.7.6.1 to read as follows: |
|  | 6.2.7.6.1 | If the automatic switching mode of dipped-beam headlamps is activated the dipped-beam headlamps shall be switched ON and OFF automatically depending on the ambient light conditions (e.g. switch ON during night time driving conditions, tunnels, etc.) according to the requirements of Annex 13.; or |
|  | Paragraph 6.2.7.6.2 to delete: |
|  | 6.2.7.6.2 | Daytime running lamps operate in conjunction with the lamps listed in paragraph 5.11. where, as a minimum requirement, at least the rear position lamps shall be activated; or |
|  | Paragraph 6.2.7.6.3 to renumber and to read as follows: |
|  | 6.2.7.6.3 6.2.7.6.2 | If the automatic switching mode of dipped-beam headlamps is deactivated the distinctive means are provided to inform the driver that the headlamps, position lamps and if so equipped end outline marker lamps and side marker lamps are not illuminated. Such means are: |
|  | Paragraph 6.2.7.6.3.1 to renumber as 6.2.7.6.2.1 |

|  | Paragraph 6.2.7.6.3.2 to delete: |
| --- | --- |
|  | 6.2.7.6.3.2 | Non-illuminated indicators and identification of hand controls that are required by Regulation No. 121 to be illuminated when the headlamps are activated; or |
|  | Paragraph 6.2.7.6.3.3 to renumber as 6.2.7.6.2.2 and to read as follows: |
|  | 6.2.7.6.3.3 6.2.7.6.2.2 | A tell-tale visual, auditory or both, shall be activated only in reduced ambient lighting conditions as defined in Annex 13 to inform the driver that the dipped-beam headlamps should be switched ON. Once the tell-tale is activated, it shall only be extinguished switched off when the dipped-beam headlamps have been switched on or the device which starts and/or stops the engine (propulsion system) is set in a position which makes it impossible for the engine (propulsion system) to operate. |
|  | Paragraph 6.2.7.7 to read as follows: |
|  | 6.2.7.7 | Without prejudice to paragraph in addition to factors, listed in paragraph 6.2.7.6.1., the dipped-beam headlamps may switch ON and OFF automatically relative to other factors such as time or ambient conditions (e.g. time of the day, vehicle location, rain, fog, etc.) |
|  | Paragraph 6.9.7 to read as follows: … However, if a front position lamp is reciprocally incorporated with a direction-indicator the electrical connection of the front position lamp on the relevant side of the vehicle or the reciprocally incorporated part of it may be such that it is switched off during the entire period (both ON and OFF cycle) of activation of the direction-indicator lamp. If the front position lamps are reciprocally incorporated with the daytime running lamps the electrical connection may be such that the front position lamps are switched off for the entire period (both ON and OFF cycle) of activation of the daytime running lamps. |
|  | Paragraph 6.9.8 to read as follows: |
|  | 6.9.8 | Tell-tale |
|  |  | Circuit-closed tell-tale mandatory. This tell-tale shall be non-flashing and shall not be required if the instrument panel lighting can only be turned on simultaneously with the front position lamps. |
|  |  | This requirement does not apply when light signalling system operates according to paragraph 6.2.7.6.2 5.11.1.3. |
|  | Paragraph 6.10.7 to read as follows: … However, if a rear position lamp is reciprocally incorporated with a direction indicator, the electrical connection of the rear position lamp on the relevant side of the vehicle or the reciprocally incorporated part of it may be such that it is switched OFF during the entire period (both ON and OFF cycle) of activation of the direction-indicator lamp. If the rear position lamps are reciprocally incorporated with stop lamps or fog-lamps electrical connection may be such that the rear position lamps are switched off for the entire period (both ON and OFF cycle) of activation of mentioned above lamps. |
|  | Paragraph 6.10.8 to read as follows: |
|  | 6.10.8 | Tell-tale |
|  |  | Circuit-closed tell-tale mandatory. It shall be combined with that of the front position lamps. |
|  |  | This requirement does not apply when light signalling system operates according to paragraph 6.2.7.6.2 5.11.1.3. |
|  | Paragraph 6.19.7.1.3 to read as follows: |
|  | 6.19.7.1.3 | Prior to the vehicle being set in motion for the first time, after each manual activation of the engine (propulsion system). |
|  | Paragraph 6.19.7.3 to read as follows: |
|  | 6.19.7.3 | The daytime running lamp shall switch OFF automatically when the device which starts and/or stops the engine (propulsion system) is set in a position which makes it impossible for the engine (propulsion system) to operate or the front fog lamps or headlamps are switched ON, except when the latter are used to give intermittent luminous warnings at short intervals15. When the front fog lamps or headlamps are switched off, the daytime running lights must automatically turn on. |
|  | Footnote «15» to delete: |
|  | 15 | New vehicle types which do not comply with this provision may continue to be approved until 18 months after the entry into force of Supplement 4 to the 03 series of amendments. |
|  | Paragraph 6.19.7.4 to delete: |
|  | 6.19.7.4 | The lamps referred to in paragraph 5.11. may be switched ON when the daytime running lamps are switched ON, except if daytime running lamps are operating according to paragraph 6.2.7.6.2., where at least the rear position lamps shall be activated. |
|  | Paragraph 6.19.7.5 to renumber as 6.19.7.4 |
|  | Paragraph 6.19.7.6 to renumber as 6.19.7.5 |
|  | Paragraph 6.22.4.1.2 to read as follows: |
|  | 6.22.4.1.2 | Additional lighting units, if any, on either side of the vehicle shall be positioned at a distance not exceeding 140 mm1615 in horizontal direction… |
|  | Footnote «16», to renumber as: |
|  | 16 15 | In case of additional "two symmetrically placed lighting units" ... |
|  | Paragraph 6.22.7.4.3 to read as follows: |
|  | 6.22.7.4.3 | ... a) The road characteristics correspond to motorway conditions 1716 ... |
|  | Footnote «17», to renumber as: |
|  | 17 16 | Traffic directions being separated by means of road construction ... |
|  | Paragraph 6.22.7.4.5 to read as follows: |
|  | 6.22.7.4.5 | ... i) A horizontal movement of the asymmetric cut-off side-wards from the longitudinal axis of the vehicle, if any, is allowed only when the vehicle is in forward motion 1817 and shall be such that ... |
|  | Footnote «18», to renumber as: |
|  | 18 17 | This provision does not apply for passing beam lighting when ... |
|  | Paragraph 6.22.9.1 to read as follows: |
|  | 6.22.9.1 | An AFS shall be permitted only in conjunction with the installation of headlamp cleaning device(s) according to Regulation No. 451918, for at least ... |

|  | Footnote «19», to renumber as: |
| --- | --- |
|  | 1918 | Contracting Parties ... |
|  | Paragraph 12.17 to read as follows: |
|  | 12.17 | Paragraph 6.19.7.3 6.19.7.5 comes into force 30 months for new types of vehicles of categories M1 and N1 and 48 months for new types of vehicles of other categories after the date of entry into force of the 04 series of amendments. |
|  | Paragraph 12.22 to read as follows: |
|  | 12.22 | … shall grant approvals only if the vehicle type to be approved meets the requirements of this Regulation as amended by the 05 series of amendments. However, as from 66 months for new vehicles types of categories M1 and N1 and 84 months for new vehicle types of other categories after the official date of entry into force of the 05 series of amendments to this Regulation, Contracting Parties applying this Regulation shall grant approvals only if the new vehicle type to be approved meet the requirements of this Regulation as amended by the 05 series of amendments excluding paragraphs 6.2.7.6.2. and 6.2.7.6.3. to 6.2.7.6.3.3. Existing approvals … |
| II. | Justification (comments) |
| 1. | For paragraph 5.11.1.3 The algorithm for the joint operation of the lights in accordance with paragraph 5.11 and headlamps (paragraph 6.2.) is defined in paragraph 5.12. The condition of paragraph 5.11.1.3 concerns only the algorithm of simultaneous operation of the lights under paragraph 5.11 with the DRL under item 6.19 and in this case the reference to 6.2.7.6.2 is completely inappropriate. Along with the change of this paragraph the amendment of paragraph 6.19.7.4 is provided. The proposed amendment is aimed at eliminating the error and excluding the incorrect interpretation of the Regulation requirements. |
| 2. | For paragraph 5.11.2 (former) Change in numbering is due to the fact that the condition in paragraph 5.11.2 (former) is not independent, but is, in fact, a continuation of the listing of the exceptions set out in paragraph 5.11.1. |
| 3. | For paragraph 5.11.3 (former) Change in numbering is due to changing the numbering of the above paragraphs. |
| 4. | For paragraph 6.2.7.5 The amendment is aimed at excluding the possibility of the ambiguous interpretation of this condition and the correct use of the conjunction "and" instead of the alternative conjunction "or". There is no need to divide a single process into two components - automatic switching or automatic shutdown. |
| 5. | For paragraph 6.2.7.6 The deletion of the existing text is due to the fact that the automatic operation of headlamps referred to in paragraph 6.2.7.6.1. below, is in no way related to the presence (or absence) of daytime running lights in the vehicle. Instead of the existing text a direct indication of the presence of the automatic headlamp on / off system in the vehicle is made. [In general, the terms "manual on/off" and "automatic on/off" are used in the text of the Regulation, but in fact there are the following modes of switching on/off lighting devices: - manual (directly by the driver of the vehicle) switching on/off the dipped beam/main beam lights and other devices; - automatic (without driver’s intervention) switching on/off the dipped beam/main beam lights and other devices; - manual (directly by the driver of the vehicle) switching on/off (activation/deactivation) of the automatic control mode of switching on/off the headlamps (automatic light); Perhaps, for the purpose of unambiguous interpretation (understanding) of the described actions, it is necessary to develop terms and definitions related to the indicated modes of switching on lighting devices and introduce them into Section 2 "Definitions" of the Regulation] |
| 6. | For paragraph 6.2.7.6.1 An additional clarification for the automatic dipped beam lights on/off system is introduced to this paragraph. |
| 7. | For paragraph 6.2.7.6.2 The deletion of the existing text is due to the fact the algorithm for joint operation of functions (PL and DRL) not directly related to headlights is described. It is more logical and appropriate to take this condition into account in paragraph 5.11.1.3. |
| 8. | For paragraph 6.2.7.6.3 (former) An additional clarification for the condition of the automatic dipped beam lights on/off system is introduced to this paragraph. At the same time, the item numbering is changed to 6.2.7.6.2. |
| 9. | For paragraph 6.2.7.6.3.1 The change in numbering to 6.2.7.6.2.1 is due to the change in the numbering of the paragraph above. |
| 10. | For paragraph 6.2.7.6.3.2 (former) The deletion of the paragraph is due to the fact that it refers to the condition "headlamps are activated", and paragraph 6.2.7.6.2. (new) refers to the condition "headlamps are deactivated". This avoids contradictions in the requirements. |
| 11. | For paragraph 6.2.7.6.3.3 The change in numbering to 6.2.7.6.2.2 is due to the change in the numbering of the paragraph above. The word “extinguish” is not applicable to the sound signal. |
| 12. | For paragraph 6.2.7.7 Editorial correction of the text. |
| 13. | For paragraph 6.9.7 The amendment is aimed at increasing the longevity of lamps, reducing environmental pollution and fuel consumption. In the case of reciprocally incorporated lamps, the temporary disabling of the marker lamps does not affect the safety of traffic. This amendment is similar, in its essence, the condition under paragraph 5.11.1.3. |
| 14. | For paragraph 6.9.8 A footnote to paragraph 5.11.1.3 is introduced due to the amendment of paragraph 6.2.7.6.2. |
| 15. | For paragraph 6.10.7 The amendment is aimed at increasing the longevity of lamps, reducing environmental pollution and fuel consumption. In the case of reciprocally incorporated lamps, the temporary disabling of the marker lamps does not affect the safety of traffic. |
| 16. | For paragraph 6.10.8 A footnote to paragraph 5.11.1.3 is introduced due to the amendment of paragraph 6.2.7.6.2. |
| 17. | For paragraph 6.19.7.1.3 The amendment is aimed at simplifying the text and eliminating the possibility of its ambiguous interpretation. |
| 18. | For paragraph 6.19.7.3 The amendment is aimed at introducing an additional clarification for the DRL operation algorithm when the headlamps are switched off. The introduction of the reference to footnote "15" is due to the fact that the effect of the condition on this footnote ended on 11.01.2010, a year before the entry into force of the 05 series of amendments. |
| 19. | For footnote «15» The condition in footnote "15" allowed other ways to switch off the daytime running lights only for a limited period. The allowed period (18 months) expired on January 11, 2010. The existence of this footnote is relevant only in the text of UN Regulation No. 48, as amended by 04 series of amendments. UN Regulations No. 48, as amended by 05 series, entered into force on January 30, 2011, that is, almost a year after the expiry of footnote "15". Consequently, all vehicles designed under requirements of UN Regulation No. 48, as amended by 05 series (and especially 06), must unambiguously comply with the requirements of 6.19.7.3. Without any reservations. |
| 20. | For paragraph 6.19.7.4 The deletion of this paragraph is aimed at ensuring unambiguous interpretation of the Regulation requirements. The existence of this paragraph in UN Regulation No. 48 was initially meaningless (as from Rev.1/Add.47/Rev.5/Amend.2), since the admissibility of other ways to turn off DRL was provided for in the footnote (currently "15"), which was in effect only for a limited period of time (from 11.07.2008 to 11.01.2010). The wording of paragraph 6.19.7.4 from the moment of its introduction is interpreted by many people as non-possibility of simultaneous functioning of DRL and lights according to paragraph 5.11. At the same time, at an illumination level in the range of 1000 to 7000 lux and switched off headlamps (see Annex 13), it may occur that the driver deems it necessary and sufficient to switch on the position lamps, not switching the headlamps. For example, in conditions of insufficient (in driver’s opinion) rear visibility of the vehicle, such a decision would be absolutely justified. |
| 21. | For paragraphs 6.19.7.5 (former), 6.19.7.6 (former) Change in numbering is due to the change in numbering of the paragraphs above. |
| 22. | For paragraphs 6.22.4.1.2, 6.22.7.4.3, 6.22.7.4.5, 6.22.9.1 Change in numbering is due to the deletion of footnote “15”. |
| 23. | For footnotes «16» (former), 17 (former), 18 (former), 19 (former) Change in numbering is due to the deletion of footnote “15”. |
| 24. | For paragraph 12.17 The amendment is aimed at eliminating the error in the numbering of the paragraph resulting from the development of E/ECE/TRANS/505/Rev.1/Add.47/Rev.6/Amend.4, when the numbering of 6.19.7.3 changed to 6.19.7.6. |
| 25. | For paragraph 12.22 The existing version of paragraph 12.22 divides UN Regulation No. 48 into two parts. One of is valid until July 30, 2016, and the second part is valid from July 30, 2016. Wherein, a termination of a number of requirements is involved. These requirements cannot be excluded. At the same time, 06 series of amendments also contains transitional provisions with respect to 05 series of amendments. And in this case the effect of completely different paragraphs is terminated. As a result, there is an insoluble contradiction between the two documents. The amendment is aimed at eliminating the contradictions that have arisen and it must be considered together with the proposed amendments to paragraphs 5.11.1.3, 6.2.7.6 and 6.19.7 above. |