## Slide 1
Action item 4 : ETRTO will make a proposal on the relationship between the test pressure used in each GTR test and the test pressures stamped on the sidewall as per 3.3.5 and 2.56.
Informal Working Group Tyre GTR
Session 17, Brussels Nov 2nd-3th
TYREGTR-17-07
Agenda item 4.1

## Slide 2
2. Definitions
2.56. "PSI index" is a code identifying the inflation pressure which may be used during
testing of tyres as shown in Annex 4;
3.0 Requirements
3.3. Other Sidewall markings
3.3.5. In the case of LT or C type tyres, the maximum load rating and corresponding inflation
pressure of the tyre, shown as follows: "Max load single ___kg (___lb) at ___kPa (___psi) cold"; "Max load dual ___kg (___lb) at ___kPa (___psi) cold". For LT and C type tyres rated for single fitment only, mark as follows: "Max load ___kg (___lb) at ___kPa (___psi) cold".
3.3.11. In the case of LT or C type tyres, an indication, by the "PSI" index, of the
inflation pressure to be adopted for the load/speed endurance tests. A table showing
the relationship among "PSI" and "kPa" units is listed in Annex 4.
Global technical regulation No. 16, Amendment 1, ECE/TRANS/180/Add.16/Amend.1

## Slide 3: Background FMVSS vs ECE Reg 54
FMVSS 139 - Tire markings
S5.5 … each tire must be marked … with …
(c) The maximum permissible inflation pressure, subject to the limitations of S5.5.4 through S5.5.6 of this standard;
(d) The maximum load rating and for LT tires, the letter designating the tire load range;
S5.5.6 For LT tires, the maximum permissible inflation pressure shown must be the inflation pressure that corresponds to the maximum load of the tire for the tire size as specified in one of the publications described in S4.1.1.(b) of §571.139…
UN-ECE Reg 54 Rev 3. amdt 3. – Tire markings
  An indication, by the "PSI" index, of the inflation pressure to be adopted for the load/speed endurance tests. For tyres first approved after 1 January 2018, the Inflation pressure for the dimension measurement and for the load/speed endurance test, pursuant to paragraph 4.1.12. of this Regulation, shall be indicated in kilopascals, replacing the "PSI" index.
A pressure to carry the load
A test pressure
“Current”
≠
“Future”

## Slide 4: Regulation ECE R54 and FMVSS requirement
FMVSS-119 |  | ECE-R54
Defined as the Inflation Pressure corresponding to the maximum load rating marked on the tire; IT IS ALSO the FMVSS 119 endurance test inflation pressure | Regulatory test pressure | Manufacturer’s decision;
Inflation Pressure associated with the maximum load rating | Pressure Marking | Test pressure
Maximum Load Rating to be not less than the lowest of the published standards | Link with Industry standards | THEORETICALLY: No linkage required; IN PRACTICE: Usually equals the inflation pressure prescribed by a standards organization
Test Condition
UN- ECE 54
Defined by the regulation
Manufacturer’s decision
Tyre Manufacturer is Responsible for the definition of the ECE54 test pressure,
which is usually aligned with the industry standards
Industry Standards
Tire Stamping
Test Conditions
FMVSS 139
US CFR
Title 49
Transportation

## Slide 5: Industry proposal, ECE R54 Test inflation pressure
Industry Standards
Tire Stamping
Test Conditions
Defined by the regulation
Manufacturer’s decision
Link test inflation to the tyre load carrying capacity
Proposal:
2.56 Reference Test Inflation Pressure applicable for LT/C tyres is the minimum cold inflation pressure for the maximum load carrying capacity of the tyre. [for single application]

## Slide 6
Remaining issue: Tire Marking
Option 1: keep in the Technical Prescription the two markings and CP’s to decide which one(s) they want to implement
  3.0 Requirements
  3.3. Other Sidewall markings
  3.3.5. In the case of LT or C type tyres, the maximum load rating and corresponding inflation
  pressure of the tyre, shown as follows: "Max load single ___kg (___lb) at ___kPa (___psi) cold"; "Max load dual ___kg (___lb) at ___kPa (___psi) cold". For LT and C type tyres rated for single fitment only, mark as follows: "Max load ___kg (___lb) at ___kPa (___psi) cold".
  3.3.11. In the case of LT or C type tyres, an indication, by the "PSI" index, of the
  inflation pressure to be adopted for the load/speed endurance tests. A table showing
  the relationship among "PSI" and "kPa" units is listed in Annex 4.
Option 2: Harmonize the markings

## Slide 7
ETRTO Standard, CP tyres (tyres on 5 deg drop-centre rims for motorcaravans – Radial), vehicle fitment:
“On rear axles in single fitment increase the inflation pressure by 75kPa with no increase of the maximum load capacity”
  FMVSS 139 S5.5 Tire markings (c) The maximum permissible inflation pressure, subject to the limitations of S5.5.4 through S5.5.6 of this standard;
  (d) The maximum load rating and for LT tires, the letter designating the tire load range;
  S5.5.6 For LT tires, the maximum permissible inflation pressure shown must be the inflation pressure that corresponds to the maximum load of the tire for the tire size as specified in one of the publications described in S4.1.1.(b) of §571.139. At the manufacturer's option, the shown inflation pressure may be as much as 10 psi (69 kPa) greater than the inflation pressure corresponding to the specified maximum load.
Increase in Inflation pressure required for specific applications should not result in testing tires at higher Inflation Pressure
The maximum inflation pressure as per FMVSS139 S5.5 (c) and S5.5.6 are in the sense of ETRTO minimum inflation pressures that can/must be raised in specific cases like CP on rear axle.

## Slide 8
Tyre Industry is asking for some more time to further work out a proposal for the tyre Sidewall marking regarding the Reference Test Inflation Pressure in relation to the