## Slide 1: GRSG/VRU-Proxi Informal Working Group Japan Proposals for Technical Requirements on Sonars November 21th 2017 Tokyo

## Slide 2: Table of Contents
Basic Ideas for Developing Technical Requirements on Sonars under GRSG
Proposals for Technical Requirements on Sonar system for VRUs detection

## Slide 3: 1. Basic Ideas for Developing Technical Requirements on Sonars under GRSG
ISO 17386 (MALSO(*)) is a technical requirements on sonar system.
As ISO 17386 is aimed for assisting driver to understand the distance to various objects, such as wall, thin pole, luggage carrier of truck, etc. in parking scene , some modification is necessary for the purpose of VRUs detection.
Our proposal is to make new requirement based for the purpose of VRUs detection by modifying ISO 17386.
*: MALSO: Maneuvering Aids for Low Speed Operation

## Slide 4: Reference: ISO 17386 MALSO
○Outline of ISO 17386
  Requirements on sonars and other sensing technologies
  Detection areas: Front, rear, corner
   Requirements specified for each area (detection area, response time, etc.)
  Main rearward detection requirements
    Detection area: 1 m max. in the rear
    Detection area requirement:
    The area shall be divided into 0.1 x 0.1 m grids and a target (φ75 mm, H 1000 mm) shall be located there. Testing shall determine whether or not each grid can be detected.
    Detection latency:
    The detection latency standard for when the target appears within the area is also specified.
Vehicle
0.6 m
1 m
Image of a test in the rear horizontal area
Detection areas
Rear
Corner
Front
Detected
Not Detected
Target

## Slide 5: 2. Proposals for Technical Requirements on Sonars
ISO 17386 (Clause 5) |  | Issue, etc. | Proposals for technical requirements on sonar system for VRUs detection
5.1 System activation |  | The automatic activation requirement is unnecessary except for reversing. | Delete provisions except those related to reversing.
5.2 Driver interface and information strategy |  | - | (As per ISO’s requirements)
5.3 Dynamic performance of object detection | 5.3.1 Relative velocity of objects | - | (As per ISO’s requirements)
 | 5.3.2 Start-up detection delay | - | Add definition.
 | 5.3.3 Detection latency | The specified test procedures are not appropriate (unrealistic situation for VRUs detection). | Newly specify realistic test procedures.
 |  | The average detection latency requirement is unnecessary (because its purpose is to ensure merchantability). | Delete the average detection latency requirement.
5.4 Monitoring range coverage | 5.4.1 Sections of the monitoring range | Two sections of the rear detection area (0.6 m or 1 m) | Choose the 1-m section.
 | 5.4.2 Horizontal areas of relevance | This clause is unnecessary for VRUs detection (with many items that are redundant with Clause 5.4.3). | Delete (and incorporate into Clause 5.4.3).
 | 5.4.3 Rear horizontal area | - | (Use Clause 7 for test procedures.)
 | 5.4.4 Front horizontal area | This requirement is unnecessary for VRUs detection (because it concerns areas other than the rear field of vision). | Delete.
 | 5.4.5 Corner horizontal areas | This requirement is unnecessary for VRUs detection (because it concerns areas other than the rear field of vision and its purpose is to avoid property damage). | Delete.
 | 5.4.6 Minimum coverage ratios | The requirement "no more than two contiguous detection holes" needs to be modified for VRUs detection. | Relax the requirement to the size equivalent to that of a person.
 | 5.4.7 Vertical areas of relevance | This requirement is unnecessary for VRUs detection (because its purpose is to avoid property damage) . | Delete.
5.5 Self-test capabilities and failure indication |  | - | (As per ISO’s requirements)
5.6 Operation with trailers |  | - | (As per ISO’s requirements)
(See 2.1)
(See 2.2.)
(See 2.3.)
Modification points of ISO17386 for the purpose of VRUs detection

## Slide 6: 2.1. Detection Latency Test Procedures
(1) ISO 17386
The target is dropped from a height of 1 m and the response time is measured (video camera image  audible warning).
A situation where the detection target is landing from above is unrealistic for VRUs detection
Video camera
Target
System warning height
Audible warning system
Microphone
Detection area
Dropped from a height of 1 m
Microphone
Recording

## Slide 7: (2) Proposal for the response time measurement
The system response time should be measured with the time duration from selecting the reverse gear to the warning activation for a stationary target placed in valuation area.
Video camera
Target
Audible warning system
Microphone
Detection area
having been placed within the area in advance
Microphone
Recording
Gearshift
Filming the gearshift lever operation and recording the audible warning

## Slide 8: 2.2. Minimum Coverage Ratios
(1) ISO17386
ISO’s requirement “there shall be no more than two contiguous detection holes”(*1) is to avoid property damage by thin object such as pole.
(2)Proposal for minimum coverage
It is sufficient if the target covers grids equivalent to the size of a person for VRUs detection.
Change to “no more than 2 x 2 undetected grids” which considered as equivalent to the size of a pedestrian.
*1: Within the whole monitoring range, there shall be no more than two contiguous detection holes in a straight line, either horizontally, vertically or diagonally in the horizontal plane.
*2: VRU-Proxi-02-03
0.1 m
0.1 m
ISO’s requirement
(No more than two contiguous detection holes)
Proposal: No more than 2 × 2 undetected grids
Target in the field of vision requirement:
φ300 mm
Image of the undetected grids requirement
Detected
Not Detected

## Slide 9: 2.3. Vertical Range Requirement
(1)ISO 17386
Vertical range requirement (see below) is defined to avoid property damage by various object, such as luggage carrier of truck.
(2)Proposal
Delete vertical range test
0.8 m
Target in the proposed field of vision requirement
(H 1000 mm)
0.2 m
0.1 m
1 m
ISO’s target

## Slide 10: Supplementary Information

## Slide 11: Reference: Reversing Speed Models Studied by ISO
Source: The Commentary section of “JIS D 0803：0000 (ISO 17386：2010) Transport information and control systems - Manoeuvring Aids for Low Speed Operation (MALSO) - Performance requirements and test procedures”
Speed at which the vehicle is 1 m from the object in the rear
Speed (m/s)
Model of speeds used by the driver
Simplified model of speeds used by the driver
Distance to the object (m)