## Slide 1: TC22 SC37 WG3 Liaison Report for EVS-GTR Thermal Propagation Work Item
            Dr. Annika Ahlberg Tidblad (SE)
            Brian J. Lawrence (UK)
Sep-2017

## Slide 2: Introduction
AAT & BJL attended two TC22 SC37 WG3 meetings on Thermal Propagation since EVS 14th session:
  9 & 10-Mar-2017, Okinawa
  29 & 30-Aug-2017, Dresden
7 national standards organisations represented:
  China (CN), France (FR), Germany (DE), Japan (JP), South Korea (KR), Sweden (SE) and UK
Timeframe, title & scope of work item agreed in Okinawa:
  3-year project envisaged
  Title:
  ISO 6469-1:2007/Amd 1: Electrically propelled road vehicles – Safety specification – Part 1: On-board rechargeable energy storage system (RESS) Amendment 1 Safety management of thermal runaway propagation
  Scope:
  This amendment specifies demonstration methods for thermal runaway risk mitigation in case of a cell internal failure within a battery system/battery pack. The focus is on protection of persons against direct exposure to possible risk caused by such failure.
  The amendment applies to lithium ion battery packs and systems used for propulsion of electric vehicles. It also describes associated data and the methods to collect them.

## Slide 3: National Proposals for Work Content (ISO 6469-1 Amendment)
Range of national proposals presented and reviewed during Dresden meeting:
  Shared focus between…. (a) Development of fit-for-purpose test method and… (b) Support for “documented approach” (framework)
  Both objectives accommodated in Dresden meeting outcome
Several common themes:
  Repeatability and reproducibility of any method must be assessed and accepted (general agreement)
  Pre-test manipulation of DUT must be minimised (different views as to level of acceptability – to be resolved)
    Drilled holes, disabling of safety devices, attached cables or trigger mechanisms, special test software, etc. OR
    Custom-built REESS for test, incl. in-cell implanted device for remote controlled internal short circuit
  Different trigger mechanisms proposed:
    Heating (electric or chemical), overcharge, nail penetration, external short circuit
  Conflicting views on whether trigger should necessarily force thermal runaway (regardless of real world form)
    Several advocates on each side of the argument

## Slide 4: Next Steps….
Validation and commenting on proposed evaluation scheme for trigger methods
  See Annex 1. (from DE proposal)
Draft standard/guideline with basic content for “documented approach”
  Including functional descriptions and risk assessment inventory
Next meetings:
  10-11 Jan-2018 (UK, SE, FR or DE tbd)
  19-20 Mar-2018, Ningde, China

## Slide 5: Annex.1 Initiation methods for single cell thermal runaway inside a battery pack
Trigger |  | Description | Reliability | Reprodu-cibility | Pack modifi-cation | Useable for different |  |  | Additional Energy | Shipment of cell/DUT | Mani-pulation proof | Remark | 
 |  |  |  |  |  | Type: any | Pos.: any | Pos.: edge |  |  |  |  | 
Internal Short | Internal short seed | Insertion of a defined defect into the cell which can be triggered by moderate heating/cycling | Good | Good | None | Yes | Yes |  | None | No (cell and pack) | High | Proprietary (NASA). Modification on cell. Cannot be done by OEM. Limited experience. | 
External Short |  | Shortening of a single cell inside the battery | Low | Good | High | Yes | Yes |  | None | Yes | Medium | Most cells will not enter TR | 
Nail Penetration | Mild steel nail | Penetration of cells perpendicular or parallel to electrodes to produce an internal short | Medium | Low | Medium | Yes | No |  | None | Yes | Medium | Generally considered to be over-hard Not suitable for any position | 
 |  |  | Medium | Low | Medium | Yes |  | Yes | None | Yes | Medium |  | 
 | Metal tip ceramic or metal-coated nail |  | Medium | Low | Medium | Yes | No |  | None | Yes | Medium | Limited experience Not suitable for any position | 
 |  |  | Medium | Low | Medium | Yes |  | Yes | None | Yes | Medium |  | 
Over-heating | Heating plate (el.) | Heating device (resistive) is built inside battery to heat single cell | Good | Good | High | No | Yes |  | Yes > 50% | Yes | High | Battery is heated up by device to a higher temperature. | 
 | Heating plate (el.) cell replacement | Heating device (resistive) mimics thermal runaway of a single cell | Good | Good | High | Yes | Yes |  | Yes < 20% | Yes | High | No experience. Slow heating, entire battery heated up. | 
 | Shock heater (el.) | Fast heater built inside battery to heat single cell | Good | Good | Medium | Yes | No |  | Yes < 20% | Yes | High | Proprietary (NRC). Limited experience | 
 |  |  | Good | Good | Medium | Yes |  | Yes |  | Yes | High |  | 
 | Laser | Laser heating of single cell | Medium | Good | Medium | Yes | No |  | None < 1% | Yes | High | Limited experience Not suitable for any position | 
 |  |  |  |  | Medium | Yes |  | Yes |  |  |  |  | 
 | Chemical heating cell replacement | Cell is replaced by a dummy cell with chemical charge (e.g. Thermite, electrolyte and oxidizer) | Good | Good | Medium/High | Yes | Yes |  | None | Yes | High | No experience, new idea | 
Overcharge |  | One single cell is overcharged | Medium | Good | High | Yes | No |  | Yes > 50% | Yes | Medium | Additional energy inserted. | 
 |  |  | Medium | Good | High | Yes |  | Yes |  | Yes | Medium |  | 
! Tests, which cannot be performed on pack level without triggering several cells are excluded. E.g.: cell crush, nickel J …