## Slide 1
Japan’s proposal for
GTR2 B2
17-18 Oct 2017
JAPAN AUTOMOBILE STANDARDS INTERNATIONALIZATION CENTER
http://www.jasic.org

## Slide 2
Japan proposed to add E0 to the reference fuel of the principal limit value (EPPR-20-2) and justification was required by means of indicating the gap between E0 and E5.
Followings are the result of the test.
Item |  | A | B | C | D
WMTC Category |  | Class1 | Class2 | Class3 | Class3
Vehicle weight | kg | 114 | 188 | 182 | 193
Equivalent inertia mass | kg | ISO 190 | ISO 260 | ISO 260 | ISO 270
Engine type |  | Water-cooled,4Stroke | Water-cooled,4Stroke | Water-cooled,4Stroke | Water-cooled,4Stroke
Emission control |  | Catalyst、O2S | Catalyst、O2S、AI | Catalyst、O2S | Catalyst、O2S、AI
Disuplacement | cc | 124 | 248 | 689 | 649
Max.power | kW/rpm | 8.3/8500 | 18/8000 | 54/9000 | 50/8,000
Max.torque | N-m/rpm | 11/5000 | 22/6500 | 68/6500 | 65/6,500
Idling speed |  | 1700rpm | 1400rpm | 1350rpm | 1300rpm
Fuel supply |  | FI | FI | FI | FI
Transmission |  | CVT | Manual | Manual | Manual
Vehicles for the test
Purpose

## Slide 3
As a result, the examination of E0 and E5 fuel are considered equivalent
Chart: CO [mg/km]
| 353 | 492 | 470 | 312.60000000000002
 | 323 | 489 | 449 | 298
Chart: THC [mg/km]
| 111 | 93 | 106 | 57.8
 | 114 | 89 | 105 | 60.1
Chart: NOx [mg/km]
| 27 | 31 | 11 | 27.1
 | 28 | 31 | 11 | 30.3
■ Vehicle A ◆Vehicle B ▲Vehicle C ● Vehicle D
Test result

## Slide 4
Conclusion
The result of the measurements of E0 fuel and E5 fuel are equivalent.
Therefore, it is justified to add E0 fuel to the principal fuel.
E5 fuel property |  | Limits | 
Parameter | Unit | Minimum | Maximum
Research octane number, RON |  | 95 | 
Motor octane number |  | 85 | 
Density at 15 ℃ | kg/m3 | 743 | 756
Vapor pressure | Kpa | 56 | 60
Water content | % v/v |  | 0.015
Distillation |  |  | 
Evaporated at 70 ℃ | % v/v | 24 | 44
Evaporated at 100 ℃ | % v/v | 48 | 60
Evaporated at 150 ℃ | % v/v | 82 | 90
Final boiling point | ℃ | 190 | 210
Residue | % v/v |  | 2
Hydrocarbon analysis |  |  | 
Olefins | % v/v | 3 | 13
Aromatics | % v/v | 29 | 35
Benzene | % v/v |  | 1
Saturates | % v/v | report | 
Carbon/hydrogen ratio |  | report | 
Carbon/oxygen ratio |  | report | 
Induction period | minutes | 480 | 
Oxygen content | % v/v | report | 
Existent gum | mg/ml |  | 0.04
Sulphur content | mg/kg |  | 10
Copper corrosion |  |  | class 1
Lead content | mg/l |  | 5
Phosphorus content | mg/l |  | 1.3
Ethanol | % v/v | 4.7 | 5.3
E0 fuel property | Limits | 
 | regular | premium
Lead content | Not to be detected | 
Sulphur content | 10wt ppm or less | 
Aromatics | 20～45%vol | 
Olefins | 15～25vol% | 
Benzene | 1% vol or less | 
Oxygen concentration | Not to be detected | 
MTBE | Not to be detected | 
Methanol | Not to be detected | 
Ethanol | Not to be detected | 
Existent gum | 5mg/100ml or less | 
Kerosene | Not to be detected | 
Octane number RON | 90～92 | 99～101
Octane number MON | 80～82 | 86～88
Density | 0.72～0.77g/cm3 | 
Fractional distillation properties |  | 
10% distillation temperature | 318～328K（45～55℃） | 
50%distillation temperature | 363～373K（90～100℃） | 
90%distillation temperature | 413～443K（140～170℃） | 
Final distillation temperature | 488K(215℃）or less | 
Vapor pressure | 56～60kpa | 

## Slide 5
Fuel E5
 |  | Limits |  | VehicleA | VehicleB | VehicleC | VehicleD
Parameter | Unit | Minimum | Maximum |  |  |  | 
Research octane number, RON |  | 95 |  | 96.9 | 96.9 | 97.1 | 97.0
Motor octane number |  | 85 |  | 86.3 | 86.3 | 86.8 | 86.5
Density at 15 ℃ | kg/m3 | 743 | 756 | 749.5 | 749.5 | 751.2 | 747.3
Vapor pressure | Kpa | 56 | 60 | 59.0 | 59.0 | 57.8 | 59.9
Water content | % v/v |  | 0.015 | 0.010 | 0.010 | 0.011 | 0.014
Distillation |  |  |  |  |  |  | 
Evaporated at 70 ℃ | % v/v | 24 | 44 | 32.5 | 32.5 | 32.3 | 34.7
Evaporated at 100 ℃ | % v/v | 48 | 60 | 54.6 | 54.6 | 54.5 | 54.2
Evaporated at 150 ℃ | % v/v | 82 | 90 | 85.6 | 85.6 | 85.5 | 86.7
Final boiling point | ℃ | 190 | 210 | 194 | 194 | 193.7 | 194.4
Residue | % v/v |  | 2 | 0.7 | 0.7 | 0.6 | 1.0
Hydrocarbon analysis |  |  |  |  |  |  | 
Olefins | % v/v | 3 | 13 | 6.3 | 6.3 | 6.5 | 9.9
Aromatics | % v/v | 29 | 35 | 30.1 | 30.1 | 30.4 | 31.4
Benzene | % v/v |  | 1 | 0.1 | 0.1 | 0.1 | 0.4
Saturates | % v/v | report |  | 58.7 | 58.7 | 58.2 | 48.0
Carbon/hydrogen ratio |  | report |  | 6.3 | 6.3 | 6.3 | 6.4
Carbon/oxygen ratio |  | report |  | 47.1 | 47.1 | 47.1 | 47.4
Induction period | minutes | 480 |  | 528 | 528 | 528 | >480
Oxygen content | % v/v | report |  | 1.8(m/m) | 1.8(m/m) | 1.8(m/m) | 1.7(m/m)
Existent gum | mg/ml |  | 0.04 | 0.01 | 0.01 | 0.01 | 0
Sulphur content | mg/kg |  | 10 | 3 | 3 | 3 | 5
Copper corrosion |  |  | class 1 | 1a | 1a | 1a | 1a
Lead content | mg/l |  | 5 | 5 | 5 | 5 | 1
Phosphorus content | mg/l |  | 1.3 | 1.3 | 1.3 | 1.3 | 1
Ethanol | % v/v | 4.7 | 5.3 | 4.9 | 4.9 | 4.9 | 4.7

## Slide 6
Fuel E0
E0 fuel property | Limits |  | VehiclA | Vehicle B | Vehicle C | Vehicle D
 | regular | premium |  |  |  | 
Lead content | Not to be detected |  | 0.001(-) | 0.001(-) | 0 | 0.001(-)
Sulphur content | 10wt ppm or less |  | 4 | 7 | 1 | 5
Aromatics | 20～45%vol |  | 22.1 | 22.0 | 27.0 | 22.6
Olefins | 15～25vol% |  | 18.6 | 19.6 | 16.6 | 20.4
Benzene | 1% vol or less |  | 0.3 | 0.3 | 0.1 | 0.4
Oxygen concentration | Not to be detected |  | 0.1(-) | 0.1(-) | 0 | 0.1(-)
MTBE | Not to be detected |  | 0.1(-) | 0.1(-) | 0 | 0.1(-)
Methanol | Not to be detected |  | 0.1(-) | 0.1(-) | 0 | 0.1(-)
Ethanol | Not to be detected |  | 0.1(-) | 0.1(-) | 0 | 0.1(-)
Existent gum | 5mg/100ml or less |  | 0 | 0 | 0 | 0
Kerosene | Not to be detected |  | 0.7(-) | 0.7(-) | 0 | 0.7(-)
Octane number RON | 90～92 | 99～101 | 91 | 91 | 91.5 | 90.8
Octane number MON | 80～82 | 86～88 | 81.8 | 81.9 | 81.5 | 81.6
Density | 0.72～0.77g/cm3 |  | 0.731 | 0.734 | 0.728 | 0.733
Fractional distillation properties |  |  |  |  |  | 
10% distillation temperature | 318～328K（45～55℃） |  | 54 | 53 | 54 | 53
50%distillation temperature | 363～373K（90～100℃） |  | 96 | 98 | 92 | 97
90%distillation temperature | 413～443K（140～170℃） |  | 162 | 163 | 164 | 162
Final distillation temperature | 488K(215℃）or less |  | 179 | 179 | 182 | 178
Vapor pressure | 56～60kpa |  | 58.5 | 57.6 | 58.3 | 57.2

## Slide 7
test result
Class1 |  |  |  | 
VehicleA |  | unit | E0 | E5
 | CO | mg/km | 353 | 323
 | THC | mg/km | 111 | 114
 | NOx | mg/km | 27 | 28
 | CO2 | g/km | 45.7 | 46.5
Class2 |  |  |  | 
VehicleB |  | unit | E0 | E5
 | CO | mg/km | 492 | 489
 | THC | mg/km | 93 | 89
 | NOx | mg/km | 31 | 31
 | CO2 | g/km | 66.5 | 67.4
Class3 |  |  |  | 
VehicleC |  | unit | E0 | E5
 | CO | mg/km | 470 | 449
 | THC | mg/km | 106 | 105
 | NOx | mg/km | 11 | 11
 | CO2 | g/km | 94.2 | 96.5
Class3 |  |  |  | 
VehicleD |  | unit | E0 | E5
 | CO | mg/km | 312.6 | 298.0
 | THC | mg/km | 57.8 | 60.1
 | NOx | mg/km | 27.1 | 30.3
 | CO2 | g/km | 96.8 | 96.0